CROWECPM-----A Z80 ASSEMBLER


The assembler provides all the features of Zilog's assembler except
for macros, conditional assembly and lower case. It was originally 
written to be used with cassette or paper tape, with the desired pass
number entered from the console. The assembler is now set up to recieve
the pass numbers from a buffer in the program itself. The output of the 
assembler is sent to files except the error listing which is sent to the
console. For each pass, the source is re-read and the appropriate output
generated. Pass 1 builds the symbol table and is required. Pass 2 outputs
the assembly listing, pass 3 writes Intel format hex object and pass 4
gives an assembly listing of those lines containing errors on the console.
The assembler has been modified to perform pass 4 before writing the files
(passes 2 and 3) so that errors can be seen and corrected before the time
consuming output is done.

The linkage routines are written so that the assembler can be run as
a standard CP/M .COM file with the following command format: 

		CROWECPM FILENAME.YY  

The characters in the normal file extension position are Y/N selects
(default is Y), the first for listing file and the second for the hex
object file. The source must have a file extension of .Z80 while the
listing is created with an extension of .PRN and the object with an
extension of .HEX. Only minimal error checking and reporting is done
when creating files. If no source file with the correct name is found
a message is displayed. If any other disk error on a BDOS call occurs,
that is reported. In either case, the routine waits for a keystroke
before exiting to CP/M.

SYNTAX--------------------------------------------------------------------

The CROWECPM assembler requires that the source file be written using 
standard Zilog mnemonics. In addition it requires that tabs be used as
field delimiters. Labels may have colons following but this is not required.
Comments can be entered anywhere (in any field) following a semicolon as
is usually the case. Hexidecimal numbers that begin with a letter must be
preceded by a 0 and conclude with an H with no imbedded spaces. Since the
source of the assembler is included, and it is syntactically correct, it
can be used as a model of assembly language programming.

FUNCTIONAL OPERATORS-------------------------------------------------------

+		MONADIC PLUS
-		MONADIC MINUS
.NOT. or \	LOGICAL NOT
.HIGH.		VALUE OF MOST SIGNIFICANT BIT
.LOW.		VALUE OF LEAST SIGNIFICNANT BIT
.RES.		RESULT
**		EXPONENTIATION
*		MULTIPLICATION
/		DIVISION
.MOD.		MODULO
.SHR.		LOGIGAL SHIFT RIGHT
.SHL.		LOGICAL SHIFT LEFT
+		ADDITION
-		SUBTRACTION
.AND. or &	LOGICAL AND
.OR. or ^	LOGICAL OR
.XOR.		LOGICAL EXCLUSIVE OR
.EQ. or =	EQUALS
.GT. or >	GREATER THAN
.LT. or <	LESS THAN
.UGT. 		UNSIGNED GREATER THAN 
.ULT.		UNSIGNED LESS THAN

PSEUDO-OPS-----------------------------------------------------------------
ŠThe following Pseudo-ops are supported by CROWECPM:

ORG ---Sets the address reference
EQU ---For assigning a value to a label (can appear only once per label)
DEFL --Also assigns a value to a label but can be used to assign different
	values to a label at different places in the program 
END ---Must conclude the program. Can be followed with the starting address
	of the target program.
DEFB --Defines the content of one byte of memory at the address the OP 
	appears in the program.
DEFB 'x'--Same as above but defines the byte to be the ascii code for the 
	character between the quotes. (x in the example)
DEFW --Defines the contents of two bytes of memory
DEFS --Reserves bytes in memory beginning with the address the OP appears
DEFM 'x'--Defines the contents memory to be the ascii code of the characters
	appearing between the quotes----MUST NOT EXCEED 32 CHARACTERS-----
TITLE 's'-Defines the program title. It is printed in the listing headers.
__________________________________________________________________________
WARNING___________________________________________________________________

An additional note about the assembler the way it stands:  there
is a limit of 32 characters for a quoted string as operand of a DEFM
statement.  If this limit is exceeded NO error message is generated, the
string is truncated.  If you're not careful, the terminating '$' for
a CP/M output string could be lost and the results would be unpredictable.
__________________________________________________________________________
__________________________________________________________________________

LISTING THE .PRN FILE-----------------------------------------------------

The assembler has a strange way of creating the .PRN file which will
cause problems on many printers. A program is included with the disk 
to solve this bug and must be used to send your listing file to the 
printer. See PRINTPRN.DOC for details.
__________________________________________________________________________

The CROWCPM.Z80 file has the linkages incorporated into it, near the
end.  As it now stands, the symbol table is limited only by the amount of
available memory since the assembler reads the start address of BDOS from
locations 6&7 and sets that as the top of available symbol space.  

There has been one minor improvement to the assembler: you can now
specify that the .LST or .HEX files should be sent to drive B rather than
the current default drive by putting a B in the proper position in the 
normal filename extension.  E.g. CROWECPM CROWECPM.NB would assemble the 
file CROWECPM.Z80, skip the .LST file and send the .HEX file to drive B.
The source file must still reside on the same drive as the assembler.

The source is currently set up for the CROWECPM assembler. To assemble it
with M80 you will need to add ASEG and .Z80 commands to it.

****************************************************************************

Bug fixes from Thomas Hameenaho
ŠThe first bug resulted when the single quote character in EX AF,AF'
caused the assembler to expect the following characters
to be a text string. Now I test if the character preceding the ' is
a 'F', if so, the 'QUOTE' flag should not be set.

The other bug (LBFSZ-1) resulted because the minus character (instead
of the "_" character) was declared legal in a label.
Probably a typing error when entering the source code.

So now CROWCPM.COM will assemble CROWECPM.Z80.

	Thomas Hameenaho
	Djaknegatan 7
	S-754 23 Uppsala
	Sweden
******************************************************************************