Documentation for UNSPOOL Version 3.2
		    for	CP/M 2.0 and up.

AUTHOR:
		    Gary P. Novosielski
		       Rutherford, NJ
		       (201) 935-4087
		   Evenings and	weekends.

INTRODUCTION:

	 UNSPOOL  is  a	program	to send	a standard CP/M	file
such as	a .PRN or .ASM file to the system's  list  or  punch
device,	  while	 still	allowing  nearly  all  other  system
operations to take place. The  file  is	 transferred  during
periods	when console is	waiting	for input.

SYNTAX:

	 UNSPOOL [d:]filename.ext [dev]
		 or
	 UNSPOOL dummy OFF

	 [square brackets denote optional parameters]

Where	       d:	       is  an  optional	 drive	spec
			       such as	A:  or	B:.  If	 not
			       entered,	 the current default
			       drive is	assumed.

	       filename.ext    is the name of the CP.M	file
			       to be printed/punched.

	       dev	       is  the	symbolic name of the
			       output  device  to  be  used.
			       Note   that   the  colon	 (:)
			       usually	present	 in   device
			       names  is  NOT entered. Valid
			       devices	are  LST  and	PUN,
			       which  refer  to	the physical
			       devices	 assigned   to	 the
			       logical LST: and	PUN: devices
			       at   the	  time	 UNSPOOL  is
			       started,	as well	 as  PAG,  a
			       special	name  recognized  by
			       unspool.	PAG  refers  to	 the
			       same  physical device as	LST,
			       but supplies automatic paging
			       of output by  inserting	Form
			       Feed   characters   into	 the
			       output. This  is	 useful	 for
			       UNSPOOLing    source   files,
			       which  normally	contain	  no
			       Form  Feeds.  LST is normally
			       used for	.PRN files, or other
			       types which have	 Form  Feeds


Revised	82-01-06	      Page 1 of	6







			       already	 included.   If	 not
			       specified, LST is assumed.

	       OFF	       If OFF is  specified  instead
			       of   a	device	 name,	 the
			       operator	will be	offered	 the
			       option  of cancelling UNSPOOL
			       if it is	already	running.

	       dummy	       Because the word	OFF  is	 the
			       second  parameter, a filespec
			       is still	needed.	A dummy	name
			       of  "."	will  suffice  as  a
			       place holder.

EXAMPLES:
	 UNSPOOL TEST.PRN
		 will	send  the  file	 TEST.PRN  from	 the
current	default	drive to the current LST: device.

	 UNSPOOL A:TEST.PRN LST
		 is  exactly  equivalent   to	the   above,
assuming  drive	A is the default drive.	Note that the device
name has no trailing colon.

	 UNSPOOL B:TEST.ASM PAG
		 will send the file TEST.ASM from  drive  B:
to  the	 current  LST:	device,	regardless of which drive is
currently the default. Form Feeds will be inserted  whenever
the page length	would exceed 56	lines. If any Form Feeds are
contained  in TEST.ASM,	they will also start a new page. The
program	assumes	 that  the  paper  has	been  positioned  to
top-of-form for	the first page by the operator.

	 UNSPOOL B:ZINGER.HEX PUN
		 will  send  the  file ZINGER.HEX from the B
drive to the current PUN: device. Note that  the  device  is
"PUN" not "PUN:".

	 UNSPOOL . OFF
	 UNSPOOL *.* OFF
	 UNSPOOL OFF OFF
		 all  cause an operator	prompt:	"Do you	want
to cancel UNSPOOL?" A single "Y"  or  "N"  (Yes	 or  No)  is
accepted from the console as a response. Any other character
is assumed to mean "No".

	 UNSPOOL OFF
		 causes	the file "OFF.	 " to be sent to the
list device.








Revised	82-01-06	      Page 2 of	6







OPERATION:

	 Upon  loading,	 the  program checks to	see that the
the BIOS vector	table pointed to by  the  word	at  location
0001H  is  valid,  i.e.	 is  a	table  of  JMP	instructions
containing at least 16 entries.	If an error is detected, the
program	will display an	error message  on  the	console	 and
attempt	to warm-boot CP/M.

	 If  found, the	BIOS vector table is copied into the
program	segment	which will remain active  during  unspooling
so that	subsequent application programs	running	concurrently
with UNSPOOL will still	have access to the BIOS.

	 This  table  is  modified  to trap attempts to	warm
boot the system, perform direct	console	 input,	 or  perform
direct	disk  sector  writes.  Direct  sector writes are not
permitted (see notes) under UNSPOOL. Warmboot  requests	 and
direct console input are handled as described below.

	 The  address of the old BIOS vector table, the	BDOS
entry address, and the CCP return address (from	the  top  of
the stack on entry) are	saved in memory.

	 The  "dev"  parameter	from  the  command  line  is
checked. If not	valid, an error	message	is typed and control
returns	to the CCP.

	 If the	"dev" parameter	 is  the  literal  OFF,	 the
program	 executes  a  BDOS  funcion  0	(System	 Reset)	 and
terminates.

	 The file named	in the command line  is	 opened	 for
input.	If not present,	the command is echoed to the console
followed by a "?" and control returns to CCP.

	 If the	drive is not explicit, the  current  default
drive  number  is  recorded  internally	 in case the default
drive is changed while UNSPOOL is active.

	 The current  user  number  and	 IOBYTE	 values	 are
checked	 and stored internally so that if the user number is
changed, UNSPOOL will still be able to read the	input  file.
If  the	device is changed (using STAT LST:=TTY:	for example)
unspool	will continue to use the physical device  in  effect
at  the	 time  the  program  was  initiated. Any application
programs will, however,	use  the  new  values  of  the	user
number and the new physical device assignments.

	 If  no	 errors	 were  detected,  the active program
segment	which monitors all calls to BDOS is  relocated	into
high  memory  just below the CCP. This reduces the available
user program area by 3 K: 4 pages for the UNSPOOL supervisor
segment,  and  8  pages	 for  the  CCP	which  is   commonly
overwritten by user program buffers. The BOOT and BDOS jumps
in  low	 memory	 are modified to protect the CCP and UNSPOOL


Revised	82-01-06	      Page 3 of	6







supervisor segment.

	 Control is then returned  to  the  console.  Normal
CP/M  operation	 will  then  be	possible. Characters will be
sent from the input file to the	output device  whenever	 the
console	is idle.

	 Whenever an application program or the	CCP requests
console	input using BDOS functions 1 or	10, or a direct	call
into  the  jump	 table	at  A(BOOT + 1)	+ 6,  the supervisor
segment	intercepts these requests and checks to	see  if	 the
console	 is  idle. If it is, characters	are transferred	from
the input file	to  the	 output	 device	 until	the  console
becomes	 ready,	i.e. a key is actually pressed.	At that	time
the BDOS function or BIOS call	is  executed  normally,	 and
control	returns	to the application program.

	 If  a	jump  to  BOOT	is  attempted,	this is	also
intercepted by the UNSPOOL supervisor segment.	The  message
"Unspooling in progress" is displayed on the console, and no
actual	 boot  takes  place.  Control  is  returned  to	 the
protected copy of the CCP instead. Before returning, a	disk
reset  is  performed and the default DMA address is reset to
0080H to simulate a true warm-boot as closely as possible.

	 If warmboot is	attempted using	BDOS function 0, the
program	will prompt the	operator with the option to  cancel.
If  the	 response  is  "Y", warmboot is	performed using	BDOS
function 0 as requested. Otherwise the request is handled as
with normal warmboot, above.

	 If a direct BIOS call to write	a sector to disk  is
attempted,   UNSPOOL   will  display  the  message  "Invalid
operation attempted under  UNSPOOL.  Program  aborted."	 The
application  program  will  be	terminated, but	UNSPOOL	will
continue to run. (See Notes.) This restriction applies	only
to direct BIOS writes. All normal file-oriented	(BDOS) reads
and writes are fully supported under UNSPOOL.

	 When the input	file is	completely transferred,	or a
1AH  end-of-file  character  is	 detected,  the	spool writer
becomes	 inactive,  and	 passes	 on  previously	 intercepted
requests  immediately,	without	checking console status. The
sole exception to this is that direct BIOS writes are  still
not  permitted	until  the  next  warmboot.  When  the	next
warm-boot request is detected, the supervisor removes itself
from memory by executing a true	warm-boot, and	informs	 the
operator with the message "UNSPOOL completed.".










Revised	82-01-06	      Page 4 of	6







NOTES:

	 While	UNSPOOL	 makes	every  effort to restore the
values of the DMA address, USER	number,	IOBYTE,	and  default
disk  drive  before  returning	control	 to  the  program, a
hardware reset may leave these	values	in  an	undetermined
state if unspooling was	actually taking	place at the time.

	 When  function	 10,  Read  Console  Buffer is used,
UNSPOOL	will transfer characters only until the	first key is
pressed. At that time, no  characters  will  be	 transferred
until  the  input  line	 is completed by pressing a carriage
return.

	 UNSPOOL requires that the List	Status	function  in
the  BIOS  was	properly  implemented at system	installation
time. UNSPOOL will not send characters to  the	LST  or	 PAG
devices	 unless	 it recieves a ready condition from the	List
Status routine.	If the PUN device is used, no  status  check
is  provided  for  by  CP/M, so	a not-ready condition on the
punch may cause	the system to hang up if PUN  was  specified
on  the	 command  line.	 See the CP/M Alteration Guide for a
discussion of the BIOS List Status routine.

	 Although the console is  polled  frequently  during
the  unspooling	of the file, some of the diskette operations
may take a second or two to complete, for example when a new
extent is opened. Since	the console  is	 not  polled  during
this  period,  high  speed  typing  may	 cause	one  or	more
characters to be lost. This effect will	vary depending	upon
the program being run, the types of input reqests (character
or  line) it uses, and the relative locations on disk of the
spool file and any files in use	by the program.	As a result,
heads-down typing  is  not  reccommended  while	 UNSPOOL  is
running.  Some	experience  with UNSPOOL will teach the	user
when caution is	required.

	 Although it would be  possible	 to  perform  direct
BIOS  writes  while  unspool  is  active,  (indeed  this was
permitted in earlier versions) this action  is	now  trapped
and prohibited.	The reason this	was deemed necessary is	that
some existing software,	for example DU.COM, uses direct	BIOS
writes in a manner which could cause a major system crash if
allowed	under UNSPOOL.

	 The  problem  arises  when a program calls the	BIOS
directly (it is	actually calling UNSPOOL's copy	of the	BIOS
table)	to  select  the	drive, set the track and sector, and
perform	direct disk I/O	without	 going	through	 the  normal
CP/M  file  handling  system.  This causes no problem if the
selecting, addressing, and I/O are all done together, but if
a console input	is done	between	the time the disk address is
set and	the call to read or write a sector, the	disk address
may no longer be valid.	This could cause the  sector  to  be
written	 to  the  wrong	 disk  address,	 or  even  over	 the
directory.


Revised	82-01-06	      Page 5 of	6








	 This is true because a	request	for console input is
taken by UNSPOOL  as  an  opportunity  to  perform  its	 own
functions,  which themselves include disk I/O. Although	this
problem	could be eliminated by insuring	that  console  input
is not allowed to intervene between disk addressing and	disk
I/O, it	is not in the author's power to	rewrite	all existing
applications  software.	This better-safe-than-sorry trap was
therefore included.

	 Note that direct reads	are NOT	trapped, since	they
do  not	 have the same potential for disaster, but still may
be  unreliable	for  the  same	reasons.  It  is   therefore
recommended  that  software using direct disk I/O not be run
under UNSPOOL. Normal CP/M file-oriented  (BDOS)  reads	 and
writes	always	re-select  and	re-address  the	 disk before
reading	or writing a sector, so	no similar problem exists in
the vast majority of software which  uses  the	normal	CP/M
file handling system.

INSTALLATION:

	 The  source  file  is written for assembly with the
MAC assembler. The .HEX	file produced is LOADed	 to  a	.COM
file  and executed just	as any normal program. Relocation is
done at	execution time as described above.

	 If the	assembly option	EXPAND is set to  TRUE,	 tab
characters in the input	file will be expanded to spaces	with
assumed	 tab  stops  at	 every	eighth	print position.	This
option should be set to	FALSE if the printer driver  or	 the
printer	itself can properly handle the tab character. If the
option	PHYSBS	is  set	 to TRUE, a backspace character	will
cause the tab expansion	 algorithm  to	recognize  backspace
characters  and	 decrement the column count when a backspace
is encountered in the input file. This option should be	 set
to FALSE if backspace characters are ignored by	the printer.
All  other  control codes except carriage return are assumed
to be non- printing, and are ignored by	the algorithm.

	 If tab	expansion is included, the version number in
the signon message will	be followed by "/T".

	 The default page size used by the PAG device is set
at 56 in the distribution version. This	value may be changed
by altering the	value  of  the	assembly-time  variable	 LPP
(lines per page).

		      Gary Novosielski









Revised	82-01-06	      Page 6 of	6


-time  variable	 LPP
(lines per page).

		      Gary Novosielski