UMPIRE  is  a comprehensive memory test program implementing 
two test  algorithms developed at the University  of  Illinois.
  The algorithms  were  published  in June 1978 'IEEE 
TRANSACTIONS  ON COMPUTERS'.   The  University of Illinois test
algorithms are the 'BOOMERANG' and the 'HALF SLOW' test
routines.  Also included are two test routines I devised.

The  test will automatically size the TPA and test all of 
memory up the start of BDOS.   There are only three control
codes.  A ^K will cause the test to restart, a ^C will cause a
jump to address zero (i.e. warm boot), and a ^S will cause the
program to stop or start.  The ^S function is particularlly
useful in the 'SCRAMBLE' and 'SPIRAL' routine to stop to test
causing refresh verification on dynamic memories.   Another ^S
will cause the test to start up again.  Both the 'SCRAMBLE' and
'SPIRAL' test routines use random data  so  this  is  a fair
test of a  memory  array  for  pattern sensitivity.

Send any comments or suggestions to:
     Mel Cruts
     DIGITAL DELI COMPUTER STORE
     80 WEST EL CAMINO REAL

A>wwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwww
UMPIRE  is  a comprehensive memory test program implementing 
two test  algorithms developed at the University  of  Illinois.