The XDIR Directory Program

     XDIR  (Extended Directory Display) is an enhanced version of 
the  Digital Research 'built-in' CP/M command 'DIR' which  allows 
the  userto  search  a range of drives and/or user  areas  for  a 
specified   file,  and creat a sorted  directory  display.   This 
capability is patterned after FILEFIND, but is significantly more 
useful in that  XDIR will report the sizes of files matched.    A  
new  BDOS intercept  routine  has been added, which although more 
involved   than   the  FILEFIND  method,    is   more   generally  
applicable  and should  run "as-is" on most CP/M systems.   Thus, 
by using XDIR,  the use of a separate FILEFIND program should  be 
unnecessary.  

                    XDIR - Basic User Operation

     You  merely   type   "XDIR",    followed  by   an   optional  
ambiguous   or  unambiguous  filename (as  you  would  with   the  
CCP  directory command).   Omitting  the  filename  (i.e.,  "XDIR  
[CR]"),  will be interpreted  as  "XDIR *.*".   Similarly,  "XDIR 
A:" would  imply  "XDIR A:*.*" and "XDIR B:"  would  imply  "XDIR 
B:*.*".   In  addition  to the filename option,  up to 8  command  
line  options  may  be  specified.    If   options   are   to  be 
specified, then  the  filename  must  be EXPLICITLY specified  by  
at  least a drive code.  Option fields are  preceded  by a single 
dollar  sign  as  with  most  Digital Research programs  such  as 
MAC,  and may be essentially free-form in format.  Example:  XDIR  
A:  $s  a  D  rn u0 fp.  Note that the reference  to the A drives 
in  "A:" is mandatory.     Invoking  XDIR with a command  of  the 
form  "XDIR  $s a D rn u0 fp" would result in XDIR thinking  that  
$S  was the file to be searched for.   Note also that spaces  and 
case   within   the  option field  are  insignificant  (i.e.,  "$ 
SADrNu0F p" is equivalent  to  "$  S A D R N U0 F P").  The  only  
exception  concerns the "USER" option  which  will  be  explained 
later.   Users  should also be aware of two restrictions  on  the 
command  line  format.   XDIR scans the entire command line for a 
dollar  sign  preceded  by  at  least  1  blank  to  delimit  the 
beginning   of  the option field.   For  this  reason,   invoking  
XDIR  with a command line  such as "XDIR $ $AR" is illegal  since 
XDIR  will consider the first dollar sign to be the option  field 
delimiter.   If  you  need to specify  a  a filename whose  first 
character is a dollar sign, precede it with  a  drive  code as in 
"XDIR A:$ $AR".   In  this  instance,   XDIR  will  consider  the 
first   dollar   sign insignificant as it is not  preceded  by  a 
blank.  
 

     The  second restriction is that command  line options may be 
specified once and only once per invocation.    That  is,   "XDIR 
A:  $XDIRS"   would be illegal since the "S" option is  specified 
twice.   This shortcoming  is  due  to  the fact that options can 
be made into defaults at assembly time.  

     The eight options recognized are:  

  "S"  - system  option :  system files will be included  in  the 
         output rather than being suppressed.  

  "F"  -  file  option :  the directory  output  will  be  echoed 
         to   a   disk  file  named  "XDIR.DIR"  on  the  DEFAULT 
         drive.  If XDIR.DIR already  exists,  then the directory 
         output  will  be  APPENDED  to the  end  of   the  file.  
         Otherwise,  XDIR.DIR will be created as a new file.  The 
         append feature allows you to build  up  one massive file 
         on  the default drive containing the directories of  all 
         of  your  disks,  without  having   to  concantenate   a  
         swarm  of individual directory  files.

  "U"  - user option :  allows  the  specification  of  the  user  
         number  for  the directory of the form "Uxx"  where  the  
         user   #   is  greater  than 0,  but not greater than  a 
         specified  value  not to exceed  15.   The  user  option 
         specification  will  be illegal if the user # is out  of 
         range,  or omitted.  Note  that since  the  user  option  
         requires   a  parameter (i.e.,  the user  number),   the  
         user   number must immediately follow the "U" option  on 
         the command field.    That is, "U1" is legal, but "U  1"  
         is not.   In this respect, the U option differs from the 
         other   options    in    that    embedded   spaces   ARE 
         significant.  

  "A"  - all users :  causes XDIR to display  directories of  all  
         user   areas   starting  at  the  user   area  specified  
         in   the   U  option or,  if U option  is  omitted,  the 
         default  user  area  and continuing up  to  the  maximum 
         number of user directories (15).  

  "R" - reset option : allows for automatic resetting of the disk 
         prior  to  performing  directory  search  so  that   the  
         allocation vector  will  be  updated.   Same as doing  a 
         CTRL-C  when  changing disks,  but handy if  you  didn't  
         (such  as  when  running  a SUBMIT  file).   Useful  for 
         XDIRing a stack of disks with the "F" option, but  slows  
         down XDIR considerably in normal use.  

  "N"  - no  page option :  unconditionally  disables   the  page  
         pause   option.    Useful  when running XDIR in the  "F" 
         and/or  "A"  modes when you don't want the  page  prompt 
         slowing you  down.    Note that XDIR will  not  put  the 
         page-pause prompt  into  the output file.  

  "P" -  printer option : forces all console output to be  echoed 
         to  the CP/M  list  device,   with the most  significant 
         bit set to 0.  

  "D" - all disk option : allows XDIR to search  all  disk drives  
         on-line   starting  with  the  disk drive specified   or  
         implied   with   the   command   line  filename.     For 
         example, "XDIR B: $D" will result in XDIR searching  all 
         drives  beginning  with  drive B.   "XDIR *.*  $D"  will  
         result  in XDIR searching all drives beginning with  the  
         drive  that is logged in.  

     If   an  unrecognized  option  (or  illegal   user    option 
specification) is detected,  then the command line will be played 
back  to the  console  up  to  the  point  where  the  error  was 
detected.