The KayPro II (and the other models) emulate the Lear-Seigler ADM-3A
terminal. In order to install some screen oriented software it is necessary
to know the terminal attributes. The following may help.

CURSOR CONTROL
      cursor left  -    8 dec    08H
      cursor right -    12 dec   0CH
      cursor down  -    10 dec   0AH
      cursor up    -    11 dec   0BH
      home cursor  -    30 dec   1EH
      clear scr & home  26 dec   1AH
      carriage return   13 dec   0DH

CURSOR POSITIONING
      rows              = 0 - 23 dec
      columns           = 0 - 79 dec
      escape sequence  -  27, 61 dec     1BH, 3DH
      constant offset   = 20 dec    14H

      So in Mbasic to position the cursor at row 12, col 40
      print chr$(27)chr$(61)chr$(20+12)chr$(20+40)
                 ESC      =        row        col

LINE INSERT / DELETE
      insert line    - 27, 69 dec      1BH, 45H { scroll down }
      delete line    - 27, 82 dec      1BH, 52H { scroll up   }

CLEAR TO END OF LINE / SCREEN
      clear to EOL - 24 dec   18H
      clear to EOS - 23 dec   17H

CHANGE CHARACTER SETS
      set ASCII - 27,65 dec   1BH,41H
      set greek - 27,71 dec   1BH,47H

In order to use the RS-232 port for communications it must be initialized
to the proper data word length, parity, and number of stop bits as well as
the correct baud rate. Below is an I/O port map and an RS-232 initialization
procedure in Sbasic.

I/O PORTS
      RS-232 status -   6 dec
      RS-232 data   -   4 dec
      keyboard status - 7 dec
      keyboard data -   5 dec
      parallel status - 9 dec
      parallel data -   8 dec
      system status -   29 dec   1DH
      system data -     28 dec   1CH

RS-232 INITIALIZATION

procedure initmod(word1,word2,word3 = integer)
var sio,resetchan,nointerrupt,reg1,reg3,reg4,reg5 = integer

   sio = 6           rem { RS-232 status port }
   resetchan = 24    rem { sio channel reset  }
   nointerrupt = 0   rem { turn off interupts }
   reg1 = 1          rem { next byte goes to register #1 }
   reg3 = 3          rem { next byte goes to register #3 }
   reg4 = 4          rem { next byte goes to register #4 }
   reg5 = 5          rem { next byte goes to register #5 }

begin
rem { change 2 byte integer to 1 byte integer with chr function }
   out(sio),chr(resetchan)
   out(sio),chr(reg4) : out(sio),chr(word1)
   out(sio),chr(reg1) : out(sio),chr(nointerrupt)
   out(sio),chr(reg3) : out(sio),chr(word2)
   out(sio),chr(reg5) : out(sio),chr(word3)
end

The values for 8 data bits, 1 stop bit, No Parity are:
   word1 = 68 dec
   word2 = 193 dec
   word3 = 106 dec
These are values to correctly tell the Z-80 sio chip what to do, each bit is
significant. For other values see a Zilog data book. 

To set the baud rate you just send an integer between 0 and 15 dec to port 0
For 300 baud send 5, for 1200 baud send 7
   out(0),5  ' 300 baud
      OR
   out(0),7  ' 1200 baud


The status port for the RS-232 has 3 registers, only 2 are used for 
asynchronus communication, 0 and 1. Nothing special needs to be done to
read register #0,
       i.e N=inp(6)
works just fine, but in order to get to read register #1 you must write
to the status port first,
       i.e out(6),1
to get register #1 then:
       N=inp(6)
to get the value in register #1.

The bits in read register #0 are:
      0 = Rx char ready
      1 = Int pending
      2 = Tx buffer empty
      3 = DCD (data carrier detect)
      4 = Sync/Hunt (synchronous only)
      5 = CTS (Clear to send)
      6 = Tx underrun/Eom (?)
      7 = Break/Abort

The bits in read register #1 are:
      0 = All sent
      1 = 
      2 = Field bits in previous & 2nd previous bytes (?)
      3 =
      4 = Parity error
      5 = Rx overrun error
      6 = CRC/framing error
      7 = End of frame

KAYPRO RS-232 PINOUT

Only pins 1 - 8 and 20 seem to be used and they go like this:
   1  frame ground
   2  Tx transmit data
   3  Rx recieve data
   4  RTS request to send
   5  CTS clear to send
   6  DSR data set ready
   7  signal ground
   8  DCD data carrier detect
   20 DTR data terminal ready

Well there you have it the hardeware-software interface for two of the most
used communications peripherals on the KayPro the screen and the RS-232 port.