Instruction for Building BIOS2200 CP/M 2.2 System
                                Date 22-Jun-83

         1) Make any corrects/additions to the distribution copy of
            BIOS220° tï supporô youò computeró seriaì I/Ï hardware

         2) Use MOVCPM.COM (supplied with the distribution disk of
            your CP/M v2.2 system) to generate a 60k CP/M system.
            Use the following command:

                              A>MOVCPM 60 *
                              A>SAVE 34 CPM60.COM

         3) Using M80.COM (or a compatible assemblier), assemble
            BIOS2200.MAC into BIOS2200.REL.  Verify that no errors
            occurred during this process.  Use the following
            command:  

                             A>M80 =BIOS2200

         4) Now the BIOS2200.REL file must be converted into a Intel
            hex-ascii format (.HEX) file before it can be placed in
            thå CPM60.COÍ file®  Tï dï this¬ L80.COÍ (Micro-Sofô's
            linker supplied with M80.COM) must be used.  The command
            line looks like this:

                     A>L80 BIOS2200/N,BIOS2200/P:EA00/X/E

            After the link, make sure that the end of the BIOS module
            dosn't wrap around back to zero (BIOS too big). Answer
            NO to the question about moving the module above loader
            memory.


         5) Use DDT.COM to perform the system patching as follows.
            A) First load DDT and CPM60.COM with the following
               command:   A>DDT CPM60.COM
            B) Next include the BIOS module with the correct offset
               to load it into the right place in the system, use
               the commands:
         
                                -IBIOS2200.HEX<cr>
                                -R3580<cr>
               1] It should be noted at this point that no cold start
                  booter is placed on the system tracks of the disk.
                  The sector which would normally be used for this
                  purpose is free for use by the user for any purpose
                  desired.  The cold start booter is assumed to be in
                  ROM.
            C) Make note the the NEXT field which is printed by DDT
               After loading the BIOS module.  Take the two most
               significant digits of the next field and convert this
               value to decimal.  Add one to this value and note this
               value for step 5E below.

            D) Type ^C (control C) to exit to the operating system.
            E) Save the newly created system with the SAVE command.
               Compute the number of pages to save from the NEXT field
               noteä iî steð 5Ã above®  Namå thå saveä filå CPM60.SYS.

         6) Place a cartriage which will receive the system into the
            first IOMEGA drive.

         7) Run the supplied program IPLGEN00.
            A) Type 'M' (for make system) to the first prompt.
            B) Type the name of the file containing the gen'ed
               system to the next file, this is CPM60.SYS.
            C) Type the Correct Drive to the drive selection prompt.
            D) Following this you will have a IOMEGA cartrige with
               a system track on it.