REFERENCE MANUAL
                                        FOR
                                BACKUS DATA SYSTEMS
                                    DIGILINK II
                           INFORMATION NETWORKING SYSTEM






































                               BACKUS DATA SYSTEMS
                            1440 KOLL CIRCLE, SUITE 110
                                SAN JOSE, CA.  95112
                                  (408) 279-8711

                                     REVISION 5.1



DATE:  OCTOBER  1983






                                    TABLE OF CONTENTS

SECTION                             TITLE                               PAGE

1                                   INTRODUCTION                        1
1.1                                 PURPOSE                             1
1.2                                 SCOPE                               1
1.3                                 RADIO FREQUENCY INTERFERENCE        1

2                                   FACTORY DEFAULTS                    1
2.1                                 pORT pARAMETERS                     1
2.2                                 DEFAULT SECURITY KEY                1

3                                   DIGILINK II                         2
3.1                                 INSTALLATION REQUIREMENTS           2
3.2                                 CABLE REQUIREMENTS SERIAL           2
3.3                                 CABLE REQUIREMENTS PARALLEL         2

4                                   MASTER CONTROL PORT ACCESS          2
4.1                                 GENERAL                             2
4.2                                 ACCESS WITH SECURITY DISABLED       2
4.3                                 ACCESS WITH SECURITY ENABLED        2

5                                   COMMAND PROCESSOR                   3
5.1                                 GENERAL                             3
5.2                                 STATUS LINE                         3
5.3                                 COMMAND BLOCK                       3
5.4                                 COMMAND OPERATION                   4

6                                   CONTROL PORT COMMANDS               5
6.1                                 GENERAL                             5
6.2                                 COMMAND OPERATION                   5

7                                   SECURITY SYSTEM                     5
7.1                                 GENERAL                             5
7.2                                 USER ID FIELD                       6
7.3                                 pASSWORD FIELD                      6
7.4                                 pORTS ALLOWED                       6
7.5                                 AUTO CALL BACK                      6
7.6                                 FAILED CALL BACKS                   6
7.7                                 ENABLING SECURITY                   6
7.8                                 DUPLICATE ID's AND PASSWORDS        6

8                                   PIN ASSIGNMENT                      7
8.1                                 RS232 PIN ASSIGNMENTS               7
8.2                                 PARALLEL pORT PIN OUT               7

9                                   STATISTICAL INFORMATION             8
9.1                                 GENERAL                             8
9.2                                 STATISTICAL REPORT GENERATOR        8








                                           i






10                               SYSTEM OPERATION                           8
10.1                             LOGON PROCEDURE                            8
10.2                             INVALID LOGONS                             8

11                               PORT RECONFIGURATION                       8
11.1                             GENERAL                                    8
11.2                             STOP BITS                                  9
11.3                             BITS PER CHARACTER                         9
11.4                             BAUDRATE                                   9
11.5                             PARITY                                     9
11.6                             PORT ID                                    9
11.7                             PASSWORD SECURITY SYSTEM                  10
11.8                             X-ON X-OFF                                10
11.9                             DATA ENCODING                             10

12                               SECURITY RECONFIGURATION                  10
12.1                             GENERAL                                   10
12.2                             MASTER PASSWORD                           10
12.3                             EDITOR COMMANDS                           11

13                               PARAMETERS RESTORAL                       12
13.1                             GENERAL                                   12
13.2                             OPERATION                                 12

14                               RESET                                     12
14.1                             DTR DISCONNECT                            1@
14.2                             MASTER RESET                              12

APPENDIX A                       WIRING DIAGRAMS




























                                       ii






                                  SECTION !
                                INTORDUCTION


1.1  PURPOSE

The Digilink II Information Networking System (IN SYSTEM) FUNCTIONS AS
a local area network for connecting and switching between dissimilar
devices.  The Digilink allows various communications devices to commun-
icate to other devices on any other port independent of baud rate, bits
per character or other dissimilar characteristics.

Field programmability is provided via port #6 which is the master control
port for the unit.

1.2 SCOPE

This manual defines the operational, functional and interface necessary
for the Information Networking System.

1.3

RADIO FREQUENCY INTERFERENCE

WARNING:  This equipment generates, uses, and can radiate radio frequency
energy and if not installed and used in accordance with the reference
manual, may cause interference to radio communications.  This unit has
been tested and found to comply with the limits for a Class A computing
device pursuant to Subpart J of Part 15 of FCC Rules, which are designed
to provide reasonable protection against such interference when operated
in a commercial environment.  Operation of this equipment in a residential
area is lik@ly to cause interferenc@ in which cas@ the user at his own
expense will be required to take whatever measures may be required to
correct the interference.


                                  SECTION 2
                              FACTORY DEFAULTS

2.1  SERIAL PORT PARAMETERS

       BAUDRATE                    4.8 KBPS
       PARITY                      EVEN
       STOP BITS                   1
       BITS PER CHARACTER          7
       X-ON/X-OFF                  DISABLED
       SECURITY                    DISABLED
       PORT ID                     BLANK
       BLANK ENCODING              NRZ

2.2  DEFAULT SECURITY KEY

       DEFAULT ID. . . . . . . . . MASTER
       DEFAULT PASSWORK. . . . . . SECURE
       DEFAULT PORTS ALLOWED . . . 123456



                                      1






                                  SECTION 3
                                 DIGILINK II

3.1  INSTALLATION REQUIREMENTS

       AC POWER REQUIREMENTS
       105 to 120 VAC   60 HZ                      FUSE .7 AMP SLOBLOW 110 VAC

       PHYSICAL DIMENSIONS
       12.125 WIDTH 13.125 DEPTH 4.750 HEIGHT

       ENVIRONMENTAL
TEMPERATURE   0 to 45c .  (32 to 113 F)
HUMIDITY     UP to 80% NO CONDENSATION

3.2    CABLE REQUIREMENTS SERI@. PORTS

In order to minimize radio frequency interference shielded cables are
recommended for the RS232 ports.  Ten conductors are needed for a fu@ inter-
face.  If the cable is only used for CRT'S or printers then a eight conductor
c@.le is sufficient as pins 15 and 17 are not required.

3.3    CABLE REQUIREMENTS PARALLEL PORT

The parallel printer port uses a thirty four conductor cable.  Since many
printers require different conectors refer to the printers user manual
for the type of connectors needed.

                                   SECTION 4
                          MASTER CONTROL PORT ACCESS

4.1    GENERAL

The RECONFIGURATOR OF THE IN SYSTEM CAN BE ENTERED BY CONNECTING A CRT
or TTY type device to the master control port.  This is port number six on
the rear panel of the Digilink II.  (Refer to tabcl 8.1 for RS232 pin out
compatibility).

4.2    ACCESS WITH SECURITY DISABLED

To access the reconfigurator with security disabled enter a control P
(DLE), ths@ a control@@DC4@ THIS ALLOWS ENTRY INTO THE COMMAND PROCESSOR. 
Then enter the command  Enter Reconfigurator, the operator will then be
prompted to enter the master ID and Password.

4.3    ACCESS WITH SECURITY ENABLED

When the correct master ID and Password is entered the operator is given
access to the reconfigurator.










                                    2





                               SECTION 5
                      COMMAND PROCESSOR OPERATION

5.1    GENERAL

All commands and replies in the COMMAND PROCESSOR are in upper case
characters only.  The reply to all commands is displayed in the command
block. ie:  COMMAND:  XXXXX

5.2    STATUS LINES

The STATUS lines are located at the top of the command processor menu. 
The port number of the port entered will be displayed along with the
status of the destination port.
The possible status are '@NLINE OR BUSY. ONLINE that the
destination port is available for data and BUSY INDICATES THAT THE
destination port is currently unable to receive data.

5.3    COMMAND BLOCK

The Command Block is at the bottom of the Command Processors menu.  The
replies in the Command Block indicate the action taken when in the Command
Processor.  The possible replies are  REJECTED, PORT BUSY, '@ORT
DISCONNECTED, DEVICE DISCONNECTED AND COMMAND ERROR. 
A COMMAND REJECT indicates that the command is valid, but the Command
Processor is unable to execute it at this time.  The c@mand DP is valid,
                is no port to disconnect, the command is rejected. 
,but since 'there'isto inform the user that the port requested is busy and is
 @ORT BUSY
unable to receive data at this time.
When the disconnect port command, is successful the reply '@ORT DISCONNECTED"
is displayed in the command block.
The DEVICE DISCONNECTED reply indicates that the requested port does not
have the required input signal to the port.  This reply is only given when
both (DTR and RTS) are not held high on the RS232 line.  If this message is
received check the RS232 wiring and insure that the terminal is powered up
on the port in question.
A COMMAND ERROR indicates that the command entered is invalid for any case. 
Only the commands in table 5.1 are valid.

                   HP                                  H@@
                   C# 1 thru 6                        CONNECT PORT
                   T# 1 thru 6                        CONNECT PORT TRANSPARENT
                   DP                                 DISCONNECT PORT
                   PI                                 PORT ID
                   LO                                 LOG OFF
                   X                                  EXIT

                                TABLE 5.1

Only if security is disabled will the command '@R ENTER RECONFIGURATION, BE
accepted in port #6.  If th@ parallel port option is installed without
statistical reporting then port seven can be used as a common printer port. 
To connect to the printer the user would enter in 
seven.





                                    3





5.4    COMMAND OPERATION

CONNECT PORT              C#

The CONNECT PORT command is used to connect a port to one of the other
available ports in the Information Network.  This is done by entering in the
command ' followed by the port number of the desired destination.  The
valid port numbers are from 1 to 6 and are labeled on the rear panel of the
Digilink II.  If the parallel port option is installed without statistical
reporting then the valid ports are from 1 to 7.  Ports one thru six are
serial RS232 ports and port seven is a high speed parallel printer port. 
When the connect command is successful, the user will be automatically
exited from the command processor and the message CONNECTED TO PORT#
will be displayed.

TRANSPARENT CONNECTION    T#

,Two', ports can be connected totally transparently by entering the command
    followed by the destination port number.  This mode of operation is
necessary when the data to be sent may contain the command processor entry
code, @P or T.  When in the transparent mode of operation all control codes
are sent to the destination port.  The only way to disconnect from this
mode of operation is to drop DTR AND RTS, this will cause both ports to
be disconnected and the messag@@EMOTE DISCONNECT WILL BE SENT TO THE
destination port.  This type of disconnect will restore both ports back
to the normal idle state.

DISCONNECT PORT           DP

The Disconnect Port command is used to release a device to the network so
others may use that resource.  This is done by entering in the characters
DP.  The command processor will indicate the status of the command in
the command block.
The possible status are COMMAND REJECTED, or PORT DISCONNECTED.  If
a command reject was received, this is because there was not a port to be
disconnected so the command could not be processed.  If PORT DISCONNECTED
was received, this shows that the command is completed and the status line
will indicate the new status.
pORT IDENTIFICATION       PI

The '@ORT IDENTIFICATION COMMAND IS USED TO LIST THE PREPROGRAMMED PORT
identifiers for each port, the maximum length of which is five characters. 
The identifier for each port is programmed in the port reconfiguration mode.

LOG OFF                    LO

When finished, the LOG OFF command can be used to exit the IN system
command processor.  This then resets the ports security system if enabled
and the port will be made available to other resources.

EXIT                      X

To exit the command processor enter the character X.  This allows a user
to exit the command processor without logging off of the system.

HELP                       HP

This will display a list of all the valid commands.
                                    4






                                 SECTION 6
                              RECONFIGURATOR

6.1      GENERAL

The following commands can only be accessed thru the master control port
which is port number six.  These commands require the correct master key
ID and Password in order to be executed.
If an incorrect Password or ID is entered three times in succession, the
user will be immediately logged off.
The master Password is needed to access the Reconfigurator.  The IN
system is shipped with a factory supplied master ID and Password to enable
the user to access the system.  The user ID is MASTER and the Password
is SECURE.
THESE ARE THE FACTORY DEFAULTS AND SHOULD BE CHANGED AS SOON AS POSSIBLE
TO SECURE THE SYSTEM.

6.2      COMMAND OPERATION

RECONFIGURE PORT                 R#

This command allows the network manager to change any of the port depen-
dent parameters such as baudrate, parity, flow control or setting the
security system for a desired port.  Refer to section 11 for details of
operation.

RECONFIGURE SECURITY DIRECTORY   RS

This command allows the network manager to change any of the parameters
of the security system such as Passwords, user ID's. ports allowed or
telephone numbers for auto call back.  Refer to section 12 for details
of operation.

SET TIME                         ST

This allows the operator to set the 24 hour clock inside of the unit. 
The format is HH:MM.

EXIT                             X

This command exits the operator from the reconfigurator and returns the
port to normal operation.
If security is disabled for port #6 then this command will return the operator
to the command processor.

                                 SECTION 7
                              SECURITY SYSTEM

7.1      GENERAL

The IN system security directory is only changeable from the master
control port and the Password key is needed to access or change it
in any way.  The  system security directory has four fields.  Only
printable characters are allowed in these fields.
The standard security directory can accommodate up to thirty five users. 
At time of order an optional add-on can increase this to 120 users.



                                   5







7.2      USER ID FIELD

The first field is the USER ID.  The maximum length of the USER ID
is six characters.

7.3      PASSWORD FIELD

The second field is the users PASSWORD.  The maximum length of the users
Password is six characters.  During logon the Password echo will be #
instead of the entered character to prevent the Password from being dis-
played on the users terminal.

7.4      PORTS ALLOWED

The third field is PORTS ALLOWED.  The maximum length is six numeric
characters from 1 to 6.  A user can only communicate with a port if the
port number is in this field.  This provides a useful tool to restrict
access to unauthorized devices for a particular ID and Password.  A11
users can access port number seven which is the parallel printer port if
this option is installed.

7.5      AUTO CALL BACK

Field four is the auto call back field.  The maximum length of the telep@one
number is thirty one numeric entries or a colon which can be used two ways. 
If a colon is the first character, this enables the system to accept an
external phone number for this Password and ID for auto call back.  If the
colon is used anywhere else, it will give a two second pause in dialing which
can be used to wait for a second dial tone.

7.6      FAILED AUTO CALL BACK CA@S

If the IN system is in the auto call back mode and the phone n'mber called
back is busy or not answered, the ' system will call back again in 30
seconds.  This will repeat three times, if the call back is not sCCESSFUL
in the three attempts, the port will be reset back to an idle state.

7.7      ENABLING SECURITY

The security system for the ports can be activated individually.  This is
done from the master control port by entering the port reconfigurator and
then enabling the s+curity system for that port.  Refer to section 11.6
for details.

7.8      DUPLICATE ID'S AND PASSWORDS

The operator is allowed to duplicate an ID or a Password individually but
not as a set.  If the operator enters in a duplicate ID and Password set,
the message DUPLICATE USER KEY FOUND will be displayed in the command
block and the operator will be prompted to enter in a new ID and Password.








                                   6







                                 SECTION 8
                             PIN ASSIGNMENT

8.1      RS232 PIN ASSIG@@NT

All of the Digilink II ports are wired as '@CE specially ordered. 
Sone manufactures do not follow the EIA STANDARDS OR MAY USE A MODIFIED
interface for the RS232.  It is still possible to connect a non-standard
device to the Digilink II by making special cables.  Refer to appendix A
for information on connecting to non-standard devices.
If a communication failure occurs after wiring up a cable re-check all
of the connections to insure the cable is wired properly.

                              PORTS 1 THRU 6

   PIN EIA DIRECTION FUNCTION
 NUMBER       DESIGNATOR
---------------------------------------------------------------------------- -

   1             AA           -------------              FRAME GROUND
   2             BA           TO   DIGILINK              RECEIVE DATA
   3             BB           FROM DIGILINK              TRANSMIT DATA
   4             CA           TO   DIGILINK              REQUEST TO SEND
   5             CB           FROM DIGILINK              CLEAR TO SEND
   6             CC           FROM DIGILINK              DATA SET READY
   7             AB           -------------              SIGNAL GROUND (ISOLATED)
   8             CF           FROM DIGILINK              DATA CARRIER DETECT
   15            DB           TO   DIGILINK              TX CLOCK
   17            DD           TO   DIGILINK              RX CLOCK
   20            CD           TO   DIGILINK              DATA TERMINAL @EADY

                              TABLE  8.1

8.2      PARALLEL PORT PIN OUT

   PIN SIGNAL DIRECTION                  DESCRIPTION
 NUMBER        NAME
--------------------------------------------------------------------------------

   1          STROBE          TO PRlNTER                 ACTIVE LOW
   3          DATA Dl         TO PRINTER                 HIGH INDICATES 
   5          DATA D2         TO PRINTER                 HIGH INDICATES 
   7          DATA D3         TO PRINTER                 HIGH INDICATES 1
   9          DATA D4         TO PRINTER                 HIGH INDICATES 
  11          DATA D5         TO PRINTER                 HIGH INDICATES 1
  13          DATA D6         TO PRINTER                 HIGH INDICATES 1
  15          DATA D7         TO PRINTER                 HIGH INDICATES 1
  17          DATA D8         TO PRINTER                 HIGH INDICATES 1
  21          BUSY            FROM PRINTER               ACTIVE HIGH
  23          PAPER END       FROM PRINTER               ACTIVE HIGH
  25          SELECT          FROM PRINTER               ACTIVE HIGH
  33          CHASSIS         GROUND                     FRAME GROUND (ISOLATED)
  26          PRIME           TO PRINTER                 ACTIVE LOW
  28          FAULT           FROM PRINTER               ACTIVE LOW

   PINS 2-24,27,30,31     SIGNAL GROUND
                              TABLE  8.2







                                        SECTION 9
                                 STATISTICAL INFORMATION

 9.1    GENERAL

 This section contains statistical information for management of the security
 system.  The  ENTRY ATTEMPTS COUNTER.

 9.2    STATISTICAL REPORT GENERATOR

 The statistical report generator uses port number seven, the parallel printer port,
 as the monitor port for statistical reporting.  The time of logons, logoffs and
 the phone number called are recorded for every port.  The format of the report
 is TIME LOGGED ON, PORT @@BER,  DIRECTORY PAGE AND LINE NUMBE@
 of the user.   LOGGED OFF, AUTO CALLED PHONE NUMBER if enabled. 
 If an illegal entry attempt is encountered this also will be logged to the monitor
 port.
 This provides for complete time usage of the system.  The security system has to
 be enabled to be able to obtain this information.  NOTE:  THIS IS AN OPTIONAL
 FEATURE.

                                        SECTION 10
                                     SYSTEM OPERATION

 10.1    LOGON  PROCEDURE

 After dial completion the user must give a valid user ID and Password in order to
 gain access to the system.  The security system will prompt the user for an ID
 and Password.  The Password echo will be a # instead of the character eTERED
 to prevent an unauthorized person from reading the Password on the CRT.  When the
 correct ID and Password is received the user will be called back at the telephone
 number stored on the security directory, if the auto call back is enabled.  The
 first character of the telephone field indicates the auto call each mode of
 operation.
A colon : as the first character in the telephone field selects the external
 mode of call back.  This allows the user to be prompted to give the telephone
 number for call back.
 A valid telephone number in the field indicates that the user is to be called
 back at that phone number.
 If the field is blank the auto call back feature will be disabled and no call
 back performed.

 10.2    INVALID LOGONS

 The user is allowed to make only three errors in any logon attempt.  After the
 third invalid logon attempt the user will be disconnected from the system.  The
 number of illegal logon attempts are tallied and can be displayed in the statistical
 section of the command processor when connected to the master control port.

                                        SECTION 11
                                PORT CONFIGURATION OPERATION

 11.1    GENERAL

 The port reconfigurator is used to set any of the port dependent parameters @uch
 as baudrate, parity, flow control or setting the security system.  See section
 6.1 fo' details on gaining access to the port reconfigurator.


                                           8







The port reconfigurator has three fields, these are the '@CURRENT VALUE, NEW
VALUE AND DEFAULT VALUE.
The NEW VALUE FIELD indicates any changes to the CURRENT VALUES when the SER
changes a parameter.  This field is defaulted to ###### until one of the port
options are changed and then the N@F VA@)E IS DISPLAYED INSTEAD OF THE DEFAULT
entry.  When the user exits the port reconfigurator aY @EW VALUES ARE sed to
reset the parameters of the selected port.
The DEFAULT VALUE indicates the factory supplied defaults of the port.  These
parameters can be reset for the port selected by entering in the command R. 
This causes all of the factory defaults for the selected port to be placed in the
NEW VALUE field.

11.2    STOP BITS

The first option is number' of STOP BITS.  The Digilink II will receive with
any number of  BITS'.  This field is used to set the number of transmitted
STOP BITS.  The options available are 1, 1B or 2 STOP BITS per byte.

11.3    BITS PER CHARACTER

This field is used to set the number of data bits.  Most ASCII devices only
require seven data bits per character.  If '@EX FILES ARE TO BE TRANSFERRED THEN
eight data b@ts per character may be required.  Either seven or eight data bits
may be selected.

11.4    BAUDRATE

This field sets the operating baudrate of the port.  The options available are
listed below in bits per second (BPS).

(0)   50    (1)   75    (2)   110    (3)   134.5    (4)   150    (5)   300    (6)  600
(7)   1200  (8)   1800  (9)   2000   (A)   2400     (B)   3600   (C)   4800   (D)  7200
(E)   9600  (F)   EXTERNAL CLOCK

19200 BPS can be obtained by special order at time of purchase at no additional costs,
but 50 BPS option (0) will be lost.
When the EXTERNAL CLOCK MODE IS SELECTED THE BAUDRATE IS DETERMINED FROM THE XL
clock input on pins 15 and 17 on the RS232 connector.

11.5    PARITY

This field allows tha operator to enable or disable parity checking for the port. 
The options are even parity, odd parity or no parity checking.

11.6    PORT ID

A five character port identifier may be programmed here.  Only printable characters
are allowed in this field.











                                        9








11.7    PASSWORD SECURITY

This field allows the operator to enable or disable the security system.  The
security system can be enabled with or without a no activity disconnect.  The
no activity disconnect feature is enable by enabling the security system with
TIME OUT.
When the no activity TIME OUT feature is enabled the user has a 60 second
period in which to enter a valid logon.  If the user doesn't enter a valid logon
in this 60 second period the system will automatically disconnect this user as
a invalid logon attempt.
If the security system is disabled for a port then the report generator will not
collect data for the disabled port.

11.8    X-ON X-OFF

This field allows the operator to enable or disable this mode of buffer control. 
The X-ON or X-OFF characters also can be programmed to any control code in the
EDIT MODE.

11.9    DATA ENCODING

This field allows the operator to select either '@RZ OR @RZI ENCODING FOR THE
port.  '@RZ used with most RS232 devices and should be selected unless other-
wise specified.

                                       SECTION 12
                              SECURITY RECONFIGURATION

12.1    GENERAL

To gain access to the security directory refer to section 6.  The security direc-
tory has its own built-in editor.  The commands needed for operation are E#,
D#, DA. '@#(@P) and (CR).  When a command is entered, a reply will be given
in the command block.  The command, if rejected, will display COMMAND REJECTED. 
If this happens, check that the command entered was a valid command. 
If the command is valid the command block will indicate the action taken. 
Back space is allowed for any of the entries and if the maximum length of any
of the field is exceeded, the bell (@G) will sound and the last character entered
will be ignored.

12.2    MASTER PASSWORD

The master Password is needed to access the security directory.  After access to
the directory the operator can change the master Password by entering in L to
list page zero.  Th@n '@l edit line number one.  Then the master key can be
updated.












                                        10






12.3    EDITOR COMMANDS

EDIT LINE NUl@ER              E#

The command E followed by the line number will allow the user to change any
entry on that line.  When this command is accepted '@DIT LINE # WILL BE DIS-
played in the command block.  The user is then prompted to enter a new user ID,
NEW USER ID =  if the user ID is to be changed or a new,user ID is to be added,
enter the new data and at the end enter a (CR).  If the user ID is not to be changed
enter (@P) which causes this field to be skipped and the next field is displayed. 
The user is then prompted NEW PASSWORD = .  Enter the new Password or a @%P) to
skip over the field and go to the next field PORTS ALLOWED.  Enter in the new
data or (@P) if the old data is not to he changed and the next field displayed is
the telephone number.  The user is again asked to make any changes if needed
NEW TELEPHONE NUMBER = .  Enter the new data or (@P) to skip changes to this
field.
The (CR) is used to execute a command, so no action is taken until it is entered.

LIST PAGE NUMBER               L#

This allows the operator to move from one page to another in the security
directory.  The page number is displayed in the upper right hand corner of the
display ie; PAGE 1 of 4.  Page zero alwys contains the master Password and ID. 
The command L followed by the desired page number will display that page.

DELETE LINE NUMBER             D#

The command D followed by the line number will delete that line from the
directory.  The master Password and ID can not be deleted by this command.

DELETE ALL ID AND PASSWORDS    DA

The command DA will delete all of the user Passwords and ID's. After entering
this command the operator is asked to verify the command.  If the operator answers
yes, then the command will be executed, otherwise no action will be taken.  This
will not delete the master Password and ID.

SKIP OVER FIELD                 P

A @P (DLE) is used to skip over fields that the user does not wish to change
during the editing process.

FIND ID                        FI

This command allows the user to find a desired ID.  After the command is entered,
the user will be prompted to enter the ID to be found.  If the ID is found the
line number will be displayed in the command block.  The page shown will also
b@ changed to display the ID found.  This is a global search and 'starts'NOTfrom the,
beginning of the directory.  If the ID is not found, the message ID FOUND'
will be displayed in the command block.  After the first occurrence of the ID is
found, the operator can find the next occurrence of the ID by just entering a (CR).








                                          11






FIND STRING                            FS

A particular ID and Password can be found by entering FS.  The operator will then
be prompted to enter in the desired ID and Password to be located.  If the particular
set of ID and Password is found the page of the occurrence will be displayed and
the line number of the located ID and Password will be displayed in the command block.

HELP                                   HP

The HELP COMMAND IS USED TO LIST ALL OF THE VALID COMMANDS.

SAVE CURRENT PARAMETERS AND EXIT       X

To exit back to the command processor and save the current directory in non-
volatile memory, enter in a X.  The unit will reply SAVING on the command
line and when the save is complete, the operator will be returned back to the
command processor.

                                       SECTION 13
                                   PARAMETERS RESTORAL

13.1    GENERAL

The Digilink II has a master reset mode that will restore all factory defaults
back to the unit.  This sets all of the ports back to there original factory
settings and the master Password and ID back to their default values.

13.2    OPERATION

To restore all of the defaults remove the top cover.  This is done by removing
the screws located on each side of the cover.  Then locate SW 1 ON THE CONTROL
circuit board.  These two small posts are located near '@-15 IN THE UPPER LEFT
hand side of the board.  With the AC power applied to the unit momentarily short
out the two small terminal posts.  The factory defaults will be restored in
approximately thirty seconds.

                                       SECTION 14
                                         RESET

14.1    DTR DISCONNECT

The Digilink II has a forcad disconnect mode of opetation.  This allows a device
to be disconnected with the RS232 control signals RTS AND DTR when the unit
is wired as a DCE.  Then by using the DTR disconnect mode.  Any port can be
individually disconnected by dropping DTR AND RTS on the port to be disconnected. 
This will disconnect the port and reset it back to the idle state.

14.2    MASTER RESET

Pressing the red button on the front panel will disconnect all users and reset
all channels to an idle condition.  This reset will not change any of the program-
mabl@ parameters @f any of the ports.
A key lock switch is an available option at time of purchase to help prevent
accidental resets.





                                           12