TABLE OF CONTENTS


    CHAPTER                   TITLE                              PAGE

    INTRODUCTION
                        FEATURES                                   1
                        INSTALLATION                               1
                        POINTS OF INTEREST                         2
                        CHECKOUT                                   2
    CHAPTER 1
                        HOW TO PROGRAM A READ ROUTINE              5
                        HOW TO READ THE DATE                       9
                        SUMMARY                                   11
     CHAPTER 2
                        HOW TO WRITE A SET ROUTINE                12
                        ADJUST THE TIME                           13
                        INTERRUPTS                                14
                        SUMMARY                                   14
     CHAPTER 3
                        FUNCTIONAL DESCRIPTION                    15
                        DISCRIPTION OF OPERATION                  16
                        READ TIME AND DATE                        16
                        SET TIME AND DATE                         17
                        ADJUST TIME +-30 SECONDS                  17
     APPENDIX
        A               I/0 PORTS                                 18
        B               I/0 PORT ADDRESS SELECT                   19
        C               CLOCK DEMO PROG. (BASIC LISTING)          21
        D               CLOCK READ PROG. (ASSEMBLER LISTING)     24




















 










                          INTRODUCTION .

     FEATURES

        The ComputerWatch utilizes the popular MSM5832 real time
     CLOCK/CALENDAR chip designed for use in bus-oriented
     microprocessor applications.  A 32.768 Hz crystal controlled time
     base will provide addressable 4-bit I/0 data of SECONDS, MINUTES,
     HOURS, DAY OF WEEK, DATE, MONTH, YEAR.  The data access is
     controlled by a 4-bit address, read, write, and hold inputs.

        Features include:
            . Time in Hours, Minutes, Seconds
            . Program selectable 24 hour or 12 hour format
            . Date in Month, Day, Year, Day of Week, Leap recognition
            . Fast time and date setting
            . +-30 Second adjust
            . Four hard interrupts.   1024Hz (approx.  1 millisecond@
              1 Hz, 1 minute, 1 hour
            . Crystal controlled time base
            . Latched input and output ports
            . On board battery backup power
            . Automatic power off sensing
            . Simple programming interface
 
        Applicational uses of the ComputerWatch features are limited
     only to the imagination.  In any application where TIME or DATE
     is useful the ComputerWatch can be used.  Applications would
     include, time or date stamping of reports, checks, letters, file
     updates, calculation of time intevals, recording measurements,
     ect.  I am sure you can think of many more uses for the
     ComputerWatch.

     INSTALLATION

        @efore installing the ComputerWatch, the address must be
     selected by setting the switches at location SWl on the board. 
     Look up the address you have selected in Appendix B and set the
     switches as shown.  If possible use address range 128 - 131. This
     is the range used in the programming examples in this manual.

     NOTE- THE COMPUTERWATCH USES FOUR I/0 ADRESSES. BE SURE THAT THEY
           DO NOT OVERLAP OTHER DEVICE ADDRESS RANGES OR THE BOARD
           WILL NOT OPERATE PROPERLEY.

        Ensure that all the ICs are properly installed with pin 1
     toward the left side of the board.  Inspect the board for shorts
     or damaged components.  If damage is found return the board to
     place of purchase for replacement.

        Carefully  install  the board in the system  with  power  off,


                                      1





    .being  certain that pins 1 and 50 line up with the ground pins on
     the S100 bus connector.  Plugging the board in backwards will
     cause damage to the board and void your warranty.



     POINTS OF INTEREST

        There is a NI-CAD 3.6V battery mounted on the circuit board
     that will keep the clock circuit running when power is removed
     from the system.  The battery will be charging whenever the
     system is powered on.  The battery has sufficent capacity to keep
     the clock circuit running for mon@hs between chargings.  It will
     take the battery about eight hours to reach full charge.

        There is a trimmer capacitor located beside the clock chip U5. 
     This capacitor is used to fine tune the clock time base circuit. 
     The trimmer capacitor has been adjusted at the factory to the
     crystal frequency and should not be tampered with.

     CHECK OUT

        Appendix C contains a listing of a program that will check out
     all the time and date features of the ComputerWatch.  It is
     highly recommended that you enter this program and become
     familiar with the features of the ComputerWatch.  The rest of
     this section deals with the operation of this DEMO program and
     allows you to check out the operation of the board.
 
        After you have entered the program and are sure there are no
     errors, RUN the program.  The following will appear on the
     screen:

                 TYPE T TO DISPLAY TIME/DATE
                 TYPE R TO RESET THE TIME/DATE
                 TYPE A TO ADJUST THE TIME +-30 SECONDS
                 TYPE E TO END PROGRAM

        Type T and then RETURN, from here on it will be assumed that
     you will press the RETURN key after each keyboard entry.  The
     following display will be returned:

                 THE DATE IS M M / D D / Y Y
                 TODAY IS ( day of week )
                 THE TIME IS H H : M M : S S AM/PM

        The time and date read should be somthing reasonable to your
     time.  If you are in a time zone other than Pacific time you will
     want to reset the time and possibly the date.  Before attempting
     to reset the date type T again and satisfy yourself the the board
     is working by comparing the first response with the second
     response. The time will have increased. To set the clock type R. 
     The following message will appear.

                                  YEAR TENS


                                      2






   Type the tens digit of the year or 8 for 81.  The next message
will be.

                            YEAR UNITS

  Type the units digit of the year or 1 for 81.  Continue
typing the requsted information until the following question
appears:

               DAY OF WEEK, 0 = SUN, 1 = MON, ect.

The day of week is kept in the ComputerWatch as seven numbers. 
They are:

        0 = SUNDAY
        1 = MOMDAY
        2 = TUESDAY
        3 = WEDNESDAY
        4 = THURSDAY
        5 = FRIDAY
        6 = SATURDAY

   Type the number that applies to the day you want to enter. 
continue entering the requested information until the following
question appears:

                         IS THIS LEAP YEAR

Your response should be a Y for yes or a N for no.  The next
question,

                       12 OR 14 HOUR FORMAT

should be answered with a 12 or 24.  12 hour format will act like
a normal clock with AM OR PM notation. 24 hour format or military
time will keep time up to 23:59:59 with 00:00:00 being midnight
and 12:00:00 being noon time.  The next question,

                             AM OR PM

you would respond to by typing AM or PM.  If you had selected 24
hour format this question would not have appeared.  The following
message will be displayed:

                    THE DATE IS M M / D D / Y Y
                    TODAY IS ( day of week )
                    THE TIME IS H H : M M : S S AM/PM

                    TYPE T TO DISPLAY TIME/DATE
                    TYPE R TO RESET THE TIME/DATE
                    TYPE A TO ADJUST THE TIME +-30 SECONDS
                    TYPE E TO END THE PROGRAM

    Now try the +-30 second adjust routine by typing A.   The same


                                  3






screen as above will appear except that the minutes may have
advanced by one and the seconds reset to zero.  If the seconds
are greater than 30 then one will be added to the minutes units
digit and the seconds reset to zero.  If the seconds are less
than 30, then only the seconds would be reset.

   You  can  exit  the  program by typing  E.

   The next two chapters will show you how to program the
ComputerWatch so that you can interface it into your programs and
applications.

   Chapter 1 will show you how @o program read operations and
Chapter 2 will show you how to set or write time/date data to the
ComputerWatch.











































                                 4





                           CHAPTER  1

HOW TO PROGRAM A READ ROUTINE

   The  CLOCK/CALENDAR chip used in the ComputerWatch has 13 four
bit registers.  This means that all data stored in the clock chip
registers  is  numeric.   The  13 registers  have  the  following
meaning, as shown in TABLE 1.

REGISTER/ADDRESS       DATA DESCRIPTION                 VALUES
----------------------------------------------------------------
       0             Seconds Units Digit                 0 TO 9
       1            Seconds Tens Digit                  0 TO 5
       2            Minutes Unit@ Digit                 0 TO 9
       3            Minutes Tens Digit                  0 TO 5
       4             Hours Units Digit                   0 TO 9
       5             Hours Tens Digit                    0 TO 1
       6             Day of Week Digit                   0 TO 6
       7             Day of Month Units Digit            0 TO 9
       8             Day of Month Tens Digit             0 TO 3
       9             Month Units Digit                   0 TO 9
      10            Month Tens Digit                    0 TO 1
      11            Year Units Digit                    0 TO 9
      12            Year Tens Digit                     0 TO 9
  ---------------------------------------------------------------
                 TABLE 1  CLOCK REGISTER LAYOUT

   If  you  examine  TABLE  1 you will find that  each  digit  of
information has a register address.  When programming you have to
specify  the address for each digit.   FIGURE 1 is a  chart  that
shows in a different form,  the same information as TABLE 1.  You
will  be using these charts from no@ on.   Examine the chart  and
become familiar with it.   As you progress,  the charts will have
more information added to them.                                       

                                                                           / YEAR                                                                                            
                                                 /@@ /          / MONTH /
                         @@!NUTES/     HOUR             DAY
                      /                      



                                                                              
 j REG 1|  0   1         3    4     5  j  6    7    8     9    10    11   12  j
 l                                j    |     j:   j    j     j                j
 j     |                     j                                                 
                                  l                    l     l     l
.j     '                               j    j     j    j                j     
                             j     j    j    j  *       j     j     j  *  j  *  j
     8 l  *  l    l          l     l    l    l                      l         
     4 j .       |  *       j  .  j       *    *  j    j  *        j  *  j    j
j    2 @j .  +         j                j  *  '  .      '|    j'
            j
|    1 j  *  j  *  j              j     j  *  j    j  *         *    .@ j     j
 *ACTIVE B!TS
                         FIGURE l    PROGRAMMING CHART


                                         5






   The next thing you need to know is how to raise the
signal.  This signal is used to prevent the internal clock
registers from being rolled over during a read or write
operation.  Without this feature, it could be possible to read a
units digit of 9, and before @he tens digit could be read the
clock could count the units register causing a rollover to the
tens register.  The result would be nine units off.  For example,
a 49 would read as a 59.  The use of the HOLD signal will
eliminate this undesirable condition.  It is, however, not
necessary to raise the HOLD signal to read clock data.  In fact
it might be undesirable in some cases to do so.  You will be
given an example of one case later on in this chapter.

   Assuming that you have already set the clock using the demo
program you will now create a small program to read the seconds
units digit. Type the following program in BASIC.

NOTE- Only two of the I/0 port addresses are used.  These two
addresses will be refered to as the Address Port and the Data
Port. Refer to Appendix B for the correct addresses for the range
you have selected. In the following examples you will have to use
different values for Cl and C2 if you have selected a address
range other than 128 - 131.

010 Cl = 130 : C2 = 129
020 OUT C2,16
030 OUT C1,32
040 X = INP(Cl)
050 PRINT X
060 OUT C2,0 : END

   Run the program and see what happens.  Run it a number of
times.  You will notice that the number displayed is changing. 
This is because you have been reading @he seconds units digit. 
Its value should change every second.

EXPLANATION
   The first instruction at line 010 sets the Address and Data
Port I/0 address into variable Cl and C2.  Line 020 raises the
HOLD signal by writing a 16 to the Data Port.  Line 030 sets the
address of the register you want to read into the Address Port. 
You must add 32 to the register value of the register address of
the digit you want to read.  In this case you wanted to read the
seconds units digit, who's register address is 0.  By adding 32
to 0 the actual value for the address would be 32.  If, for
example you want to read the hour tens digit, you would add 5 to
32 for an actual address of 37.  The chart in figure 2 reflects
this new information.  Line 040 will read the data from the
selected register from the Address Port and store it in variable
X.  Line 060 will lower the HOLD signal to allow the clock to
continue counting by putting a 0 in the Data Port.  The HOLD
signal should never be held up longer than one second.  There
must be a delay of 150 microseconds after the HOLD is raised. 
When using BASIC, this delay will not be necessary due to the
time BASIC takes to interpret the next instruction.  If, however,


                                 6





 you plan to use an assembler or machine language, then this delay
 must be provided.
                                                                      

                                                                           / YEAR                                                                                            
                                                                 / MONTH /
                         @@@NUTES/    HOUR              D@Y
                      /,/
               /    /     /    /  /                        /                     




 |. REG ,|  0  ,j  1  |'  2  j  3  '[  4  ,|  S  '|  6  7  j  8  9  |,  10  |' 11  j'  12

:  +32  l 32 !@ 33 ' 34 j  3S  | 38  j 37  |. 38 | 39  | 40  41  ; 42  43 |  44
j     |           j    j     j    j     j               j          j    l     
                                                               j    j  *       l
     8 l  +        l  *      l  *       j                                   *  
                                              l  *  l    l     l    l
     4 |  .  j     j'                         j  *  j      *  j     j  *    *  j
                                   l    j
     2 |  *    *     *  j       *  '       *  j  *  '  *      j       *  j  *  
 j
 j   1 j       *        j            *     *  j  *  j  *  j  *   *  j  *  j    |'
  *ACTIVE BITS      FIGURE 2      PROGRAMMING CHART (expanded)

    For  a  variation on the previous routine enter the  following
 program, and then run it.

 010 Cl = 130
 020 OUT C1,32
 030 X = INP(Cl)
 040 IF Y=X THEN 030
 050 Y=X
 060 PRINT X : GOTO 030

 EXPLINATION
    Notice  in  this  program  the HOLD  signal  was  not  raised,
 therefore  it was not necessary to reference the Data Port  (C2).
 The  program  only  reads  the seconds units  digit  and  is  not
 concerned  about digit rollover.  Line 040 checks to see if there
 was a change in the seconds digit.   If there was a  change,  the
 new digit is printed and the varibale Y is given the new value.

    The  next  step  would  be to read the  digits  from  all  the
 registers concerned with Hours, Minutes, and Seconds.  Before you
 do  this  however,  you  need  to learn  about  the  option  bits
 associated   with  the selection of 12/24 hour format and  AM/PM.
 Refer to FIGURE 3.

    The hours ten digit contains the information to determine what
 format is being used,  12 or 24 hour.  It also contains the AM/PM
 information.   Bit 4 is used to determine AM/PM and bit 8 is used
 for 12/24 hour format.





                                  7





                                                  


                                     HOUR
                                          @



                           ,          
                    | REG | 4    5  '
                    '                  
                     j  +32  j 36   37  |                                  
                     '      '          
                           |         j  
                          8 !  *  @ 24 
                     j @                       BIT 8   ON 24 HOUR FORMAT
                   4 |                BIT 8 OFF 12 HOUR FORMAT
                                     BIT 4 ON PM
                   2 :  . 4 OFF AM

               '   1 |  |.  .|


                    FIGURE 3   TIME OPTION BITS

   The following program will read the time digits and display
them as H H : M M : S S AM/PM

010 Cl = 130 : C2 = 129
020 DIM T(6)
030 OUT C2,16
040 LET I=0
050 FOR D = 37 TO 32 STEP -1
060 OUT Cl,D
070 T(I) = INP(Cl)
080 I=I+1
090 NEXT D
100 B=T(0)
110 IF B>7 THEN P$ =  
120 IF T(0)>7 THEN T(0) = T(0)-8
130 IF B<8 AND T(0)>3 THEN P$ = PM
140 IF B<8 AND T(0)<4 THEN P$ = AM
150 IF T(0)>3 THEN T(0) = T(0)-4
160 PRINT THE TIME IS ;T(0);T(1);:;T(2);T(3);:;T(4);@(5);P$
170 OUT C2,0 : END

   Check to be sure you entered the program correctly and then
RUN it.  The display on the screen should be:

                THE TIME IS H H : M M : S S AM/PM

EXPLINATION
   The array T has been set up for six elements at line 020.  The
FOR loop between 050 and 090 allows the digit register address's
to be stepped down each time a digit is read from the Address
Port.  The digit is stored in array T and is subscripted by I. 
After all the time digits are read the IF statements between 110


                                 8





and 150 check for 12 or 24 hour format and AM/PM.  The PRINT
statement will print the contents of the array T and insert a :
between the hours minutes and seconds.  You must strip the option
bits before using them, otherwise the value you display will be
wrong.  The code at line 120 and 150 does this for the 8 and 4
bit.  You may want to add some remarks to the program and save it
for future use.

HOW TO READ THE DATE
   Refer back to FIGURE 2 and look at register 6 of the Day of
Week.  The day of the week is stored in this register as one of
six digits.  For example:
                    0 = SUNDAY
                    1 = MONDAY
                    2 = TUESDAY
                    3 = WEDNESDAY
                    4 = THURSDAY
                    5 = FRIDAY
                    6 = SATURDAY
    FIGURE 4 shows the option bits that you must be concerned with
 when working with.the date digits.

                                        


                                OAY




                ,/@@  /        

                l REG l@ 7  |1  8
                     :  +32 l 39  : 10  : 
                           j    j      
                     j    8   *        j
                                               BIT 4 = 0 (28 DAYS IN FEB.)
                      4|               BIT 4 = 1 (29 DAYS IN FEB.)
                      2
                  ,|   1!        


                       FIGURE 4   PROGRAMING CHART LEAP YEAR

     Bit 4 of the Days Tens register controls whether or not there
  are 28 or 29 days in Febuary.  If bit 4 is on then it is leap
  year and Febuary will have 29 days.  If bit 4 is off then Febuary
  has 28 days.  If it is leap year and Febuary 29th has passed the
  clock chip will automaticaly reset bit 4.  The programming chart
  in FIGURE 5 has been updated with the information you have
  learned so far.





                                   9




                                                                                    

                                                                / MONTH // YEAR                                                                                   
                         @@I@UTES@    HOUR            DAY
                      /                     



                             / . /     ./                                    
                                                                              
 j REG j  0    1     2   3    4    S  ]!  6  l  7  l  8  9   10   11    12  1|
 '     '                                                                      
 @  +32    32    33 | 34 j 3S                      40    41  42  | 43 | 44  j  
 |                j     j         j    j     j    j                            

     8   .  l                 *    24      !|  *  j              |  *    *    
                                                        l  *  l    l
     4   *    *   *     *    *         *  j  *         *       j  *  '  *     
     2 |  *            '  *     *  j       *  |'  *  j  *  '  *    j  *       j
j
j    1 [  *  j  *   *     *  '  *       j  *  j'  *  j  *  *    *       j     
 *ACTIVE BITS

                FIGURE 5 PROGRAMMING CHART (updated)

     Enter the following program.

  010 Cl = 130 : C2 = 129
  020 DIM T(7) : DIM W$(7)
  030 DATA SUNDAY,MONDAY,TUESDAY,WEDNESDAY,THURSDAY,
           FRIDAY,SATURDAY
  040 FOR A = 0 TO 6 STEP 1
  050 READ W$(A)
  060 NEXT A
  070 OUT C2,16
  080 LET I=0
  090 FOR D = 44 TO 38 STEP -1
  100 OUT Cl,D
  110 T(I) = INP(Cl)
  120 I=I+1
  130 NEXT D
  140 IF T(4)>3 THEN T(4) = T(4)-4
  150 PRINT THE DATE IS ;T(2);T(3);/;T(4);T(5);/;T(0);T(1)
  160 PRINT TODAY IS W$(T(6))
  170 OUT C2,0 : END

     Check  the  program  to be sure all lines  have  been  entered
  correct1y and then RUN it.  The display should look like this:
                    THE DATE IS (mm/dd/yy)
                    TODAY IS (day of week)

   EXPLINATION
      The  basic  difference between this routine and  the  previous
   time routines is the addition of the array W$ and the definition
   of the days of the week.  Line 140 strips the 4 bit if it was
   set, from the days tens digit.  If you dont strip this bit the
   digit that is displayed will be wrong.



                                   10






            An interesting exersise would be to combine the date and time
         routines into a single program.  Try it.  If you need help check
         the clock demo program in Appendix C.
  
         SUMMARY
         1.  There are 13 clock registers. 
         2.  All data stored in the clock is numeric. 
         3.  Each digit of information has its own address. 
         4.  The HOLD signal prevents counter rollover. 
         5.  When using Assembler or Machine Languages 150 micrsecond delay
             is required after the HOLD signal is raised. 
         6.  You must add a 32 to the register address when doing a read. 
         7.  You must lower the HOLD signal after reading to enable the
             registers to continue counting.
         8.  You must examine the option bits when reading the hours tens
             digit.
         9.  You must strip the option bits when displaying the hours tens
             digit.
         10. The day of the week is a value from 0 to 6. 
         11. The leap year bit is stored in the Day Tens 4 bit. 
         12. The leap year bit must be striped when displaying the days
             ten digit.
         13. Only  two I/0 Port addresses  are used.  The Address Port and
             the Data Port.


































                                        11






                          CHAPTER 2

HOW TO WRITE A SET ROUTINE
   In order to set or write data into the clock chip the
following events must occur in! the listed sequence.

1. Raise the HOLD signal by writing a 16 to the Data Port. 
2. Write the register address to the Address Port. 
3. Write the data plus 16 to the Data Port.  The plus 16 is
   required to keep the HOLD signal active.  For example, if you
   wanted to WRITE a 3, the value sent to the Data Output Port
   would be 3+16 or 19.
4. Write the address plus 16 to the Address Port. This will raise
   the write signal.
5. Write  the  register address to the Address Port.   This  will
   will lower the WRITE signal and complete the write operation. 
6. Repeat steps 2, 3, 4, and 5 until all the desired registers
   are set.
7. Write a zero to the Data Port to lower the HOLD signal.

   Enter and RUN the following program.  It is an example of a
simple set routine.

010 Cl = 130 : C2 = 129
020 OUT C2,16
030 INPUT ENTER REG. ADDRESS 0-12;N
040 INPUT ENTER DATA 0-9;T
050 OUT Cl,N
060 OUT C2,T+16
070 OUT Cl,N+16
080 OUT Cl,N
090 OUT Cl,N+32
100 D = INP(Cl)
110 PRINT D
120 OUT C2,0 : END

   This program will allow you to set a digit into any register
and then it will read the data back and display it.  Experiment
with this program by entering different register addresses and
data.  Try loading the current time and date. Then use your read
routine to read the data back to verify your settings.

NOTE- YOU  CANNOT SET @ VALUE INTO THE SECONDS REGESTERS.  IF YOU
      WRITE DATA INTO THE SECONDS REGISTERS THEY WILL BE SET TO
      ZEROS.

   Try writing a set routine similar to the clock demo program. 
If you have a problems refer to the listing in Appendix C. 
FIGURE 6 has been updated to reflect the new data necessary to
set the registers.







                                12







                                                                                     
                                                                           / YEAR     /  /                                                                                   
                                                                / MONTH /
                          @MINUTES/    HOUR             DAY

                                 /               /          /                                                                                               



       ,/             - ,/   ,/                                                
 l REG |  0     1    2    3     4   5     6  j  7  '  8   9   l  10 | 11  12  l
 !  +32  l  32  |!  33  | 34 |  3S  36  | 37  j 38 | 39  | 40  41  : 42  j 43 j  44  j
' +16  | 16  | 17 j 18 j  19   20 |  21  j  22 | 23  | 24  2S  j 26  | 27 j  28  j
      8 @  .  |@        |@   |@    l  24 l    ||        |1    |     |  L J
                                                               l
      4 @  .    *  '    'j  *   *  @@M/PM|' @.  @'  *         |                
                                                               l               ;@
 j @  2  *  '  *    *  '     !    |  *    *    *                     *     *  '|

     1 |       *    *  j  *    *     *  j  *  j  *  j  *        *    *  j      
  .ACTIVE BITS




                 FIGURE 6 PROGRAMMING CHART (updated)

   ADJUST THE TIME
      A  feature of the ComputerWatch is the ability to  adjust  the
   time by +-30 seconds.  If you find that the clock has gained or
   lost time you can adjust it with a +-30 second routine.  This
   feature will advance the minutes units digit if the seconds are
   greater than 30 and reset the seconds to zero.  If the seconds
   are less than 30 the minutes units digit will not be advanced and
   the seconds will be reset to zero.

      To  reset  the  time you must first raise the  ADJUST  signal.
   This signal must be active for 32 milliseconds.  To complete the
   operation you must lower the ADJUST signal.  Enter the following
   program.

   010 C2 = 129
   020 OUT C2,32
   030 FOR A=1 TO 20 STEP 1
   040 NEXT A
   050 OUT C2,0 : END

   EXPLINATION
      Line 020 will write a 32 to the Data Port.  This will activate
   the +-30 second ADJUST signal.  Line 030 and 040 provide a time
   delay of 32 milliseconds and line 050 will write a zero to the
   Data Port.  This will lower the ADJUST signal and complete the
   operation.  Add this program to the ones you have completed and
   you will have a complete set of programs to operate the
   ComputerWatch.


                                   13






INTERRUPTS
   There are four interrupts provided by jumper options. The read
signal and the address of the timers is detected external to the
clock chip and enables the hard interrupt signals.  These signals
can then interrupt the system CPU if an option jumper is
activated.  The hard interrupts are only enabled during the time
that the timer signals are being read from the clock chip, thus
they can be controlled by software.  The system CPU can input the
timer signals when they are enabled at the clock chip.  The four
interrupts are:
               1024 Hz (approx. 1 millisecond)
               1 SECOND
               1 MINUTE
               1 HOUR
   The 1024 Hz signal is a 50% duty cycle square wave and the 1
second, 1 minute, and 1 hour signals provide a low pulse for
122.1 microseconds at the indicated rate.  The pulsed signals are
normally high and go low momentarily (122.lus) when the indicated
time interval has occured.  The following ]umpers must be
installed if you want an interrupt at:
                                         
                    PAD      IRQ      NMI
      1024 Hz        D   TO   E   OR   F
      1 SECOND       C   TO   E   OR   F
      1 MINUTE       B   TO   E   OR   F
      1 HOUR         A   TO   E   OR   F

    To enable the timers you write a 47 to the Address Port.  To
 disable the timers write a 0 to the Address Port.

 NOTE- ANY READ OPERATION WILL DISABLE THE TIMERS@ YOU MUST ENABLE
       THE TIMERS AFTER EACH READ OPERATION BY WRITTING A 47 TO
       THE ADDRESS PORT.

 SUMMARY
 1. You have to raise the HOLD signal and write the address of the
    register to be written in the Data Port. 
 2. You have to write the data +16 to the Data Port. The 16 keeps
    the HOLD signal active.
 3. You have to write the address +16 to the Address Port to raise
    the WRITE signal.  Then write the address again to lower the
    WRITE signal.
 4. You should read the data back for verification. 
 5. You should lower the HOLD signal by writing a zero to the Data
    Port.
 6. You  adjust the time +-30 seconds by writing a 32 to the  Data
    Port.  A time delay of 32 milliseconds is required before
    writing a zero to the Data Port to lower the ADJUST signal.
 7. To enable the timers write a 47 to the Address Port. 
 8. To disable the timers write a zero to the Address Port. 
 9. If timmers are being used be sure to enable them after each
    read operation.





                                 14






                             CHAPTER 3

FUNCTIONAL DESCRIPTION
   The ComputerWatch is interfaced to the bus by two TTL latching
type output ports and one tristate input port.  The ComputerWatch
responds to two of the four I/0 port addresses selested.  The
output port latches are selected by address bit zero or one. 
When the ComputerWatch is selected for access and an output cycle
(OUT) is taking place with address bit zero active (high) the
data port latches data from the system bus.  When the
ComputerWatch is selected and an output cycle (OUT) is performed
with address bit one active (high) the address port latches data
from the system.  The data port interfaces to the 4 bit
bidirectional data bus of the clock chip by means of a tristate
buffer.  This buffer is disabled whenever a read of the clock
chip is taking place, to allow the clock chip to drive its data
onto the bus.  The data port latches also interface two control
signals to the clock chip.  The 30 second +- adjust signal and
the hold signal are controlled by the two most significant bits
of the data latches.  The address latches provide a four bit
address to the clock chip for selection of the desired clock
register.  The two most significant bits of the address latches
control the signals read and write to the clock chip.  The read
signal is made active after presenting an address to the clock
chip.  The clock chip will then present the selected data from
the clock on the 4 bit data bus.  This data may then be read by
the system on an input (INP) operation.
   When data is to be written to the clock chip, it is first
written to the Data Port latches and the address is written to
the Address Port latches.  The write signal is then raised and
lowered to complete the write to the clock chip.

   Before reading or writing the clock chip the hold signal
should be raised.  When the read or write operation is completed
the hold signal should be lowered to allow the clock to continue
counting.

   The interval timers are output by the clock when a read is
performed to address 15 (hex F).  The read signal and the address
of the timers is detected external to the clock chip and enables
the hard interrupt signals.  These signals can then interrupt the
system CPU. if an optional hard interrupt is enabled (jumper
installed).  The hard interrupts are only enabled during the time
that the timer signals are being read from the clock chip and
thus can be controled by software.  The system CPU can input the
timer signa1s when they are enabled at the clock chip.  The 1024
Hz signal is a 50% duty cycle square wave and the 1 second, 1
minute, and 1 hour signals provide a low pulse for 122.1
microseconds at the indicated rate.  The pulsed signals are
normally high and go low momentarily (122.lus) when the indicated
tme interval has occured.

   The 30 second +- adjust signal must be held active (high) for
greater than 31.25 milliseconds in order to be effective.  When
this signal is made active and then lowered the clock will be


                                15






adjusted.  The seconds digits are set to zero and the divider
chain is reset so that the next toggle will occur 1 second after
the 30 second +- adjust signal is returned to the inactive state. 
The minutes are incremented by one if the seconds were equal to
30 or more when the adjust signal is raised.  If the seconds were
less than 30 at the time the adjust signal was raised then the
minutes will not be changed.

   The clock chip automatically detects power off and switches to
standby mode.  The interface circuits of the clock chip are
disabled in standby mode and the power drain is substantially
reduced (30uA max.).  The clock will continue keeping time while
the on board battery supplies power.  The clock will still
operate properly when the battery voltage drops as low as 2.2
volts.  The nominal battery voltage is 3.6 volts.  The battery is
charging whenever power is applied to the system.  The time to
fully charge a discharged battery is approximately 12 hours.  A
fully charged battery will keep the clock running for over two
months without charging.  It will even keep time when removed
from the system.

   The clock chip contains registers for the time of day in
hours, minutes, and seconds.  The date is stored as day of week,
day of month, month, and year.  The clock chip registers are
organized as 13 four bit registers.  Option bits are contained in
the hours ten register.  The two most significant bits of this
regster are used to select 12 or 24 hour format and indicate AM
or @M in the 12 hour format.  An optional bit is contained in the
day of month ten register for indicating when 29 days are needed
in Febuary (leap year).

DISCRIPTION OF OPERATION
   The ComputerWatch requires that events occur in a proper
sequence and that proper timing is allowed for certain functions
to occur.  Fo11owing is a sequence of events and timing
allowances that should be maintained when reading or setting the
clock.

READ TIME AND DATE

1. Raise hold signal by writing 16 to the Data Port. 
2. Wait 150 microseconds (not required for BASIC). 
3. Activate read operation by writing to the Address Port the
   address of the desired register plus 32. 
4. Wait 6 microseconds (not required for BASIC). 
5. Input digit data.  Note that certain registers have option
   bits encoded as part of the data.  These bits must be examined
   for active options and masked from the data prior to using it
   for display purposes.
6. Repeat steps 3, 4, and 5 until @11 desired clock registers are
   read.
7. Write zero to the Data Port to lower the hold signal. 
8. Write 47 to the Address Port to enable the interval
   timers.



                                16






SET TIME AND DATE

1. Raise hold signal by writing 16 to the Data Port. 
2. Wait 150 microseconds (not required for BASIC). 
3. Write address to the Add@ess Port.
4. Write  data  plus  16 to the Data  Port.   The  16  is
   required to keep the hold signal active. 
5. Write address plus 16 to the Address Port.  This will
   raise the write signal.
6. Write  the address to the Address Port.   This will lower  the
   write signal and complete the write operation. 
7. Repeat steps 3, 4, 5, and 6 until all the desired clock
   register are set.
8. Write zero to the Data Port to lower the hold signal. 
9. Write 47 to the Address Port to enable the interval

ADJUST TIME +-30 SECONDS

1. Write  32 to the Data Port. This will activate the +-30 second
   adjust signal.
2. Wait 32 milliseconds.
3. Write  zero to the Data Port.  This will lower the +-30 second
   adjust signal and complete the operation.



































                               17







                                       APPENDIX A

                                                S
                                       .I/0 PORT

                     ADDRESSS                            DATA
                       PORT                              PORT
                                                                       
                            |BIT |                               |BIT |
             READ SIGNAL> A5|32           +-30 SECOND ADJUST> A5|32
            WRITE SIGNAL> A4|16                   HOLD SIGNAL> A4|16
               DATA OUT } A3| 8                              } A3| 8
                  AND   } A2| 4                     DATA IN  } A2| 4
               REG ADDR @ Al| 2                              } Al| 2
                        } A0| 1                              } A0| 1
                            ------                               ------
                       |

              When A0 through A3 are active plus A5 the READ signal (decimal
           47) the interrupts are enabled.

           ADDRESS PORT

              The Address Port is used for reading clock data.  You must
           first write (OUT) the clock register address with the read signal
           active to the Address Port. The data will then be transfered from
           the selected clock register to the Address Port. To read the data
           from the Address Port to the system you would read (INP) the
           Address Port.

              The  Address Port also controls the write signal when data  is
           being set into the clock by the Data Port.

              The Address Port is also used for interrupt control. 
           Interrupts are enabled when lines A0 through A3 are active and a
           read signal is present. You would write (OUT) a decimal 47 to the
           Adderss Port.  Interrupt signals would then be placed at pads
           A, B, C, and D. They would remaine active until the next time a
           read was performed, then the interrupts would become disabled.

           DATA PORT

              To set data into the clock you must first write (OUT) the
           address of the clock re@ister selected to the Address Port.  You
           then write (OUT) the data to be set into the selected clock
           register to the Data Port.  The next step would be to raise the
           write signal by writing (OUT) the register address plus the write
           signal to the Address Port.  Next you would write the selected
           register address without the write signal to lower the write
           signal.

              The  Data  Port also controls the hold signal  and  the  +- 30
           second adjust signal.




                                           18






                           APPENDIX B

                     I/0 PORT ADDRESS SELECT


DECIMAL DATA ADDR SWl SW2 SW3 SW4 SW5 SW6
ADDRESS PORT(C2) PORT(Cl) A7 A6 A5 A4 A3 A2
 RANGE ADDR ADDR 1-12 2-11 3-10 4-9 5-8 6-7
------------------------------------------------------------
  0-3 1 2          X X X X X X
  4-7 5 6 X X X X X
  8-11 9 10 X X X X          X
 12-15                       X X X X
 16-19                       X X X          X X
 20-23                           X X                X
 24-27 25 26 X X X                X
 28-31 29 30 X X X
 32-35 33 34 X X          X X X
 36-39 37 38 X X          X X
 40-43 41 42          X X          X          X
 44-47 45 46 X X X
 48-51 49 50 X X                X X
 52-55 53 54          X X                X
 56-59 57 58 X X                     X
 60-63 61 62 X X
 64-67 65 66          X X X X X
 68-71 69 70 X          X X X
 72-75 73 74 X          X X          X
 76-79 77 78          X          X X\
 80-83 81 82 X          X           X X
 84-87 85 86 X X X
 88-91 89 90 X X                X
 92-95 93 94 X X
 96-99 97 98 X               X X X
100-103 101 102 X               X X
104-107 105 106 X               X           X
108-111 109 110 X               X
112-115 113 114 X                     X X
116-119 117 118 X                     X
120-123 121 122 X                          X
124-127 125 126 X
128-131 129 130               X X X X X
132-135 133 134               X X X X
136-139 137 138               X X X          X
140 143 141 142               X X X
144-147 145 146               X X           X X
148-151 149 150               X X          X
152-155 153 154               X X                X
156-159 157 158               X X
160-163 161 162               X          X X X
164-167 165 166               X          X X
168-171 169 170               X          X          X
172-175 173 174               X          X
176-179 177 178               X                X X
180-183 181 182               X                X


                                19







                      I/0 PORT ADDRESS SELECT (CONT)


DECIMAL DATA ADDR .SWl SW2 SW3 SW4 SW5 SW6
ADDRESS PORT(C2) PORT(Cl) A7 A6 A5 A4 A3 A2
 RANGE ADDR ADDR 1-12 2-11 3-10 4-9 5-8 6-7
-------------------------------------------------------------
184 187 185 186               X                     X
188-191 189 190               X
192-195 193 194                    X X X X
196-199 197 198                    X X X
200-203 201 202                    X X          X
204-207 205 206                    X X
208-211 209 210                    X          X X
212-215 213 214                    X          X
216-219 217 218                    X                X
220-223 221 222                    X
224-227 22@  226                         X X X
228-231 229 230                         X X
232-235 233 234                         X          X
236-239 237 238                         X
240-243 241 242                               X X
244-247 245 246                               X
248-251 249 250                                    X
252-255 253 254
                                                                    
X = Jumper installed or switch on.






























                                20







                           APPENDIX C

                    CLOCK/CALENDAR DEMO PROGRAM

PROGRAM WRITTEN IN BASIC-E

    REM *************************************************
    REM *THIS PROGRAM WILL READ AND DISPLAY TIME/DATE, *
    REM *RESET TIME/DATE, AND ADJUST TIME +-30 SECONDS. *
    REM *************************************************
    REM
    Cl= 130 : C2= 129
    DIM T(13)
    DIM W$(7)
    DIM S$(13)
    DATA SUNDAY,MONDAY,TUESDAY,WEDNESDAY,THURSDAY,\
         FRIDAY,SATURDAY
    DATA YEAR TENS,YEAR UNITS,MONTH TENS,MONTH UNITS,\
         DAY TENS
    DATA DAY UNITS,DAY OF WEEK 0 = SUN, 1 = MON, ECT
    DATA HOURS TENS,HOUR UNITS,MINUTE TENS,MINUTE UNITS"
    REM *********************
    REM * LOAD ARRAY W$ *
    REM *********************
    FOR A = 0 TO 6 STEP 1
    READ W$(A)
    NEXT A
    REM *********************
    REM * LOAD ARRAY S$ *
    REM *********************
    FOR A = 12 TO 2 STEP -1
    READ S$(A)
    NEXT A
310 PRINT TYPE T TO DISPLAY DATE/TIME
    PRINT TYPE R TO RESET DATE/TIME
    PRINT TYPE A TO ADJUST THE TIME +-30 SECONDS
    INPUT TYPE E TO END PROGRAM;I$ : PRINT
    REM **************************
    REM * SELECT CORRECT ROUTINE *
    REM **************************
    IF I$ = T THEN 500
    IF I$ = R THEN 790
    IF I$ = A THEN 990
    IF I$ = E THEN STOP
    GOTO 310
    REM **************************
    REM * TIME/DATE DISPLAY *
    REM **************************
500 OUT C2,16 : LET I = 0
    FOR D = 44 TO 32 STEP -1
    OUT Cl,D : T(I) = INP(Cl) : I = I+1
    NEXT D




                                21







    REM ***************************
    REM * CHECK FOR 12/24 & AM/PM *
    REM ***************************
    IF T(4)>3 THEN T(4) = T(4)-4
    B = T(7)
    IF B>7 THEN P$ =  
    IF T(7)>7 THEN T(7) = T(7)-8
    IF B<8 AND T(7)>3 THEN P$ = PM
    IF B<8 AND T(7)<4 THEN P$ = AM
    IF T(7)>3 THEN T(7) = T(7)-4
    REM ***************************
    REM * PRINT ROUTINE           *
    REM ***************************
    PRINT THE DATE IS ;T(2);T(3);/;T(4);T(5);/;T(0);T(1)
    PRINT TODAY IS ;W$(T(6))
    PRINT THE TIME IS ;T(7);T(8);:;T(9);T(10);:;T(11);T(12);
    PRINT : OUT C2,0
    GOTO 310
    REM ****************************
    REM *TIME/DATE SET ROUTINE *
    REM ****************************
790 OUT C2,16 :
    FOR D = 12 TO 2 STEP -1
    PRINT S$(D) : INPUT N : T(D) = N
    NEXT D
830 INPUT IS THIS LEAP YEAR;Y$
    IF Y$ = Y THEN T(8) = T(8)+4
    IF Y$ = Y THEN 880
    IF Y$ = N THEN 880
    GOTO 830
880 INPUT 12 OR 24 HOUR FORMAT;Y
    IF Y = 24 THEN T(5) = T(5)+8
    IF Y = 12 THEN 930
    IF Y = 24 THEN 980
    GOTO 880
930 INPUT AM OR PM;X$
    IF X$ = PM THEN T(5) = T(5)+4
    IF X$ = PM THEN 980
    IF X$ = AM THEN 980
    GOTO 930
980 FOR D = 12 TO 2 STEP -1
    N = T(D) : GOSUB 985
    NEXT D
    OUT C2,0 : PRINT : GOTO 500
985 OUT Cl,D : OUT C2,N+16 : OUT Cl,D+16 : OUT Cl,N : RETURN
    REM **************************
    REM * ADJUST ROUTINE *
    REM **************************
990 OUT C2,32
    FOR A = 1 TO 20 STEP 1
    NEXT A
    OUT C2,0
    GOTO 500
    END



                                22







                            APPENDIX D

        TITLE   'TIME for the CompuTime ComputerWatch'

BASE    EQU     128     ;BASE OF CLOCK BOARD
PORT    EQU     BASE+2
BDOS    EQU     5       ;4205 FOR TRS-80, ETC.
BOOT    EQU     0       ;4200 FOR TRS-80, ETC.

        ORG     0100H
        LXI     SP,STACK

        MVI     A,6     ;DAY OF WEEK
        CALL    READ
        RLC             ;*2 FOR TBL OFFSET
        LXI     H,DTBL  ;DAYTABLE
        MOV     E,A
        MVI     D,0
        DAD     D
        MOV     E,M
        INX     H
        MOV     D,M
        CALL    TEXTO

        CALL    CS      ;OUTPUT , 

        MVI     A,9     ;GET MONTH UNITS DIGIT
        CALL    READ
        MOV     B,A     ;SAVE IN B
        MVI     A,10    ;GET MONTH TENS DIGIT
        CALL    READ
        MOV     A,B     ;GET THE UNITS BACK (DON'T SET FLAGS)
        JZ      SKIP    ;WAS 1-9 (JANUARY-SEPTEMBER)
        ADI     10      ;PLUS 10 IF (OCTOBER-DECEMBER)
SKIP    DCR     A       ;MAKE 0-11
        RLC             ;*2 FOR TBL OFFSET
        LXI     H,MTBL  ;MONTHTABLE
        MOV     E,A
        MVI     D,0
        DAD     D
        MOV     E,M
        INX     H
        MOV     D,M
        CALL    TEXTO

        MVI     E,' '   ;PRINT A SPACE
        CALL    BYTEO   ;OUTPUT BYTE

        MVI     A,8     ;GET DAY TENS DIGIT
        CALL    READ
        ANI     3       ;STRIP LEAP YEAR BIT
        CNZ     ODGT    ;OUTPUT THE DIGIT (IF IT IS NON ZERO)

        MVI     A,7     ;GET DAY UNITS DIGIT
        CALL    READ


                                23







        PUSH    PSW
        CALL    ODGT    ;OUTPUT THE DIGIT
        POP     PSW

        CPI     1
        JZ      STER
        CPI     2
        JZ      NDER
        CPI     3
        JZ      RDER
THER    LXI     D,TH
        CALL    TEXTO
        JMP     PAST
STER    LXI     D,ST
        CALL    TEXTO
        JMP     PAST
NDER    LXI     D,ND
        CALL    TEXTO
        JMP     PAST
RDER    LXI     D,RD
        CALL    TEXTO

PAST    CALL    CS      ;OUTPUT , 

        LXI D,CENT ;OUTPUT CENTURY (19TH)
        CALL    TEXTO

        MVI     A,12    ;YEAR TENS
        CALL    RDOD    ;READ AND OUTPUT DIGIT

        MVI     A,ll    ;YEAR UNITS
        CALL    RDOD    ;READ AND OUTPUT DIGIT

        CALL    CS      ;OUTPUT , 

        MVI     A,5     ;HOUR TENS
        CALL    READ
        PUSH    PSW
        ANI     3       ;STRIP 12/24, AM/PM BITS
        CALL    ODGT

        MVI     A,4     ;HOUR UNITS
        CALL    RDOD    ;READ AND OUTPUT DIGIT

        MVI     E,':'   ;OBVIOUSLY
        CALL    BYTEO

        MVI     A,3     ;MINUTE TENS
        CALL    RDOD    ;READ AND OUTPUT DIGIT

        MVI     A,2     ;MINUTE UNITS
        CALL    RDOD    ;READ AND OUTPUT DIGIT

        MVI     E,':'   ;OBVIOUSLY
        CALL    BYTEO


                                24








        MVI     A,l     ;SECONDS TENS
        CALL    RDOD    ;READ AND OUTPUT DIGIT

        MVI     A,0     ;SECONDS UNITS
        CALL    RDOD    ;READ AND OUTPUT DIGIT

        POP     PSW
        MOV     B,A     ;SAVE TMP
        ANI     8       ;24 HOUR MODE?
        JNZ     EXIT    ;DONE, FINISH

        MOV     A,B     ;RESTORE
        ANI     4       ;AM OR PM?
        JZ      AM      ;AM

PM      LXI     D,PMTXT
        JMP     FOO

AM      LXI     D,AMTXT
FOO     CALL    TEXTO

EXIT    JMP     BOOT

RDOD    CALL    READ    ;READ AND OUTPUT DIGIT

ODGT    ORI     30H     ;CONVERT TO ASCII
        MOV     E,A
        CALL    BYTEO
        RET

READ    ORI     20H     ;ADD IN OFFSET
        OUT     PORT    ;WE WANT THIS DIGIT!
        NOP ! NOP       ;A SHORT DELAY
        IN      PORT    ;READ THE DIGIT
        ORA     A       ;SET THE FLAGS
        RET

CS      LXI     D,CSTXT ;POINT TO , 

TEXTO   MVI     C,9     ;STRING OUTPUT, ENDS WITH A '$'
        CALL    BDOS
        RET

BYTEO   MVI     C,2     ;BYTE OUTPUT, FROM REG. E
        CALL    BDOS
        RET

MTBL    DW      JAN
        DW      FEB
        DW      MAR
        DW      APR
        DW      MAY
        DW      JUN
        DW      JUL


                                25







        DW      AUG
        @W      SEP
        DW      OCT
        DW      NOV
        DW      DEC
JAN     DB      'January$'
FEB     DB      'February$'
MAR     DB      'March$'
APR     DB      l$'
MAY     DB       May$ '
JUN     DB      'June$
JUL     DB      'July$'
AUG     DB      'August$'
SEP     DB      'September$'
OCT     DB      'October$'
NOV     DB      'November$'
DEC     DB      'December$'

DTBL    DW      SUN
        DW      MON
        DW      TUE
        DW      WED
        DW      THU
        DW      FRI
        DW      SAT
SUN     DB      'Sunday$'
MON     DB      'Monday$'
TUE     DB      'Tuesday$'
WED     DB      'Wednesday$'
THU     DB      'Thursday$'
FRI     DB      'Friday$'
SAT     DB      'Saturday$'

ST      DB      'st$'
ND      DB      'nd$'
RD      DB      'rd$'
TH      DB      'th$'

CSTXT   DB      ', $'
CENT    DB      .'19$'

AMTXT   DB      ' AM$'
PMTXT   DB      ' PM$'

        DS      16
STACK   EQU     $
        END










                                26