*****************************************************************
  *                                                               *
  *     A Procedure for Generating .CRL Files at the Assembly     *
  *           Source Level Using Microsoft's MACRO-80             *
  *                                                               *
  *                        May, 1980                              *
  *                                                               *
  *                   William C. Colley, III                      *
  *                  305 Memorial Dr. -- #518B                    *
  *                     Cambridge, MA 02139                       *
  *                                                               *
  *                      ph. (617)258-1204                        *
  *                                                               *
  *****************************************************************
 
 
     Because  MACRO-80  has the pseudo-ops .PHASE and .DEPHASE, it can
create .CRL files directly  from  assembly  source without any tedious
hand patching.  The procedure will be described  below, and will refer
to  the  example  file enclosed which is part of a tape-disk  transfer
routine for talking to a COSMAC elf and contains 2 functions.  
 
     The steps in generating  the  assembly source are easily followed
as the code itself is written.  They are:  
 
         1)  Set up MACRO-80 for the job.

         2)  Build the directory for the functions in the .CRL file.

         3)  Write functions which consist of:

                 a)  A list of needed functions,

                 b)  the length of the function,

                 c)  dummy jump instructions for the BDS C linker,

                 d)  the code itself with relocation targets marked,

                 e)  and a relocation table for the function.

         4)  Mark the end of the package for the BDS C linker.
 
 
Setting up MACRO-80 
 
     The setup for MACRO-80 is simple.    Declare the whole package to
be an absolute segment (ASEG) and set the origin to 0.  This makes the
package load at location 0 in memory.  
 
 
Building the Directory 
 
     A  directory entry is made up of a DB to  define  the  function's
name, and  a  DW  to  define  its  address.  The last character of the
function  name  must  have the upper bit  set.    Function  names  are
8-CHARACTERS MAXIMUM.  The argument of the DW statement is a label set
up at the beginning of  the  list  of functions needed by the function
named in the DB.  For example:  
 
         DB      'FUNCTIO','N' OR 80H
         DW      FUN1
         .
         .
         .
         DB      80H             ;This terminates the directory.
         DW      NXTADR

FUN1:    <list of needed functions for FUN1>
 
     The  directory  has one entry for  each  function,  31  functions
maximum.  The directory  is  terminated by a null entry with the label
on the END statement of the package as its DW argument.  
 
     Following the directory should  be  an  ORG statement to make the
code start at location 512+5.  Note that this  reserves  the  full 512
bytes for the directory, and takes care of the 5 reserved bytes at the
beginning of the code portion of the .CRL file.  
 
 
Writing the Function 
 
     The  function  begins with a list of the names of the C functions
called by the function  being  written.    Note that the first item in
this list will bear the label referred to the  the DW statement in the
directory.  For example:  
 
FUN1:    DB      'GOFORI','T' OR 80H     ;Note that the upper order
         DB      'GNUR','D' OR 80H       ;bit is set on names
         .                               ;here, too.
         .
         .
         DB      0                       ;A null terminates
                                         ;this list.
 
     Next, the length of the function must be inserted.  The assembler
can  calculate this with a couple of cleverly placed  labels,  so  why
count  it  yourself?    This  also  causes the assembler to adjust the
length when you modify and reassemble  the  program  during debugging.
The beginning of body label is placed on the first line of code in the
routine, and the end of body label is placed JUST AFTER  the last line
of code.  For example:  
 
         DW      ENDFN1-BEGFN1
         .
         .
         .
BEGFN1:  <code goes here>
         RET
ENDFN1:
 
     Now comes the sneaky part.  In the definition of .CRL  files, all
of the code must execute from location 0 despite the fact that  it may
be  loaded  anywhere  in  memory.    In particular, the directory just
burned locations 0-0204H.  MACRO-80 allows  assembly of code loaded at
some address to be done as if it were loaded  at  some  other  address
through the .PHASE directive.  Thus, the code after the length of  the
function (the ... in the sample above) is the single statement:  
 
         .PHASE  0
     If  you  have  specified  any  functions  in  the  list of needed
functions,  you  must  start the code with a list of JMP instructions.
There needs to be one JMP  per  function in the needed functions list.
Thus if our FUN1 calls four functions, the beginning of the code would
look like this:  
 
BEGFN1:  JMP     0
         JMP     0
         JMP     0
         JMP     0
         <actual code goes here>
         RET
ENDFN1:
 
     After the jump table, you just  type  in  your  code.   To aid in
compiling  the  relocation  table, you should flag lines of code  that
contain  references to addresses  in  the  function  with  distinctive
labels.  I use A.1, A.2, A.3,...  for the first function in a package,
B.1, B.2,  B.3,...  for  the  second function, and so forth.  Look for
such  references  in  jump  instructions,   call   instructions,   LXI
instructions  that  load local table base addresses, LHLD instructions
that reference local  ram  locations,  etc.   Note that calls to BDS C
functions  should  call  the  JMP  instruction  in  the   jump   table
corresponding  to  the  particular  function  in  the  list  of needed
functions.  
 
     One remark is in order:  DO NOT KILL BC.  Your BDS C program will
die  a  painful  death if you murder the stack frame pointer.  If  you
need the BC pair,  push  and pop.  HL, A, and the flags may be killed,
but I have no experience with  DE  as I push it as a matter of course.
The return value of the subroutine goes back in HL.  
 
     To compile the relocation table for the function, you'll need the
length of the relocation table (in words)  and a DW statement for each
of the markers placed in the code as per the  paragraph  before  last.
For example, 
 
         DW      (ENREL1-$)/2    ;Note that the assembler can
         DW      A.1+1           ;count these, too.
         DW      A.2+1
         DW      A.3+1           ;THE +1 IS IMPORTANT!!!!!
         .
         .
         .
ENREL1:  DW      A.25+1          ;A pretty big function.
 
     A null relocation table looks like this:  
 
ENREL1:  DW      (ENREL1-$)/2
 
     After  the  end of function label (ENDFN1 in the above examples),
you need to get the  assembly  program counter back on course, so tack
on the line:  
 
         .DEPHASE
 
     Additional functions are in the same form as the first.  
 
 
Marking the End of the Package 
     To mark the end of the package  for  the  BDS  C  linker, put the
label  referred  to  by  the  null directory entry at the end  of  the
program as follows:  
 
NXTADR:
         END
 
 
Assembling the beast 
 
     Now that you have the source  file,  you hack on it with MACRO-80
and LINK-80 as follows:  
 
A>M80 =FILENAME

No fatal error(s)

A>L80 /D:0,/P:0,FILENAME,FILENAME.CRL/N/E

Origin below loader memory, move anyway (y/n)?N
A>ERA FILENAME.REL
A>
 
     Here,  I  have assumed that MACRO-80, LINK-80,  and  FILENAME.MAC
live on the currently logged-in disk drive.  It's not required, but it
makes life simpler.  
 
     You now have  FILENAME.CRL  which you feed to CLINK just like any
BDS C program.  Go to it.