and G: drives would be assigned to the 5_1/4" DJDMA drives.
;
dmorder	equ	3		;DJDMA floppies (8")
mforder	equ	2		;DJDMA floppies (5 1/4")
fdorder	equ	0		;DJ2D/B floppies (8" only)
mworder	equ	4		;HDDMA hard disks
hdorder	equ	0		;HDCA hard disk drives
rdorder equ	1		;ram disk drive

;HDDMA controller disk drives
;----------------------------
;	1) If the HDDMA controller has been selected then you must choose one
;	   (and only one) of the following drive types.
;
st506	equ	0		;Seagate ST-506
st412	equ	0		;Seagate ST-412
cm5619	equ	1		;CMI CM-5619

;HDCA controller disk drives
;---------------------------
;	1) If the HDCA controller has been selected then you must choose one
;	   (and only one) of the following drive types.
;
m10f	equ	0		;Fujitsu M2301B
m10m	equ	0		;Memorex
m20	equ	0		;Fujitsu M2302B
m26	equ	1		;Shugart SA4000

;DJDMA controller equates
;------------------------
;
mfslow	equ	0		;set true if slow stepping 5-1/4" floppy

;DJ2D/B controller equates
;-------------------------
;
fdorig	equ	0f800h		;Origin of DJ2D/B Disk Jockey PROM

;RamDisk equates
;---------------
;
;Ram is to be continuous from 0000 in 4k increments. 1 meg maximum.
;use 475 for 1 meg ram; 347 for 768 k ram; use  91 for 256 k ram
;219 for 512 k ram

dsmrd0	equ	91 

;Misc Considerations
;-------------------
wmdrive	equ	0		;CP/M logical drive number to warm boot from.
mwquiet	equ	0		;Set for no names printed on login (HDDMA only)

	if	maxmw ne 0
badsiz	equ	32		;Number of badmap entries for HDDMA

	else			;(Only HDDMA drives use the bad map)
badsiz	equ	1		;Leave one entry as filler
	endif
	page

;****************************
;Begin Internal CBIOS equates
;****************************
;
;
;Revision Numbers
;----------------
;	1) The CBIOS revision number is output on a cold boot of the system.
;	2) The first part of the CBIOS revision number is converted to an
;	   alpha character while the the second part is simply output as a
;	   number. For example 54 becomes E4 and 27 becomes B7.

revnum	equ	55		;CBIOS revision number
cpmrev	equ	22		;CP/M revision number 2.2

;Debug Flag
;----------
;	The DEBUG flag merely causes various internal values and
;	addresses to be printed during the assembly process.  This
;	printing is forced via assembly errors and thus should not
;	affect the resulting code in any way.
;
debug	equ	1		;set to 1 for debugging mode
	page

;General CP/M system equates.
;============================
;
;Location Definitions
;--------------------
wbot	equ	0		;Warm boot jump address
iobyte	equ	3		;IOBYTE location
cdisk	equ	4		;Address of last logged disk
entry	equ	5		;BDOS entry jump address
buff	equ	80h		;Default buffer address
tpa	equ	100h		;Transient memory

;Size Definitions
;----------------
ccpln	equ	800h
bdosln	equ	0e00h
size	equ	(msize*1024)
	if	absasm		;if mac
cbios	equ	size-(biosln*100h)
bios	equ	cbios
offsetc	equ	2100h-bios	;Offset for sysgen
	endif
;Sizes output for Debugging purposes
;-----------------------------------
	if	debug
dbgtmp	set	offsetc		;DDT offset	! <debug>
dbgtmp	set	ccp		;CCP address	! <debug>
dbgtmp	set	bdos		;BDOS address	! <debug>
dbgtmp	set	bios		;CBIOS address	! <debug>
	endif

;Misc. constants
;---------------
;
retries	equ	10		;Max retries on disk i/o before error
	page

;Internal Disk System Equates
;============================
;
;Hard Disk System Equates
;------------------------
;
m10	equ	m10f or m10m
fujitsu	equ	m20  or m10f
hdspt	equ	32*m26+21*m20+21*m10	;Sectors per track for HDCA
mwspt	equ	9			;Sectors per track for HDDMA
hdlog	equ	m10*2+m20*3+m26*3	;Logical disks per drive for HDCA
mwlog	equ	st506+st412*2++cm5619*2	;Logical disks per drive for HDDMA
maxlog	equ	(maxhd*hdlog)+(maxmw*mwlog)+maxfd+maxdm+maxmf+maxrd

;Disk System Ordering Macros
;---------------------------
;	The following macro is used in generating the logical order of the
;	CP/M drives.
;
order	macro	num
	if	num eq hdorder
	dw	hddst
	endif

	if	num eq mworder
	dw	mwdst
	endif

	if	num eq fdorder
	dw	fddst
	endif

	if	num eq dmorder
	dw	dmdst
	endif

	if	num eq mforder
	dw	mfdst
	endif

	if	num eq rdorder
	dw	rddst
	endif

	endm
	page

;***********************************
;Begin CBIOS Executable Code Section
;***********************************
;	This section consists of 3 routines
;		1) The Jump Table
;		2) Warm Boot routine
;		3) Go CPM (executed directly after every warm/cold boot)
;
;CBIOS Jump Table
;----------------
;	The jump table below must remain in the same order, the routines
;	may be changed, but the function executed must be the same.
;
	if	absasm		;mac stuff
	o