NAME
     makeprl - make a prl file from absolute hex files

SYNOPSIS
     makeprl [-s hex number] [-o output file] hex1 hex2

DESCRIPTION
     Makeprl  is  used  to  create  prl  files  suitable for
     loading by the install program (see  install.doc).  The
     format  for  prl  files can be found in prl.doc. The -s
     option is used for entering the reserved buffer  space.
     (The  reserved  buffer  space  is  entered  as a 16 bit
     number  in  addresses  4  and  5  of  the  header,  see
     prl.doc).  The  -o option is the output file specifier.
     If no output file is specified the name  from  hex1  is
     taken  with  '.prl' type extension added. If the output
     file does not have  a  type  exentension,  the  default
     '.prl'  is  added.  The  next  two  arguments  must  be
     specified. The first argument is  the  hex  file  input
     with  an  orgin at 0. The second is the second hex file
     input with an orgin at 100 hex. If the hex files do not
     have a type extension,  '.hx0'  and  '.hx1'  are  added
     respectively.

EXAMPLES
     To  create  a prl file of the hard disk i/o drivers you
     would first have to begin with  the  assembly  language
     source.  Assemble  it  at  orgin  0  and rename the hex
     output (with a .'hx0' extenson  say).  Then  you  would
     have  to  assemble  it  again  with an orgin of 100 hex
     (Consult your assembler manual on how to do this.  With
     some  assemblers  you  would  have to reedit the source
     file and change the 'org' statement).  After  you  have
     assembled the source with an orgin of 100 hex you could
     rename it with a '.hx1' extension. Now you are ready to
     use  the  makeprl  program.  This  is  an  example of a
     typical way to do the above  described  procedure.  The
     example   assumes   that   the   source  is  configured
     correctly.

     mac hd+dj                          
     ren hd+dj.hx0=hd+dj.hex
     mac hd+dj $+r
     ren hd+dj.hx1=hd+dj.hex
     makeprl -o hd+dj.prl hd+dj.hx0 hd+dj.hx1

     In the makeprl line it would not be required to specify
     the output or add type extensions because  the  program
     uses defaults. The makeprl line could be written.

     makeprl hd+dj hd+dj

     This  form does the same as the first but is quicker to
     type.

     The specification for the -s  option  must  be  a  four
     digit hex number.









FILES
     makeprl.com Makeprl program
     makeprl.doc This document.
     
     
makeprl.doc 3/17/81 ldk