DISC FILE ALLOCATION IN
                        CP/M
    
     THIS DESCRIPTION IS FOR THE STANDARD IMPLEMENTATION OF
CP/M ON SINGLE DENSITY 8 INCH IBM FORMAT FLOPPY DISCS.  THESE
DISCS HAVE 77 TRACKS (NUMBERED: 0-76) AND 26 SECTORS PER TRACK
(NUMBERED: 1-26).  EACH SECTOR HOLDS 128 BYTES OF INFORMATION.
EACH SECTOR HAS A HEADER WHICH (EXCLUSIVE OF THE 128 DATA BYTES)
CONTAINS THE TRACK AND SECTOR IDENTIFICATION NUMBERS (IN THE IBM
FORMAT).  IT IS THESE NUMBERS (READABLE BY THE DISC CONTROLLER)
WHICH SPECIFY THE "PHYSICAL" TRACK AND SECTOR NUMBERING.  THIS
NUMBERING DOES NOT NECESSARILY CORRESPOND TO THE "GEOMETRIC"
NUMBERING (I.E. PHYSICAL SECTORS 1 AND 2 MAY NOT BE ADJACENT ON
THE DISC- DEPENDING ON HOW THE DISC WAS FORMATTED).  IN ANY CASE
, THIS POSSIBLE DIFFERENCE IN THE GEOMETRIC AND PHYSICAL
NUMBERING IS NOT USUALLY APPARENT TO THE CONTROLLER OR SOFTWARE
UNLESS THEY MAKE SOME SPECIFIC TIMING ASSUMPTIONS.  HOWEVER, YOU
CAN USUALLY SEE THE DIFFERENCE IN DISC OPERATIONS IN THESE CASES
.   
     THE BOOT AND RESIDENT PORTIONS OF THE OPERATING SYSTEM
ARE HANDLED IN A DIFFERENT WAY THAN THOSE FILES WHICH ARE LISTED
IN THE FILE DIRECTORY (AS IS COMMON FOR MANY DISC OPERATING
SYSTEMS).  THE BOOT AND RESIDENT PORTIONS ARE ON TRACKS 0 AND 1
IN A MEMORY IMAGE FORM AS SHOWN BELOW:
           BOOT    : TRACK 0, SECTOR 1
           RESIDENT: TRACK 0, SECTOR 2,3,...,26
                     TRACK 1, SECTOR 1,2,...,26.
THE SECTORS LISTED FOR THE RESIDENT ARE ORDERED IN THE WAY THEY
ARE TO BE LOADED BACK INTO MEMORY.  THE REMAINING TRACKS OF THE
DISC ARE ADDRESSED BY CP/M BY A "LOGICAL" SECTORING SCHEME.
     BOTH THE DIRECTORY AND ALL FILES IN THE DIRECTORY ARE
ACCESSED IN 1024 BYTE BLOCKS (8- SECTORS) WHICH IN TURN ARE
SPECIFIED BY A LOGICAL SECTORING TABLE.  THE PHYSICAL TO LOGICAL
SECTOR MAP USES A 1:6 INTERLACE AS SHOWN IN THE TABLE BELOW.
    
           LOGICAL     PHYSICAL
           SECTOR #    SECTOR #
              1           1
              2           7
              3          13
              4          19
              5          25
              6           5
              7          11
              8          17
              9          23
             10           3
             11           9
             12          15
             13          21
             14           2
             15           8
             16          14
             17          20
             18          26
             19           6
             20          12
             21          18
             22          24
             23           4
             24          10
             25          16
             26          22
    
THE USE OF A 1:6 INTERLACE SEEMS TO BE ABOUT OPTIMUM FOR THE
STANDARD CP/M UTILITIES RUNNING WITH A 8080 AT 2 MHZ.  HOWEVER,
A Z-80 RUNNING AT 4 MHZ WITH A FAST DISC CONTROLLER CAN WORK
WITH A 1:3 INTERLACE.  THIS CAN BE FAKED BY THE FORMAT ROUTINE.
    
EACH DISC BLOCK (1024 BYTES=1K) IS ACCESSED BY ITS SEQUENTIAL
BLOCK # (0-242).  THIS SCHEME IS DEMONSTRATED IN THE TABLE BELOW
    
 BLOCK #  TRACK#   LOGICAL SECTORS         PHYSICAL SECTORS
 ------I--------I------------------------I----------------------
   0        2     1, 2, 3, 4, 5, 6, 7, 8   1,7,13,19,25,5,11,17
   1        2     9,10,11,12,13,14,15,16   23,3,9,15,21,2,8,14
   2        2    17,18,19,20,21,22,23,24   20,26,6,12,18,24,4,10
   3 *      2    26,26                     16,22
   3 *      3     1, 2, 3, 4, 5, 6         1,7,13,19,25,5
   4        3     7, 8, 9,10,11,12,13,14   11,17,23,3,9,15,21,2
   :        :     :                        :
    
                 --- DIRECTORY FORMAT ---
     THE DIRECTORY OCCUPIES BLOCKS 0 AND 1.  EACH DIRECTORY
ENTRY OCCUPIES 32 BYTES AND IS THE MEMORY IMAGE OF THE FIRST
32 BYTES OF THE 33 BYTE FILE CONTROL BLOCK (FCB) AS DESCRIBED IN
THE CP/M INTERFACE GUIDE (FIGURE 2).  EACH BYTE OF THE 16 "DM"
(DISC ALLOCATION MAP) BYTES GIVES THE BLOCK ADDRESS OF THE DISC
STORAGE OF THE FILE (IN 1024 BYTE PIECES). THUS EACH DIRECTORY
ENTRY CAN DESCRIBE THE DISC ALLOCATION OF 16 BLOCKS (OR LESS).
FILES LARGER THAN 16K (16*1024 BYTES) USE 2 OR MORE DIRECTORY
ENTRYS.  IN FACT A FILE EXACTLY 16*1024 BYTES LONG USES 2 ENTRYS
, EVEN THOUGH THE SECOND ENTRY DESCRIBES THE DISC ALLOCATION OF
ZERO BLOCKS.  DIRECTORY ENTRYS FOR LARGE FILES (>= 128 SECTORS)
CAN BE RECOGNIZED BY EITHER:
    
      1.  "EX" (EXTENT BYTE) >0
  OR  2.  "RC" (RECORD COUNT=SECTOR COUNT) =80H (128 DECIMAL).
    
EACH SUCH DIRECTORY ENTRY DESCRIBES DISC ALLOCATION OF UP TO
128 SECTORS.  THE DIRECTORY ENTRY OF THE TAIL END OF SUCH A
LARGE FILE WILL HAVE "RC" (RECORD COUNT)<80H AMD THUS LESS THAN
16 VALID "DM" BYTES.  THESE MULTIPLE DIRECTORY ENTRYS NEED NOT
OCCURE IN LOGICALLY ADJACENT POSITIONS IN THE DIRECTORY.  WHEN
A FILE IS DELETED, ALL THE DIRECTORY ENTRYS DESCRIBING THE FILE
ARE MODIFIED BY CHANGING THE FIRST BYTE ( THE "ET" BYTE) OF EACH
ENTRY FROM A  00H  TO A  E5H (THE DIRECTORY OF A NEW IBM
FORMATTED DISC IS FILLED WITH  E5H).  A HEX AND ASCII DUMP OF
A TYPICAL DIRECTORY ENTRY IS SHOWN BELOW FOR THE CASE OF A DISC
WITH 2 FILES CREATED BY THE SAVE COMMANDS:
    
              SAVE  10 TEST.COM
              SAVE 130 BIG.COM
    
 00: 00 54 45 53 54 20 20 20 20 43 4F 4D 00 00 00 14
      .  T  E  S  T              C  O  M  .  .  .  .
 10: 02 03 04 00 00 00 00 00 00 00 00 00 00 00 00 00
      .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .
 20: 00 42 49 47 20 20 20 20 20 43 4F 4D 00 00 00 80
      .  B  I  G                 C  O  M  .  .  .  .
 30: 05 06 07 08 09 0A 0B 0C 0D 0E 0F 10 11 12 13 14
      .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .
 40: 00 42 49 47 20 20 20 20 20 43 4F 4D 01 00 00 80
      .  B  I  G                 C  O  M  .  .  .  .
 50: 15 16 17 18 19 1A 1B 1C 1D 1E 1F 20 21 22 23 24
      .  .  .  .  .  .  .  .  .  .  .     !  "  #  $
 60: 00 42 49 47 20 20 20 20 20 43 4F 4D 02 00 00 04
      .  B  I  G                 C  O  M  .  .  .  .
 70: 25 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00
      %  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .
    
NOTE, IN THIS CASE THE "DM" BYTES ARE IN NUMERICAL ORDER SINCE
THE DISC WAS INITIALLY EMPTY BEFORE THESE FILES WERE SAVED.  IF
THE FILES HAD BEEN SAVED ON A DISC ON WHICH SOME FILES HAD JUST
BEEN ERASED, THERE WOULD PROBABLY BE A MORE RANDOM LOOKING CHOICE
OF THE BLOCKS USED.  HOWEVER, IF THE FILES HAD BEEN SAVED (WITHOUT
ANY INTERVENING DISC READS OR WRITES TO OTHER FILES) THE BLOCKS
CHOSEN WOULD STILL BE IN ASCENDING ORDER SINCE CP/M WILL ALWAYS
SELECT THE NEXT AVAILABLE BLOCK # WITH THE LOWEST NUMERICAL
VALUE.
     THERE ARE SEVERAL PROGRAMS ON THE VARIOUS CP/M USER'S
GROUP DISCS THAT CAN BE USED TO EXAMINE THE DISC DIRECTORY
AND FILE ALLOCATION.  THE ONE THAT I HAVE FOUND MOST USEFUL IS
            DUMP.COM     (ON DISC # 24).
HOWEVER, THIS MAY NOT WORK FOR ALL DISC CONTROLLERS (IT WORKS
OK FOR LIFEBOATS CP/M ON NORTH STAR 5" DISC AND WITH TARBELL'S
CONTROLLER BUT NOT WITH THE DISCUS CONTROLLER (A BIOS PROBLEM?)).
            SPAT1.ASM    (ON DISC #16 ) IS ALSO GOOD.
    
  -- SOME COMMENTS ON LIFEBOATS CP/M IMPLEMENTATION ON --
          THE 5" HARD SECTORED NORTH STAR SYSTEM
    
     THE LIFEBOATS IMPLEMENTATION OF CP/M ON THE 5" NORTH STAR
SYSTEM DIFFERS MAINLY IN THEIR UN-SCRAMBLING OF THE 1:6
INTERLACE.  THEIR LARGE   CBIOS   INCLUDES ANOTHER SECTOR
MAPPING TABLE THAT MAPS ONTO THE 5" DISC .  THIS MAPPING
UNWINDS THE 1:6 INTERLACE AND MAPS THE USUAL 8" DISC ADDRESSING
ONTO THE 5" DISC WHICH HAS 35 TRACKS WITH 10 SECTORS (OF 256
BYTES EACH) PER TRACK.  THUS, SAVING THE FILES DESCRIBED ABOVE
UNDER THE LIFEBOATS CP/M (ON A BLANK DISC) WOULD PUT ALL OF THE
PARTS OF THE FILES TOGATHER (THE SAME CONVENTION USED BY THE
USUAL NORTH STAR DOS).  THE FORMAT OF THE BOOT AND RESIDENT
PORTIONS IS SOMEWHAT SCRAMBLED BECAUSE OF THE WAY THE NORTH STAR
BOOT UP ROUTINE WORKS (IT LOADS FROM SECTOR 4 INSTEAD OF 0).
                ------------------------
    
               BY     BRUCE KENDALL
                      (415) 967-3613
----------------------------------------------------------------