.he Cbios Entry Points into the Rom (17_Oct_83)

Select Disk functions

	1) Native drives are not yet handeled
		-getab must be enabled to read the dpb from the current disk
		-the physpt parameter in the general operations data area 1
		 musô bå setuð (usinç thå sectoò sizå anä logicaì records
		 per track entries)
	2) Bad map must be read in from hard disk.


Rdhst, Wrthst, Fmthst

	1) These entry points are used by the bios to access the rom. It
	   is assumed that the IY (general operations data area) has been
	   forced to the start of the system IY before calling any of these
	   entry points.

	2) Enter with a user applications interface area 1 setup
		area 1:	Hst* (hstdsk,hsttrk,hstsec)
			seccnt
			retry
			hstbuf
			erflag

	3) Format operations involve special considerations:
		a) The physical parameters phytrk and phyhd must be setup
		b) The host parameter hsttrk is not used.
		c) The host parameter hstsec is used as a pointer to a pair
		   of tables: the gap table and the sector skew table.
		d) These tables are structured as follows:
			-the gap table (3 bytes long)
				gap 1 post index gap
				gap 3 post data field gap
				gap 5 pre index gap
			-the sector skew table ('physpt' bytes long)
		e) Before the fmthst entry point is called a select disk
		   function must be preformed to set physpt.
		f) If the format operation is performed on a hard disk drive
		   then the current hard disk drive sector skew table should
		   be overlaid.
		g) If gap 1 is zero then the index address mark will not be
		   written.

.paŠRdblk, Wrtblk, Discio

	1) These entry points are NOT used by the cbios. They are provided
	   for use by external routines only. Note that the base of the IY
	   (general operations data area) is NOT altered by these entry
	   points.

	2© Enteò witè alì applicationó interfacå areá parameteró setuð
	   except the host parameters.
		area 1:	seccnt
			retry
			hstbuf
			erflag
		area 2:	opflag (@serd,@serur,@nover,@recal)
			Phy* (phytrk,physec,phyhd,phydrv)
			ioadd
	3) On entry the IX register is pointing to the user applications
	   interface area.
	4) Before executing one of these entry points the system copy of
	   the user applications interface area is saved and then overlaid
	   by the user supplied copy of the applications interface area.
	5) Before returning from one of these routines the system copy of
	   the user interface area is restored.

	applications interface area

		area 1:	Host Level
			Hst* (hstdsk,hsttrk,hstsec)
			seccnt
 			retry
			hstbuf
			erflag
		area 2:	Physical Level
			opflag (@serd,@serur,@nover,@recal)
			Phy* (phytrk,physec,phyhd,phydrv)
			ioadd