The MD-11 Character Table (18_Apr_84)

	Copyright 1984
	Morrow Designs, Inc.
	San Leandro, Ca.


	The character table is located at the very beginning of the bios. The
only code preceeding it is the boot entry jump. The character table can be
read using the extended bios function call 6 (see documentation on extended
bios function calls). The character tables contains the following information:

	Serial Device Initialization
		-Default Serial Baud Rates
		-Initial value of CFlag (see the definition of
		 the bits in CFlag at the end of this document)

	System Configuration Data
		-Misc information concerning revisions and
		 data locations

	Terminal Translation Vector Table
		-A set of pointers for control/escape character
		 translations and direct cursor addressing

	Direct Cursor Addressing Data
		-All of the information needed to translate direct
		 cursor address sequences.


;----------------------------------------------------------------------
; Character Table
;----------------
;	The following code has been extracted from the Morrow Designs Cbios
;	for the MD-11 rev 1.8. This code is provided as a reference so that
;	you can get a feel for the information contained in the character
;	table. Before altering the character table in your own system you
;	should look at your copy of BNKBIOS3.MAC for the values current on
;	your system.
;
char_tables:


; Serial Device Initialization Data
;----------------------------------
;
ser1baud:	db	dflt1		;Defaults are defined in the local
ser2baud:	db	dflt2		; system equates section.
ser3baud:	db	dflt3
default_cflag:	db	23h		;translations are on


; System Configuration Data
;--------------------------
;
vnumb:		db	drives		;number of physical drives
tlev:		db	4		;terminal level (default=not installed)
		ds	3,0		;reserved
		db	BioRev		;BIOS Revision Number
		db	clevel		;compatibility level
		dw	APIF		;Pointer to Application Interface Area
		dw	ramdaty		;Pointer to RamdatY
		dw	ramdaty + MToff	;Pointer to the base of the first MTAB
		dw	pool		;Pointer to free space


; Terminal Translation Vector Table
;----------------------------------
;
etblptr:	dw	esctbl
ctblptr:	dw	ctrltbl
evctptr:	dw	escvect
cvctptr:	dw	ctvect
		dw	dcastrt


; Direct Cursor Addressing Data
;------------------------------
;
dcastrt:	db	1bh,3dh,0ffh	;dca prefix string
		ds	3,0ffh
dcamid:		ds	6,0ffh		;dca seperator
dcaend:		ds	6,0ffh		;dca terminator string

esc_lvl:	db	0		;indicates esc sequence level
offset1:	db	0		;first character offset 
offset2:	db	0		;second character offset
order:		db	0		;bit 0 = 0 --> row, then column,
					;      = 1 --> column, then row
					;bit 1 = 0 --> binary cursor adresses
					;        1 --> ascii cursor addresses
first:		db	0		; temporary storage of  first 
second:		db	0		; temporary storage of second

char_table_length	equ	$-char_tables

;---------------------------
; End of the Character Table
;----------------------------------------------------------------------


;Baud Rate Table Definitions
;---------------------------
;	These are the values placed in ser1baud, ser2baud and ser3baud.
;
;     Value   Resulting Baud Rate
	0	110
	1	300
	2	600
	3	1200
	4	2400
	5	4800
	6	9600
	7	19,200


;Cflag Bit-Flag Definitions
;--------------------------
;	The Default Value is 23h (@xl_in, @xl_out and cenlst all on)
;
	Name   Bit	Function
	----   ---      --------
	@xl_in	0	Translate input function keys
	@xl_out 1	Translate output controls & escapes
	@funact 2	Function key IMS flag (1=active)
	@siosyn 3	Hardware handshake for SIO
	@hwsync 4	Hardware handshake for list device
	@cenlst 5	Centronics is list device
	@imsact 6	In memory submit flag (1=sub active)
	@imswet 7	IMS buffer full (1=buffer has chars)