::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::
:
:          Cross Reference listing of Z-80 Mnemonics      
:
:Courtesy of Tim Eliseo
:		%PCE, 4778 Dewey Dr, Fair Oaks, Ca 95628
:June 1980
:::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::

     This  document is a cross-reference listing of the  standard 
Zilog Z-80 mnemonics to the bastardized TDL Z-80 mnemonics.   The 
TDL  mnemonics  are upward compatible to the standard Intel  8080 
mnemonics,  making  it  easy  to  upgrade  existing  8080  source 
programs to the Z-80 CPU.  The only problem is that they are just 
as illogical as the original 8080 mnemonics, and there is no real 
standard for them.   These are the mnemonics which are used  with 
PASCAL/Z  and the assembler that comes with the  package.   These 
tables   will  make  it  easy  for  the  Z-80  assembly  language 
programmer to cross reference the non-standard mnemonics.
     If an asterisk appears in the left-hand column of a line, it 
means that all of the instructions specified in that line, except 
those that refer to the Z-80 index registers, are compatible with 
the 8080.
     There   are   a  few  instructions  that   require   further 
clarification.  The TDL assembler mnemonics JV, JNV, CV, CNV, RV, 
and RNV are synonymous to the 8080 mnemonics JPE,  JPO, CPE, CPO, 
RPE,  and  RPO  respectively.   These instructions refer  to  the 
parity/overflow  flag in the Z-80 when it is used as an  overflow 
flag  and  are not included in 8080 assemblers,  even though  the 
instructions  will execute on the 8080 but will always  refer  to 
the  flag as a parity flag (this flag is always a parity flag  in 
the 8080).
     Another  instruction which requires clarification is the RST 
instruction.   In the TDL assembler the operand is a number which 
is actually the restart address divided by 8,  while in the Zilog 
assembler the operand is the actual restart address.
     Following  is a list of the abbreviations that are  used  to 
reference a group of similar operands.   Notice that although the 
same  symbol may be used as an operand for both a Zilog  mnemonic 
and a TDL mnemonic that they may refer to different things.  When 
two  lists  are given in the following table,  one for the  Zilog 
assembler and one for the  Z  assembler,  you may assume that the 
items in each list parallel each other.


Symbol	Standard (Zilog) Z-80		Bastardized (TDL) Z-80

r	Register A,B,C,D,E,H, or L	Register A,B,C,D,E,H, or L
n	One byte value			One byte value
ii	Index register IX, IY		Index register X or IX, Y or IY
jj	rr or ii			rr or ii
d	8-bit index displacement	8-bit index displacement
zz	Register pair BC or DE		Register pair B or D
nn	Two byte (address) value	Two byte (address) value
rr	Register pair BC,DE,HL, or SP	Register pair B,D,H, or SP
qq	Register pair BC,DE,HL, or AF	Register pair B,D,H, or PSW
s	r, (HL), or (ii+d)		r, M, or d(ii)
tt	Register BC,DE,SP, or IX	Register B,D,SP, or X
uu	Register BC,DE,SP, or IY	Register B,D,SP, or Y
b	Bit number 0-7			Bit number 0-7
.PA

            Z-80 instructions arranged by group


8080?	Standard (Zilog) Z-80		Bastardized (TDL) Z-80


                      8 Bit load group

*	LD	r,s			MOV	r,s
*	LD	r,n			MVI	r,n
*	LD	s,r			MOV	s,r
*	LD	A,(nn)			LDA	nn
*	LD	(nn),A			STA	nn
*	LD	A,(zz)			LDAX	zz
*	LD	(zz),A			STAX	zz
	LD	A,I			LDAI
	LD	A,R			LDAR
	LD	I,A			STAI
	LD	R,A			STAR



                     16 Bit load group

*	LD	jj,nn			LXI	jj,nn
	LD	BC,(nn)			LBCD	nn
	LD	DE,(nn)			LDED	nn
*	LD	HL,(nn)			LHLD	nn
	LD	IX,(nn)			LIXD	nn
	LD	IY,(nn)			LIYD	nn
	LD	SP,(nn)			LSPD	nn
	LD	(nn),BC			SBCD	nn
	LD	(nn),DE			SDED	nn
*	LD	(nn),HL			SHLD	nn
	LD	(nn),IX			SIXD	nn
	LD	(nn),IY			SIYD	nn
	LD	(nn),SP			SSPD	nn
*	LD	SP,HL			SPHL
	LD	SP,IX			SPIX
	LD	SP,IY			SPIY
*	PUSH	qq			PUSH	qq
	PUSH	ii			PUSH	ii
*	POP	qq			POP	qq
	POP	ii			POP	ii



         Exchange, block transfer, and search group

*	EX	DE,HL			XCHG
	EX	AF,AF'			EXAF
	EXX				EXX
*	EX	(SP),HL			XTHL
	EX	(SP),IX			XTIX
	EX	(SP),IY			XTIY
	LDI				LDI
	LDIR				LDIR
	LDD				LDD
	LDDR				LDDR
	CPI				CCI
	CPIR				CCIR
	CPD				CCD
	CPDR				CCDR



             8 bit arithmetic and logical group

*	ADD	A,s			ADD	s
*	ADD	A,n			ADI	n
*	ADC	A,s			ADC	s
*	ADC	A,n			ACI	n
*	SUB	A,s			SUB	s
*	SUB	A,n			SUI	n
*	SBC	A,s			SBB	s
*	SBC	A,n			SBI	n
*	AND	A,s			ANA	s
*	AND	A,n			ANI	n
*	OR	A,s			ORA	s
*	OR	A,n			ORI	n
*	XOR	A,s			XRA	s
*	XOR	A,n			XRI	n
*	CP	A,s			CMP	s
*	CP	A,n			CPI	n
*	INC	s			INR	s
*	DEC	s			DCR	s



      General purpose arithmetic and CPU control group

*	DAA				DAA
*	CPL				CMA
	NEG				NEG
*	CCF				CMC
*	SCF				STC
*	NOP				NOP
*	HALT				HLT
*	DI				DI
*	EI				EI
	IM	0			IM0
	IM	1			IM1
	IM	2			IM2



                  16 bit arithmetic group

*	ADD	HL,rr			DAD	rr
	ADC	HL,rr			DADC	rr
	SBC	HL,rr			DSBC	rr
	ADD	IX,tt			DADX	tt
	ADD	IY,uu			DADY	uu
*	INC	jj			INX	jj
*	DEC	jj			DCX	jj



                   Rotate and shift group

*	RLCA				RLC
*	RLA				RAL
*	RRCA				RRC
*	RRA				RAR
	RLC	s			RLCR	s
	RL	s			RALR	s
	RRC	s			RRCR	s
	RR	s			RARR	s
	SLA	s			SLAR	s
	SRA	s			SRAR	s
	SRL	s			SRLR	s
	RLD				RLD
	RRD				RRD



               Bit set, reset, and test group

	BIT	b,s			BIT	b,s
	SET	b,s			BSET	b,s
	RES	b,s			RES	b,s



                         Jump group

*	JP	nn			JMP	nn
*	JP	Z,nn			JZ	nn
*	JP	NZ,nn			JNZ	nn
*	JP	C,nn			JC	nn
*	JP	NC,nn			JNC	nn
*	JP	PO,nn			JPO	nn
*	JP	PE,nn			JPE	nn
*	JP	P,nn			JP	nn
*	JP	M,nn			JM	nn
*	JP	PE,nn			JV	nn
*	JP	PO,nn			JNV	nn
	JR	nn			JMPR	nn
	JR	Z,nn			JRZ	nn
	JR	NZ,nn			JRNZ	nn
	JR	C,nn			JRC	nn
	JR	NC,nn			JRNC	nn
	DJNZ	nn			DJNZ	nn
*	JP	(HL)			PCHL
	JP	(IX)			PCIX
	JP	(IY)			PCIY



                   Call and return group

*	CALL	nn			CALL	nn
*	CALL	Z,nn			CZ	nn
*	CALL	NZ,nn			CNZ	nn
*	CALL	C,nn			CC	nn
*	CALL	NC,nn			CNC	nn
*	CALL	PO,nn			CPO	nn
*	CALL	PE,nn			CPE	nn
*	CALL	P,nn			CP	nn
*	CALL	M,nn			CM	nn
*	CALL	PE,nn			CV	nn
*	CALL	PO,nn			CNV	nn
*	RET				RET
*	RET	Z			RZ
*	RET	NZ			RNZ
*	RET	C			RC
*	RET	NC			RNC
*	RET	PO			RPO
*	RET	PE			RPE
*	RET	P			RP
*	RET	M			RM
*	RET	PE			RV
*	RET	PO			RNV
	RETI				RETI
	RETN				RETN
*	RST	n			RST	n/8



                   Input and output group

*	IN	A,(n)			IN	n
	IN	r,(C)			INP	r
	INI				INI
	INIR				INIR
	IND				IND
	INDR				INDR
*	OUT	(n),A			OUT	n
	OUT	(C),r			OUTP	r
	OUTI				OUTI
	OUTD				OUTD
	OTDR				OUTDR



    Z-80 instructions sorted by standard Zilog mnemonics


8080?	Standard (Zilog) Z-80		Bastardized (TDL) Z-80


*	ADC	A,n			ACI	n
*	ADC	A,s			ADC	s
	ADC	HL,rr			DADC	rr
*	ADD	A,n			ADI	n
*	ADD	A,s			ADD	s
*	ADD	HL,rr			DAD	rr
	ADD	IX,tt			DADX	tt
	ADD	IY,uu			DADY	uu
*	AND	A,n			ANI	n
*	AND	A,s			ANA	s
	BIT	b,s			BIT	b,s
*	CALL	C,nn			CC	nn
*	CALL	M,nn			CM	nn
*	CALL	NC,nn			CNC	nn
*	CALL	nn			CALL	nn
*	CALL	NZ,nn			CNZ	nn
*	CALL	P,nn			CP	nn
*	CALL	PE,nn			CPE	nn
*	CALL	PE,nn			CV	nn
*	CALL	PO,nn			CNV	nn
*	CALL	PO,nn			CPO	nn
*	CALL	Z,nn			CZ	nn
*	CCF				CMC
*	CP	A,n			CPI	n
*	CP	A,s			CMP	s
	CPD				CCD
	CPDR				CCDR
	CPI				CCI
	CPIR				CCIR
*	CPL				CMA
*	DAA				DAA
*	DEC	jj			DCX	jj
*	DEC	s			DCR	s
*	DI				DI
	DJNZ	nn			DJNZ	nn
*	EI				EI
*	EX	(SP),HL			XTHL
	EX	(SP),IX			XTIX
	EX	(SP),IY			XTIY
	EX	AF,AF'			EXAF
*	EX	DE,HL			XCHG
	EXX				EXX
*	HALT				HLT
	IM	0			IM0
	IM	1			IM1
	IM	2			IM2
*	IN	A,(n)			IN	n
	IN	r,(C)			INP	r
*	INC	jj			INX	jj
*	INC	s			INR	s
	IND				IND
	INDR				INDR
	INI				INI
	INIR				INIR
*	JP	(HL)			PCHL
	JP	(IX)			PCIX
	JP	(IY)			PCIY
*	JP	C,nn			JC	nn
*	JP	M,nn			JM	nn
*	JP	NC,nn			JNC	nn
*	JP	nn			JMP	nn
*	JP	NZ,nn			JNZ	nn
*	JP	P,nn			JP	nn
*	JP	PE,nn			JPE	nn
*	JP	PE,nn			JV	nn
*	JP	PO,nn			JNV	nn
*	JP	PO,nn			JPO	nn
*	JP	Z,nn			JZ	nn
	JR	C,nn			JRC	nn
	JR	NC,nn			JRNC	nn
	JR	nn			JMPR	nn
	JR	NZ,nn			JRNZ	nn
	JR	Z,nn			JRZ	nn
*	LD	(nn),A			STA	nn
	LD	(nn),BC			SBCD	nn
	LD	(nn),DE			SDED	nn
*	LD	(nn),HL			SHLD	nn
	LD	(nn),IX			SIXD	nn
	LD	(nn),IY			SIYD	nn
	LD	(nn),SP			SSPD	nn
*	LD	(zz),A			STAX	zz
*	LD	A,(nn)			LDA	nn
*	LD	A,(zz)			LDAX	zz
	LD	A,I			LDAI
	LD	A,R			LDAR
	LD	BC,(nn)			LBCD	nn
	LD	DE,(nn)			LDED	nn
*	LD	HL,(nn)			LHLD	nn
	LD	I,A			STAI
	LD	IX,(nn)			LIXD	nn
	LD	IY,(nn)			LIYD	nn
*	LD	jj,nn			LXI	jj,nn
	LD	R,A			STAR
*	LD	r,n			MVI	r,n
*	LD	r,s			MOV	r,s
*	LD	s,r			MOV	s,r
	LD	SP,(nn)			LSPD	nn
*	LD	SP,HL			SPHL
	LD	SP,IX			SPIX
	LD	SP,IY			SPIY
	LDD				LDD
	LDDR				LDDR
	LDI				LDI
	LDIR				LDIR
	NEG				NEG
*	NOP				NOP
*	OR	A,n			ORI	n
*	OR	A,s			ORA	s
	OTDR				OUTDR
	OTIR				OUTIR
	OUT	(C),r			OUTP	r
*	OUT	(n),A			OUT	n
	OUTD				OUTD
	OUTI				OUTI
	POP	ii			POP	ii
*	POP	qq			POP	qq
	PUSH	ii			PUSH	ii
*	PUSH	qq			PUSH	qq
	RES	b,s			RES	b,s
*	RET				RET
*	RET	C			RC
*	RET	M			RM
*	RET	NC			RNC
*	RET	NZ			RNZ
*	RET	P			RP
*	RET	PE			RPE
*	RET	PE			RV
*	RET	PO			RNV
*	RET	PO			RPO
*	RET	Z			RZ
	RETI				RETI
	RETN				RETN
	RL	s			RALR	s
*	RLA				RAL
	RLC	s			RLCR	s
*	RLCA				RLC
	RLD				RLD
	RR	s			RARR	s
*	RRA				RAR
	RRC	s			RRCR	s
*	RRCA				RRC
	RRD				RRD
*	RST	n			RST	n/8
*	SBC	A,n			SBI	n
*	SBC	A,s			SBB	s
	SBC	HL,rr			DSBC	rr
*	SCF				STC
	SET	b,s			BSET	b,s
	SLA	s			SLAR	s
	SRA	s			SRAR	s
	SRL	s			SRLR	s
*	SUB	A,n			SUI	n
*	SUB	A,s			SUB	s
*	XOR	A,n			XRI	n
*	XOR	A,s			XRA	s



   Z-80 instructions sorted by bastardized TDL mnemonics


8080?	Standard (Zilog) Z-80		Bastardized (TDL) Z-80


*	ADC	A,n			ACI	n
*	ADC	A,s			ADC	s
*	ADD	A,s			ADD	s
*	ADD	A,n			ADI	n
*	AND	A,s			ANA	s
*	AND	A,n			ANI	n
	BIT	b,s			BIT	b,s
	SET	b,s			BSET	b,s
*	CALL	nn			CALL	nn
*	CALL	C,nn			CC	nn
	CPD				CCD
	CPDR				CCDR
	CPI				CCI
	CPIR				CCIR
*	CALL	M,nn			CM	nn
*	CPL				CMA
*	CCF				CMC
*	CP	A,s			CMP	s
*	CALL	NC,nn			CNC	nn
*	CALL	PO,nn			CNV	nn
*	CALL	NZ,nn			CNZ	nn
*	CALL	P,nn			CP	nn
*	CALL	PE,nn			CPE	nn
*	CP	A,n			CPI	n
*	CALL	PO,nn			CPO	nn
*	CALL	PE,nn			CV	nn
*	CALL	Z,nn			CZ	nn
*	DAA				DAA
*	ADD	HL,rr			DAD	rr
	ADC	HL,rr			DADC	rr
	ADD	IX,tt			DADX	tt
	ADD	IY,uu			DADY	uu
*	DEC	s			DCR	s
*	DEC	jj			DCX	jj
*	DI				DI
	DJNZ	nn			DJNZ	nn
	SBC	HL,rr			DSBC	rr
*	EI				EI
	EX	AF,AF'			EXAF
	EXX				EXX
*	HALT				HLT
	IM	0			IM0
	IM	1			IM1
	IM	2			IM2
*	IN	A,(n)			IN	n
	IND				IND
	INDR				INDR
	INI				INI
	INIR				INIR
	IN	r,(C)			INP	r
*	INC	s			INR	s
*	INC	jj			INX	jj
*	JP	C,nn			JC	nn
*	JP	M,nn			JM	nn
*	JP	nn			JMP	nn
	JR	nn			JMPR	nn
*	JP	NC,nn			JNC	nn
*	JP	PO,nn			JNV	nn
*	JP	NZ,nn			JNZ	nn
*	JP	P,nn			JP	nn
*	JP	PE,nn			JPE	nn
*	JP	PO,nn			JPO	nn
	JR	C,nn			JRC	nn
	JR	NC,nn			JRNC	nn
	JR	NZ,nn			JRNZ	nn
	JR	Z,nn			JRZ	nn
*	JP	PE,nn			JV	nn
*	JP	Z,nn			JZ	nn
	LD	BC,(nn)			LBCD	nn
*	LD	A,(nn)			LDA	nn
	LD	A,I			LDAI
	LD	A,R			LDAR
*	LD	A,(zz)			LDAX	zz
	LDD				LDD
	LDDR				LDDR
	LD	DE,(nn)			LDED	nn
	LDI				LDI
	LDIR				LDIR
*	LD	HL,(nn)			LHLD	nn
	LD	IX,(nn)			LIXD	nn
	LD	IY,(nn)			LIYD	nn
	LD	SP,(nn)			LSPD	nn
*	LD	jj,nn			LXI	jj,nn
*	LD	r,s			MOV	r,s
*	LD	s,r			MOV	s,r
*	LD	r,n			MVI	r,n
	NEG				NEG
*	NOP				NOP
*	OR	A,s			ORA	s
*	OR	A,n			ORI	n
*	OUT	(n),A			OUT	n
	OUTD				OUTD
	OTDR				OUTDR
	OUTI				OUTI
	OTIR				OUTIR
	OUT	(C),r			OUTP	r
*	JP	(HL)			PCHL
	JP	(IX)			PCIX
	JP	(IY)			PCIY
	POP	ii			POP	ii
*	POP	qq			POP	qq
	PUSH	ii			PUSH	ii
*	PUSH	qq			PUSH	qq
*	RLA				RAL
	RL	s			RALR	s
*	RRA				RAR
	RR	s			RARR	s
*	RET	C			RC
	RES	b,s			RES	b,s
*	RET				RET
	RETI				RETI
	RETN				RETN
*	RLCA				RLC
	RLC	s			RLCR	s
	RLD				RLD
*	RET	M			RM
*	RET	NC			RNC
*	RET	PO			RNV
*	RET	NZ			RNZ
*	RET	P			RP
*	RET	PE			RPE
*	RET	PO			RPO
*	RRCA				RRC
	RRC	s			RRCR	s
	RRD				RRD
*	RST	n			RST	n/8
*	RET	PE			RV
*	RET	Z			RZ
*	SBC	A,s			SBB	s
	LD	(nn),BC			SBCD	nn
*	SBC	A,n			SBI	n
	LD	(nn),DE			SDED	nn
*	LD	(nn),HL			SHLD	nn
	LD	(nn),IX			SIXD	nn
	LD	(nn),IY			SIYD	nn
	SLA	s			SLAR	s
*	LD	SP,HL			SPHL
	LD	SP,IX			SPIX
	LD	SP,IY			SPIY
	SRA	s			SRAR	s
	SRL	s			SRLR	s
	LD	(nn),SP			SSPD	nn
*	LD	(nn),A			STA	nn
	LD	I,A			STAI
	LD	R,A			STAR
*	LD	(zz),A			STAX	zz
*	SCF				STC
*	SUB	A,s			SUB	s
*	SUB	A,n			SUI	n
*	EX	DE,HL			XCHG
*	XOR	A,s			XRA	s
*	XOR	A,n			XRI	n
*	EX	(SP),HL			XTHL
	EX	(SP),IX			XTIX
	EX	(SP),IY			XTIY