Documentation For Program ENTRY.COM

                             by
                      Robert H. Harsch
                     ph: (916) 487-2216
             2362 American River Dr., Suite 311
                   Sacramento, Ca. 95825.
                    All rights reserved.

    A utility program to "automatically" insert entry points
into SRC extenstion files for PASCAL/Z programs; thus, making
easier the process of linking seperately compilied external
pascal procedure/functions to main programs.

DIRECTIONS FOR USE OF PROGRAM WITH EXAMPLE:

1. Create the main calling program.  For example
   file MAINPRG.PAS:

    PROGRAM MAINPRG;
    TYPE
	VECTORTYPE = ARRAY [ 1..10 ] OF INTEGER;
    
    PROCEDURE SUM( VAR RESULT: INTEGER; VAR V: VECTORTYPE);	EXTERNAL; { external procedure reference, functions
		    may also be used accordingly }
    VAR
	I, RESULT: INTEGER;
	VEC: VECTORTYPE;

    BEGIN { of main program }
	FOR I:= 1 TO 10 DO
		VEC[ I ]:= I; { initialize vector for example }
	SUM(RESULT, VEC); { call external routine }
	WRITELN(RESULT) { prints 55 as the answer }
    END.




2. Create the external routine(s) from the text editor.
   To continue the above example lets say we create
   the file EXTERN.PAS:

    PROGRAM EXTERN; { external program procedure }
    TYPE VECTORTYPE = ARRAY [ 1..10 ] OF INTEGER;
	{ parameters must be passed through the
	  procedure/function heading, not through global
	  variables }
	PROCEDURE SUM( VAR RESULT: INTEGER; VAR V: VECTORTYPE);
	VAR I: INTEGER;
			{$i+ see complier directives, puts
			     next line of source into file
			     EXTERN.SRC after compliation }
			{@SUM -- name of external routine }
			{$i- turn off complier directive }
		BEGIN
			RESULT:= 0;
			FOR I:= 1 TO 10 DO
				RESULT:= RESULT + V[I]
		END; { of procedure sum }
    BEGIN
		{ Dummy BEGIN and END exist only
		for syntax purposes of compilation.
		Never a main body of statements to execute. }
    END.

2. Type:
	PASCAL EXTERN
   compliation will proceed normally thus creating
   files EXTERN.SRC, EXTERN.LST, but unfortunatley
   there will be no entry points created for linking
   the procedure heading declaration of the main program
   with the externally called procedure sum.

3. But since we compilied the file with the following inserted 
   before the BEGIN of procedure sum (the entry point):
		{$i+ }
		{@SUM}
		{$i- }
   typing:
	ENTRY EXTERN
  executes the program and copies file EXTERN.SRC into
  EXTERN.ZZZ, and adds the needed entry points into the
  external routine so that assembly and linkage can
  properly take place.

3. Continuing with the example we type:
	ERA EXTERN.SRC
	REN EXTERN.SRC=EXTERN.ZZZ

4. The EXTERN.SRC is now in proper form for assembly
   (to produce EXTERN.REL) and linkage to produce the
   executable COM file.






SUMMARY OF DIRECTIONS USING THE ABOVE EXAMPLE.

1. Create main calling module with declarations, as an example
   here refered to as file MAINPRG.PAS.

2. Create the external module to be called, as an example
   here refered to as file EXTERN.PAS.

3. Insert the following before the BEGIN of procedure sum in
   file EXTERN.PAS:
		{$i+ }
		{@SUM}
		{$i- }

4. Type the following commands while in CP/M monitor or set up
   a SUBMIT file:
   A. Compile main calling program and produce files
      mainprg.rel, mainprg.lst:
		PASCAL MAINPRG
		ASMBL MAIN,MAINPRG/REL

   B. Compile the external called program and set up entry
      points, producing files extern.rel, extern.lst:
		PASCAL EXTERN
		ENTRY EXTERN
		ERA EXTERN.SRC
		REN EXTERN.SRC=EXTERN.ZZZ
		ASMBL EMAIN,EXTERN/REL

   C. Link the main program with the external program,
      producing the executable file mainprg.com:
		LINK MAINPRG,EXTERN /N:MAINPRG /E

   D. Finally, typing the following will execute the program:
		MAINPRG



ALGORITHM FOR ENTRY.COM:
	1. Create an open file name.ZZZ as a file to write to
	   (will destroy an existing file name.ZZZ if present).
	2. Open for reading the file name.SRC.
	3. Print to monitor the names of files opened.
	4. Read a line from file name.SRC.
	5. If the line has the string '{@' followed by an 
	   identifier (the external procedure name) the
	   following two lines are written to file name.ZZZ:
				ENTRY	identifier
		identifier:
	   An identifier is a alphabetic letter (a thru z, or
	   A thru Z) followed by zero or more alphanumeric
	   characters (a thru z, A thru Z, or 0 thru 9).  If
	   the identifier is greater than 6 character, the
	   identifier is then truncated to 6 characters and
	   convert lower-case characters to upper-case.
		It is wise to make the external procedure name
	   (identifier) from one to six characters in length,
	   in upper-case, to avoid possible confusion.
	   	Avoid conflict with labels or external libary
	   routines used by the compilier in the assembling 
	   process.  (Avoid all labels in the form L<digit(s)>,
	   e.g. L99, and labels referenced as external library 
	   routines, e.g. DIVD, by file MAIN.SRC).
	   The assembler will give you an error diagnostic
	   when you have made this mistake.
		The external procedure name should not have the
	   the characters '_' or '$' in the identifier, even
	   though the compiler permits this the assembler does
	   not.  (The assembler will give you an error
	   diagnostic).

	6. If (4.) true above then print to monitor the
	   external procedure/function name.

	5. If (4.) above untrue then copy the line from file
	   name.SRC to file name.ZZZ.

	6. Repeat (2.) thru (5.) above until the label L99 is
	   found indicating the main body of program statements
	   between BEGIN END have been found, which we do not
	   want to copy (assembly with EMAIN will cause
	   errors).