KPROMDM7.DOC  NON-LINEAR KAYCOMP KAYPRO II DOC FOR MODEM7.

	AS OF 08/21/82.      Tom McCormick.  Houston, Tx.


	This portable CP/M micro comes with an RS232c serial port,
	a BAUD.COM utility to set the baud rates on that port, and
	the SELECT editor with which to make the following changes
	to MBOOT.ASM.

	MBOOT.ASM is a minimal subset of MODEM7: all it will do is
	operate in terminal mode, and then receive one file at a time
	using the Christensen protocol of MODEM7.  It will not send,
	auto dial, send/receive without handshaking, transfer multiple
	files from a single command (wildcards), etc. like the full
	MODEM7 program will do.   BUT...it is much much shorter to
	key in the first time if you do not know anyone with MODEM7
	on a KAYPRO II compatable 5" diskette.

	Obtain a printed copy of MBOOT.ASM (free, public-domain), and
	make the following changes.  You can then use MBOOT to transfer
	the full MODEM7 program to yourself, and make the same changes
	to it.

	----------------------------------------------

	Here are the MODEM7 values to patch for KCOMP.

	04H   MODEM DATA PORT

	06H   MODEM STATUS PORT

	04H   BIT MASK: READY TO SEND

	01H   BIT MASK: READY TO RECEIVE

	----------------------------------------------

	We connected the KAYPRO serial port directly to
	an H-89 serial port as follows:

		KAYPRO	  H-89

		     2 to 3

		     3 to 2

		     5 to 4

		20-6-8
	  (JUMP ALL 3) to 20

	...and transferred several files at 9600 baud.
	We did not try 19200, might work OK.



	----------------------------------------------