Unless otherwise stated, aritmetic and logical operations operate on 32 bit twos-complement integers
"float" refers to single precision (32 bit) IEEE 754 floating point numbers.
In "before" and "after" stack pictures, the top of stack is rightmost.
Words in the category "FILE" are only relevant when the transputer is hosted in a PC and 
communicating via emSERVER.

Word	Defined by	Vocabulary	Category	Definition and/or Comment
------------------------------------------------------------------------------
*	CODE	FORTH	ARITHMETIC	signed multiply
+	CODE	FORTH	ARITHMETIC	signed or unsigned add
-	CODE	FORTH	ARITHMETIC	signed or unsigned subtract, second minus top
/	CODE	FORTH	ARITHMETIC	signed divide of second by top
/MOD	:	FORTH	ARITHMETIC	signed divide with remainder, remainder second, quotient top	( U U -- R Q )
1+	CODE	FORTH	ARITHMETIC	add one	( INC TOS BY 1 )
1-	CODE	FORTH	ARITHMETIC	subtract one	( DEC TOS BY 1 )
2*	CODE	FORTH	ARITHMETIC	multiply by two	( DIV TOS BY 2 )
2+	CODE	FORTH	ARITHMETIC	add two	( INC TOS BY 2 )
2-	CODE	FORTH	ARITHMETIC	subtract two	( DEC TOS BY 2 )
2/	CODE	FORTH	ARITHMETIC	divide by two	( DIV TOS BY 2 )
4+	CODE	FORTH	ARITHMETIC	add four	( INC TOS BY 4 )
4-	CODE	FORTH	ARITHMETIC	subtract four	( DEC TOS BY 4 )
ABS	:	FORTH	ARITHMETIC	absolute value	( N - U ) DUP 0< IF 0 SWAP - THEN ;
BPW+	ALIAS	FORTH	ARITHMETIC	increment by bytes-per-word	4+
BPW-	ALIAS	FORTH	ARITHMETIC	decrement by bytes-per-word	4-
MOD	CODE	FORTH	ARITHMETIC	signed remainder of second by top
NEGATE	:	FORTH	ARITHMETIC	change sign	0 SWAP - ;
U/	CODE	FORTH	ARITHMETIC	unsigned divide of second by top
U/MOD	CODE	FORTH	ARITHMETIC	unsigned divide with remainder, remainder second, quotient top
UMOD	CODE	FORTH	ARITHMETIC	unsigned remainder of second by top
10^I	:	FPU	ARITHMETIC	float ten to the integer power	( I --> 10^I 	TAKE TEN TO I'TH POWER )
BASE^I	:	FPU	ARITHMETIC	float current-number-base to the integer power	( I --> 10^I 	TAKE BASE TO I'TH POWER )
COS	CODE	FPU	ARITHMETIC	float cosine of radians	( XRAD --> COSINE )
DEG>RAD	:	FPU	ARITHMETIC	float convert degrees to radians	( FPDEG --> FPRAD )
EXP	:	FPU	ARITHMETIC	float second times ten to the power of top	( I EXP --> FP  take int at next and exp at top to make a real32 )
F*	CODE	FPU	ARITHMETIC	float multiply
F+	CODE	FPU	ARITHMETIC	float add
F-	CODE	FPU	ARITHMETIC	float subtract
F/	CODE	FPU	ARITHMETIC	float divide of second by top
FABS	CODE	FPU	ARITHMETIC	float absolute value
RAD>DEG	:	FPU	ARITHMETIC	float convert radians to degrees	( FPRAD --> FPDEG )
SIN	CODE	FPU	ARITHMETIC	float sine of radians	( XRAD --> COSINE )
SQRT	CODE	FPU	ARITHMETIC	float square root
TAN	:	FPU	ARITHMETIC	float tangent of radians
X^I	CODE	FPU	ARITHMETIC	float second float   to the power of top integer	( I FPX --> X^I   take REAL X TO INT I TH POWER )
^I	:	FPU	ARITHMETIC	float second integer to the power of top integer
0=	:	ASSEMBLER	COMPARISON	is top zero?
0<	CODE	FORTH	COMPARISON	is top less than zero?
0=	CODE	FORTH	COMPARISON	is top zero?	( W -- t/f )
<	CODE	FORTH	COMPARISON	is second less than top?
=	CODE	FORTH	COMPARISON	is second equal to top?
>	CODE	FORTH	COMPARISON	is second greater than top?
MINT=	CODE	FORTH	COMPARISON	is top equal to the minimum integer?	( W -- t/f )
WITHIN	:	FORTH	COMPARISON	is third within the range second to top inclusive?	( N1 N2 N3 -- T/F ; is N1 within the range N2 - N3 inclusive )
F0<	CODE	FPU	COMPARISON	is top float less than zero?
F0=	CODE	FPU	COMPARISON	is top float zero?
F1<-1 	:	FPU	COMPARISON	is the absolute value of top float less than 1?	( FP --> IS IT A FRACTION )
F<	CODE	FPU	COMPARISON	is second float less than top float?
F=	CODE	FPU	COMPARISON	is second float equal to top float?
F>	CODE	FPU	COMPARISON	is second float greater than top float?
"	:	COMPILER	COMPILER	compiles literal strings into a definition?
(	:	COMPILER	COMPILER	begins a comment
INLINE	:	COMPILER	COMPILER	switches from forth to assembly within a definition, closed by OUTLINE
LITERAL	:	COMPILER	COMPILER	compile top as a literal to dictionary
[	:	COMPILER	COMPILER	suspend compiling and begin interpreting	0 MODE !
COMPILE	:	FORTH	COMPILER	compile next address to dictionary
IMMED	:	FORTH	COMPILER	make the most recently compiled word a compiler immediate word
MODE	VARIABLE	FORTH	COMPILER	compiler mode, eg. compiling or interpreting	( COMP OR INTERP MODE )
]	:	FORTH	COMPILER	resume compiling, closes "["	SAVEMODE @ MODE !
Alt	object	ASSEMBLER	CONCURRENT	object which implements occam-style ALT
FORK	:	COMPILER	CONCURRENT	create a new FORTH interpreter to concurrently execute the following word	COMPILE [FORK] ;
FORKHI	:	COMPILER	CONCURRENT	same as FORK but make it a high priority process
FORK	:	FORTH	CONCURRENT	create a new FORTH interpreter to concurrently execute the following word, in immediate mode
FORKHI	:	FORTH	CONCURRENT	same as FORK but make it a high priority process, in immediate mode
Process	object	FORTH	CONCURRENT	object corresponding to a concurrent process, used by FORK
Semaphore_Class	class	OOPS	CONCURRENT	class for managing mutual exclusion of a resource, eg. memory allocation
*DIE	VARIABLE	RUNTIME	CONCURRENT	pointer to code which terminates the current FORTH interpreter process
AGAIN	:	ASSEMBLER	CONTROL	end of an untested indefinite loop, equivalent to FALSE UNTIL or TRUE WHILE REPEAT	( BEGINADDR 2 -- )
BEGIN	:	ASSEMBLER	CONTROL	beginning of an indefinite loop
ELSE	:	ASSEMBLER	CONTROL	beginning of the FALSE clause of a conditional branch	( ADDR 1 -- ADDR 2 )
IF	:	ASSEMBLER	CONTROL	test and beginning of the TRUE clause of a conditional branch
OUTLINE	:	ASSEMBLER	CONTROL	switches from assembly to forth within a definition, closed by INLINE
REPEAT	:	ASSEMBLER	CONTROL	end of a pre-tested or middle-tested indefinite loop	( 3 B W -- )
THEN	:	ASSEMBLER	CONTROL	end of a conditional branch	( ADDR 1|2 -- )
UNTIL	:	ASSEMBLER	CONTROL	test and end of a post-tested indefinite loop
WHILE	:	ASSEMBLER	CONTROL	test of a pre-tested or middle-tested indefinite loop	( BEGIN 0 -- BEGIN WHILE 3 )
AGAIN	:	COMPILER	CONTROL	end of untested indefinite loop, equivalent to FALSE UNTIL or TRUE WHILE REPEAT	( BEGINADDR 2 -- )
BEGIN	:	COMPILER	CONTROL	beginning of an indefinite loop
DO	:	COMPILER	CONTROL	beginning of a definite loop	( -- )
ELSE	:	COMPILER	CONTROL	beginning of the FALSE clause of a conditional branch	( ADDR 1 -- ADDR 2 )
EXIT	:	COMPILER	CONTROL	an unstructured exit from a procedure	COMPILE  {'}-  [NEXT] ; REMSMUDGE
IF	:	COMPILER	CONTROL	test and beginning of the TRUE clause of a conditional branch
LOOP	:	COMPILER	CONTROL	end of a definite loop	( -- )
REPEAT	:	COMPILER	CONTROL	end of a pre-tested or middle-tested indefinite loop	( 3 B W -- )
THEN	:	COMPILER	CONTROL	end of a conditional branch	( ADDR 1|2 -- )
UNTIL	:	COMPILER	CONTROL	test and end of a post-tested indefinite loop, equivalent to NOT WHILE REPEAT
WHILE	:	COMPILER	CONTROL	test of a pre-tested or middle-tested indefinite loop	( BEGIN 0 -- BEGIN WHILE 3 )
(	:	FORTH	CONTROL	beginning of a comment	29 WORD DROP ;
I	CODE	FORTH	CONTROL	push the definite loop index onto the stack	( MOVE RS TO TOS )
LEAVE	CODE	FORTH	CONTROL	terminates a definite loop at the end of the current pass	( MAKE R = TO R NEXT - 1 )
QUIT	:	FORTH	CONTROL	stop everything and begin interpreting from the keyboard
NUMBER	:	FORTH	CONVERSION	convert the ASCII string, pointed to by top, to an integer	( A- N )
I32TOR32	CODE	FPU	CONVERSION	convert an integer to a float
R32TOI32	CODE	FPU	CONVERSION	convert a float to an integer
DEBUG	VARIABLE	DEBUGSTUFF	DEBUG	boolean, tells compiler to generate code for single-step tracing
END-CODE	:	ASSEMBLER	DEFINING	end an assembler definition
;	:	COMPILER	DEFINING	end a forth definition
:	:	FORTH	DEFINING	begin a forth definition for the following word
<BUILDS	:	FORTH	DEFINING	begin the compile-time behaviour in the definition of a higher-level defining word
ALIAS	:	FORTH	DEFINING	defines the second following word as an alias for the following word, no runtime penalty	' OFFSET - CREATE , LATEST @ @ 8000 OR LATEST @ ! ;
CODE	:	FORTH	DEFINING	begin an assembly definition to be called from forth
CODESUB	:	FORTH	DEFINING	begin an assembly definition to be called from assembly
CONSTANT	:	FORTH	DEFINING	define a constant
DOES>	:	FORTH	DEFINING	end the compile-time behaviour and start the execution-time behaviour in the definition of a higher-level defining word	R> MARKER @  ! 
VARIABLE	:	FORTH	DEFINING	define a variable
VOCABULARY	:	FORTH	DEFINING	define a vocabulary
W,CON	:	FORTH	DEFINING	define a workspace-relative variable at the next dictionary location	( OFFSET FROM W )
'	:	FORTH	DICTIONARY	find the code address, from the dictionary path, of the next input word
,	:	FORTH	DICTIONARY	store top to the next dictionary location, increment dictionary pointer by bytes-per-word
-FIND	CODE	FORTH	DICTIONARY	find the code address, from the dictionary pointed to by second, of the word pointed to by top	( TEXT,LINK --> TEXT FALSE | CFA, TRUE :- USER = NFA )
ALLOT	:	FORTH	DICTIONARY	add top to the dictionary pointer	( N --	 MOVE DP N BYTES )
C,	:	FORTH	DICTIONARY	store the low byte of top to the next dictionary location, increment dictionary pointer
CREATE	:	FORTH	DICTIONARY	start a new definition by making a header in the dictionary for the next input word	COMPILE [ ASSEMBLER CP ^^ LDL   GCALL NOP NOP VDROP ] SMUDGE
DP	VARIABLE	FORTH	DICTIONARY	the dictionary pointer	( DICT POINTER )
DP'	VARIABLE	FORTH	DICTIONARY	the alternate dictionary pointer, used when compiling headerless code	( ALTERATE DP FOR HEADERLESS CODE )
DP'INIT	VARIABLE	FORTH	DICTIONARY	pointer to area for local heads, MINT if not allocated	( POINTS TO MEMALOCED AREA FOR LOCAL HEADS )
H/C	VARIABLE	FORTH	DICTIONARY	boolean, tells compiler to compile headerless code	( HEADERLESS FLAG )
HERE	CODE	FORTH	DICTIONARY	push the dictionary pointer onto the stack	( -- DP@ )     ( PUSH DP ON STACK )
HEREW	CODE	FORTH	DICTIONARY	word-align the dictionary pointer and push it onto the stack		( PUSH DP ON STACK )
HIDE	:	FORTH	DICTIONARY	permanently hide a word by linking around it in the dictionary	' DROP USER @ BPW - @ USER BPW + @ ! ;
SMUDGE	:	FORTH	DICTIONARY	temporarily hide or show a word by toggling a flag in its header in the dictionary
{	:	FORTH	DICTIONARY	swaps DP and DP'
}	:	FORTH	DICTIONARY	swaps DP and DP'
*EMPTY	VARIABLE	RUNTIME	DICTIONARY	points to the REMEMBERed word EMPTY, used at startup
-'	:	RUNTIME	DICTIONARY	find the code address, from the dictionary path, of the word at the dictionary pointer	( ---   SEARCH PATH FOR WORD )
ALIGN	:	RUNTIME	DICTIONARY	word-align the dictionary pointer
BYPASS	VARIABLE	RUNTIME	DICTIONARY	to save a thread for linking around future words
FIND	:	RUNTIME	DICTIONARY	find the code address, from the dictionary pointed to by top, of the next input word	( THREAD --- F | T CFA )
LATEST	VARIABLE	RUNTIME	DICTIONARY	save latest header address for smudging etc.
MARKER	VARIABLE	RUNTIME	DICTIONARY	used by <BUILDS to save link for DOES>
STRING	:	RUNTIME	DICTIONARY	put literal text into dictionary, used by ."	WORD C@ 1+ ALLOT ALIGN ;
UNSMUDGE	:	RUNTIME	DICTIONARY	repeatedly unsmudge word pointed to by top until a zero becomes top	( UNSMUDGE CFA ADDRESS ON STACK UNTIL 0 FOUND )
ABORT"	:	COMPILER	ERROR	print the following string and abort
ERTYPE	VARIABLE	DEBUGSTUFF	ERROR	stores most recent error type number
*ABORT	VARIABLE	FORTH	ERROR	pointer to the appropriate abort routine
ABORT	:	FORTH	ERROR		*ABORT @ EXECUTE ;
ABORT1	:	FORTH	ERROR	
ABORT2	:	FORTH	ERROR	
ERROR	:	RUNTIME	ERROR	
ERROR1	:	RUNTIME	ERROR		ABORT" NOT PAIRED " ;
ERRORVEC	VARIABLE	RUNTIME	ERROR	pointer to error handler
UNKNMSG	:	RUNTIME	ERROR	prints "UNKNOWN MESSAGE"
CAPTURE	:	FORTH	FILE	send terminal output to a file as well
DiskBuff_Class	class	FORTH	FILE	
FILEGETLINE	:	FORTH	FILE	get a line of text from a file to the text input buffer
INCLUDE	:	FORTH	FILE	
SAVEBOOT	:	FORTH	FILE	
File	object	NETWORK	FILE
CAPFP	VARIABLE	RUNTIME	FILE	( CAPTURE FP )
STDOUTFP	VARIABLE	RUNTIME	FILE	( CAPTURE FP )
."	:	COMPILER	IO	
.	:	FORTH	IO	( N) (.) #> SPACE ;
."	:	FORTH	IO	
.MSG	:	FORTH	IO	
>IN	VARIABLE	FORTH	IO	
>OUT	VARIABLE	FORTH	IO	
?	:	FORTH	IO	( A) @ . ;
BLK	VARIABLE	FORTH	IO	
CNT	VARIABLE	FORTH	IO	
CR	:	FORTH	IO	*CR @ EXECUTE ;
DUMP	:	FORTH	IO	memory List ;
DUMPBOOT	:	FORTH	IO	
DUMPMAIN	:	FORTH	IO	
DUMPOUT	:	FORTH	IO	( ADDR LEN -- )
ECHO	VARIABLE	FORTH	IO	
EMIT	:	FORTH	IO	( CHAR -- )
EVENT	CONSTANT	FORTH	IO	80000020	
EXPECT	CODE	FORTH	IO	( ADDR NUM --- )
GET16	CODE	FORTH	IO	( CHAN -- DATA16 )
GETBYTE	CODE	FORTH	IO	( CHAN -- BYTEDATA )
GETBYTES	CODE	FORTH	IO	( LINK DST CNT -- )
GETLINE	CODE	FORTH	IO	
GETNAME	:	FORTH	IO	
GETWORD	CODE	FORTH	IO	( CHAN -- WORDDATA )
KEY	CODE	FORTH	IO	( -- CHAR )
LINKINPTR	VARIABLE	FORTH	IO	
LINKOUTPTR	VARIABLE	FORTH	IO	
LOCALCR	:	FORTH	IO	
LOCALKEY	CODE	FORTH	IO	
LOCGETLINE	:	FORTH	IO	
List	object	FORTH	IO	
PUT16	CODE	FORTH	IO	
PUTBYTE	CODE	FORTH	IO	( BYTEDATA CHAN -- )
PUTBYTES	CODE	FORTH	IO	( SIZE &DATA CHAN -- )
PUTWORD	CODE	FORTH	IO	( WORDDATA CHAN -- )
SPACE	:	FORTH	IO	20 EMIT ;
SPACES	:	FORTH	IO	DUP 0 > IF 0 DO SPACE LOOP ELSE DROP THEN ;
TYPE	:	FORTH	IO	( CNTADDR -- NEXTADDR )
U.	:	FORTH	IO	( U) 0 U.R SPACE ;
U.R	:	FORTH	IO	( U N) >R <# #S OVER R> SWAP - SPACES #> ;
U?	:	FORTH	IO	( A) @ U. ;
WEMIT	CODE	FORTH	IO	( W --   send word down link )
#.#>	:	FPU	IO	( ..# N --> )
.ETC	:	FPU	IO	( DP N --> PRINT N WITH DECIMAL POINT AT DP )
F.	:	FPU	IO	( FP32 -->  print 32 bits float )
*CR	VARIABLE	RUNTIME	IO	
*GETLINE	VARIABLE	RUNTIME	IO	
*KEY	VARIABLE	RUNTIME	IO	
LINE#	VARIABLE	RUNTIME	IO	
SIGN	:	RUNTIME	IO	( ..# N N - ..# N )  0< IF 45 HOLD THEN ;
TIB	VARIABLE	RUNTIME	IO	DECIMAL 76 NEWALLOT HEX ( RESERVE 80 BYTES FOR TIB )
TOB	VARIABLE	RUNTIME	IO	DECIMAL 76 NEWALLOT HEX ( RESERVE 80 BYTES FOR TOB )
TYPE2	:	RUNTIME	IO	
NOT	:	ASSEMBLER	LOGICAL	boolean (not bitwise) NOT, equivalent to 0=	( Logical not , not a bitwise not )
AND	CODE	FORTH	LOGICAL	bitwise AND
FALSE	CODE	FORTH	LOGICAL	boolean FALSE, equivalent to 0	( -- F )
NOT	CODE	FORTH	LOGICAL	boolean (not bitwise) NOT, equivalent to 0=	( Logical not , not a bitwise not )
OR	CODE	FORTH	LOGICAL	bitwise OR
REV16	CODE	FORTH	LOGICAL	reverse the order of the low 16 bits
REV32	CODE	FORTH	LOGICAL	reverse the bit order
TRUE	CODE	FORTH	LOGICAL	boolean TRUE, equivalent to 1	( -- T )
XOR	CODE	FORTH	LOGICAL	bitwise XOR
*LOAD	:	ASSEMBLER	MACRO	
*STORE	:	ASSEMBLER	MACRO	
++B	:	ASSEMBLER	MACRO	
++W	:	ASSEMBLER	MACRO	
--B	:	ASSEMBLER	MACRO	
--W	:	ASSEMBLER	MACRO	
;CODE	:	ASSEMBLER	MACRO	( CALL NEXT AND END CODE )
A>NEXT	:	ASSEMBLER	MACRO	
A>TOP	:	ASSEMBLER	MACRO	
CALLSUB	:	ASSEMBLER	MACRO	
FIELDADDR	:	ASSEMBLER	MACRO	( OFFS -- )
FIELDLOAD	:	ASSEMBLER	MACRO	( OFFS -- )
FIELDSAVE	:	ASSEMBLER	MACRO	( OFFS -- )
JMPBACK	:	ASSEMBLER	MACRO	CALCBACK C, ;
LDC	:	ASSEMBLER	MACRO	DUP
NEXT>A	:	ASSEMBLER	MACRO	
POP	:	ASSEMBLER	MACRO	DUP
PUSH	:	ASSEMBLER	MACRO	
SP2DROP	:	ASSEMBLER	MACRO	
SP>A	:	ASSEMBLER	MACRO	
TOP>A	:	ASSEMBLER	MACRO	
^^	:	ASSEMBLER	MACRO	WS - BPW / ;
FPA>TOP	:	FPUASM	MACRO	SP ^^ LDL FPSTNLSN ;
POPFPA	:	FPUASM	MACRO	TOP>FPA SP ++W ;
PUSHFPA	:	FPUASM	MACRO	SP --W FPA>TOP ;
TOP>FPA	: 	FPUASM	MACRO	SP ^^ LDL FPLDNLSN ;
!	CODE	FORTH	MEMORY	( W addr --   store word at addr )
+!	CODE	FORTH	MEMORY	( *addr inc -- ADD TOS TO *ADDR AT NEXT eg  DP 1 +! TO INC DP )
@	CODE	FORTH	MEMORY	( addr - W , fetch word at addr to tos )
C!	CODE	FORTH	MEMORY	( B addr --   store byte at addr )
C@	CODE	FORTH	MEMORY	( addr - B , fetch byte at addr to tos )
CMOVE	CODE	FORTH	MEMORY	 ( SRC DST CNT -- )
ERASE	:	FORTH	MEMORY	( STRT LEN --- )
FREE	:	FORTH	MEMORY	showfree MemAlloc ;
GETMEM1	:	FORTH	MEMORY	mode1 getmem MemAlloc ;
MemAlloc	MemAlloc_Class	FORTH	MEMORY	
OFF	:	FORTH	MEMORY	FALSE SWAP ! ;
ON	:	FORTH	MEMORY	TRUE SWAP ! ;
MemAlloc_Class	class	OOPS	MEMORY	
*GETMEM1	VARIABLE	RUNTIME	MEMORY	
GetNumber	object	FORTH	NETWORK	
NETCR	:	FORTH	NETWORK	
NETGETLINE	:	FORTH	NETWORK	
NETWORK	VOCABULARY	FORTH	NETWORK	
NETWORKED	VARIABLE	FORTH	NETWORK	
REPLYPORT	VARIABLE	FORTH	NETWORK	
PATHSIZE	VARIABLE	FORTH	NETWORK	
ROUTER	VOCABULARY	FORTH	NETWORK	
STDOUT	:	FORTH	NETWORK	
&FSERVE	VARIABLE	NETWORK	NETWORK	&FSERVE DP !
&KBD	VARIABLE	NETWORK	NETWORK	&KBD DP !
&VDU	VARIABLE	NETWORK	NETWORK	&VDU DP !
ADTONO	:	NETWORK	NETWORK	
FSERVE	CONSTANT	NETWORK	NETWORK	3
INTABLE	VARIABLE	NETWORK	NETWORK	INTABLE DP !
KBD	CONSTANT	NETWORK	NETWORK	2
KEYHIT	:	NETWORK	NETWORK	
Kbd	object	NETWORK	NETWORK	
NETEMIT	:	NETWORK	NETWORK	
NETKEY	:	NETWORK	NETWORK	
OFF-NET	:	NETWORK	NETWORK	
ON-NET	:	NETWORK	NETWORK	
OUTLINK	VARIABLE	NETWORK	NETWORK	
OUTTABLE	VARIABLE	NETWORK	NETWORK	OUTTABLE DP !
Packet	object	NETWORK	NETWORK	
RELEASE	VARIABLE	NETWORK	NETWORK	
ROUTE	:	NETWORK	NETWORK	
SYNC	CONSTANT	NETWORK	NETWORK	5A5A5AA5
VDU	CONSTANT	NETWORK	NETWORK	1
-1	CODE	FORTH	NUMERIC	( -- -1 )
-2	CODE	FORTH	NUMERIC	( -- -2 )
-4	CODE	FORTH	NUMERIC	( -- -4 )
-BPW	ALIAS	FORTH	NUMERIC	-4
0	CODE	FORTH	NUMERIC	( -- 0 )
1	CODE	FORTH	NUMERIC	( -- 1 )
2	CODE	FORTH	NUMERIC	( -- 2 )
4	CODE	FORTH	NUMERIC	( -- 4 )
BASE	VARIABLE	FORTH	NUMERIC	
BPW	ALIAS	FORTH	NUMERIC	4
DECIMAL	:	FORTH	NUMERIC	A BASE !
FPONE	VARIABLE	FORTH	NUMERIC	
HEX	:	FORTH	NUMERIC	10 BASE ! ;
MINT	CODE	FORTH	NUMERIC	
PI	CONSTANT	FPU	NUMERIC	314159265 -8 EXP
Dynamic_Class	class	FORTH	OOPS	
Byte	Vardec_Class	OOPS	OOPS	
Field	compiler object	OOPS	OOPS	
GMESSAGE	:	OOPS	OOPS	
Int	Vardec_Class	OOPS	OOPS	
LOCAL	:	OOPS	OOPS	0 SIZE ! ;
MAKELOCAL	CODE	OOPS	OOPS	( ADDR -->  MOVE DATAPTR TO ADDR )
MESSAGE	:	OOPS	OOPS	
Method	object	OOPS	OOPS	
Nil	class	OOPS	OOPS	
Of	object	OOPS	OOPS	
Ptr	Vardec_Class	OOPS	OOPS	
REMOTE	:	OOPS	OOPS	0 SIZE ! ;
Real	Vardec_Class	OOPS	OOPS	
SAVESIZE	:	OOPS	OOPS	SIZE @ CONSTANT ;
Vardec_Class	class	OOPS	OOPS	
CALLOBJ	:	RUNTIME	OOPS	
COMPCALLOBJ	:	RUNTIME	OOPS	
DAP	VARIABLE	RUNTIME	OOPS	( pointer to data address stack )
INTPFLG	VARIABLE	RUNTIME	OOPS	( set is object interpretted not compiled )
LSTMSG	VARIABLE	RUNTIME	OOPS	
MAX_METHODS	CONSTANT	RUNTIME	OOPS	30  ( MAXIMUM NUMBER OF METHODS )
MP	VARIABLE	RUNTIME	OOPS	( pointer to message stack )
MPINIT	VARIABLE	RUNTIME	OOPS	
MSGLINK	VARIABLE	RUNTIME	OOPS	
MSGTYPE	:	RUNTIME	OOPS	( MSGNO. -- EMPTY )
SEARCHMETH	:	RUNTIME	OOPS	(  { msg }  -->   msg only in interp mode )
SETSUPER	:	RUNTIME	OOPS	( MS --> MS )
ADC,	:	ASSEMBLER	OPCODE	80 PRE ;  ( add constant )
ADD,	:	ASSEMBLER	OPCODE	F5 C, ;
AJW	:	ASSEMBLER	OPCODE	B0 PRE ;  ( adjust workspace )
ALT	:	ASSEMBLER	OPCODE	43 OPR ;
ALTEND	:	ASSEMBLER	OPCODE	45 OPR ;
ALTWT	:	ASSEMBLER	OPCODE	44 OPR ;
AND	:	ASSEMBLER	OPCODE	46 OPR;
BCNT	:	ASSEMBLER	OPCODE	34 OPR ;
BITCNT	:	ASSEMBLER	OPCODE	76 OPR ;
BITREVNBITS	:	ASSEMBLER	OPCODE	78 OPR ;
BITREVWORD	:	ASSEMBLER	OPCODE	77 OPR ;
BREAK	:	ASSEMBLER	OPCODE	B1 OPR ;
BSUB	:	ASSEMBLER	OPCODE	F2 C, ;
CALL	:	ASSEMBLER	OPCODE	90 PRE ;  ( call )
CCNT1	:	ASSEMBLER	OPCODE	4D OPR ;
CFLERR	:	ASSEMBLER	OPCODE	73 OPR ;
CIRJ0BREAK	:	ASSEMBLER	OPCODE	B2 OPR ;
CJ	:	ASSEMBLER	OPCODE	A0 PRE ;  ( conditional jump )
CLRHALTERR	:	ASSEMBLER	OPCODE	57 OPR ;
COMP	:	ASSEMBLER	OPCODE	32 OPR ;  ( I've changed NOT to COMP )
CRCBYTE	:	ASSEMBLER	OPCODE	75 OPR ;
CRCWORD	:	ASSEMBLER	OPCODE	74 OPR ;
CSNGL	:	ASSEMBLER	OPCODE	4C OPR ;
CSUB0	:	ASSEMBLER	OPCODE	13 OPR ;
CWORD	:	ASSEMBLER	OPCODE	56 OPR ;
DIFF	:	ASSEMBLER	OPCODE	F4 C, ;
DISC	:	ASSEMBLER	OPCODE	2F OPR ;
DISS	:	ASSEMBLER	OPCODE	30 OPR ;
DIST	:	ASSEMBLER	OPCODE	2E OPR ;
DIV	:	ASSEMBLER	OPCODE	2C OPR ;
DUP,	:	ASSEMBLER	OPCODE	5A OPR ;
ENBC	:	ASSEMBLER	OPCODE	48 OPR ;
ENBS	:	ASSEMBLER	OPCODE	49 OPR ;
ENBT	:	ASSEMBLER	OPCODE	47 OPR ;
ENDP	:	ASSEMBLER	OPCODE	F3 C, ;
EQC	:	ASSEMBLER	OPCODE	C0 PRE ;  ( equals constant )
FMUL	:	ASSEMBLER	OPCODE	72 OPR ;
GAJW	:	ASSEMBLER	OPCODE	3C OPR ;
GCALL	:	ASSEMBLER	OPCODE	F6 C, ;
GT	:	ASSEMBLER	OPCODE	F9 C, ;
IN	:	ASSEMBLER	OPCODE	F7 C, ;
J	:	ASSEMBLER	OPCODE	00 PRE ;  ( jump relative )
LADD	:	ASSEMBLER	OPCODE	16 OPR ;  ( LONG ADD )
LB	:	ASSEMBLER	OPCODE	F1 C, ;
LDDEVID	:	ASSEMBLER	OPCODE	17C OPR ;
LDIFF	:	ASSEMBLER	OPCODE	4F OPR ;
LDINF	:	ASSEMBLER	OPCODE	71 OPR ;
LDIV	:	ASSEMBLER	OPCODE	1A OPR ;
LDL	:	ASSEMBLER	OPCODE	70 PRE ;  ( load local )
LDLP	:	ASSEMBLER	OPCODE	10 PRE ;  ( load local pointer )
LDMEMSTARTVAL	:	ASSEMBLER	OPCODE	7E OPR ;
LDNL	:	ASSEMBLER	OPCODE	30 PRE ;  ( load non-local )
LDNLP	:	ASSEMBLER	OPCODE	50 PRE ;  ( load non-local pointer )
LDPI	:	ASSEMBLER	OPCODE	1B OPR ;
LDPRI	:	ASSEMBLER	OPCODE	1E OPR ;
LDTIMER	:	ASSEMBLER	OPCODE	22 OPR ;
LEND	:	ASSEMBLER	OPCODE	21 OPR ;
LMUL	:	ASSEMBLER	OPCODE	31 OPR ;
LSHL	:	ASSEMBLER	OPCODE	36 OPR ;
LSHR	:	ASSEMBLER	OPCODE	35 OPR ;
LSUB	:	ASSEMBLER	OPCODE	38 OPR ;
LSUM	:	ASSEMBLER	OPCODE	37 OPR ;
MINT	:	ASSEMBLER	OPCODE	42 OPR ;
MOVE	:	ASSEMBLER	OPCODE	4A OPR ;
MOVE2DALL	:	ASSEMBLER	OPCODE	5C OPR ;
MOVE2DINIT	:	ASSEMBLER	OPCODE	5B OPR ;
MOVE2DNONZERO	:	ASSEMBLER	OPCODE	5D OPR ;
MOVE2DZERO	:	ASSEMBLER	OPCODE	5E OPR ;
MUL	:	ASSEMBLER	OPCODE	53 OPR ;
NOP	:	ASSEMBLER	OPCODE	80 C, ;
NORM	:	ASSEMBLER	OPCODE	19 OPR ;
OPR	:	ASSEMBLER	OPCODE	F0 PRE ;  ( store non-local )
OR	:	ASSEMBLER	OPCODE	4B OPR ;
OUT	:	ASSEMBLER	OPCODE	FB C, ;
OUTBYTE	:	ASSEMBLER	OPCODE	FE C, ;
OUTWORD	:	ASSEMBLER	OPCODE	FF C, ;
POP,	:	ASSEMBLER	OPCODE	79 OPR ;
POSTNORMSN	:	ASSEMBLER	OPCODE	6C OPR ;
PROD	:	ASSEMBLER	OPCODE	F8 C, ;
REM	:	ASSEMBLER	OPCODE	1F OPR ;  ( REMAINDER )
RESETCH	:	ASSEMBLER	OPCODE	12 OPR ;
RET	:	ASSEMBLER	OPCODE	20 OPR ;
REV	:	ASSEMBLER	OPCODE	F0 C, ;
ROUNDSN	:	ASSEMBLER	OPCODE	6D OPR ;
RUNP	:	ASSEMBLER	OPCODE	39 OPR ;
SAVEH	:	ASSEMBLER	OPCODE	3E OPR ;
SAVEL	:	ASSEMBLER	OPCODE	3D OPR ;
SB	:	ASSEMBLER	OPCODE	3B OPR ;
SETERR	:	ASSEMBLER	OPCODE	10 OPR ;
SETHALTERR	:	ASSEMBLER	OPCODE	58 OPR ;
SETJ0BREAK	:	ASSEMBLER	OPCODE	B3 OPR ;
SHL	:	ASSEMBLER	OPCODE	41 OPR ;
SHR	:	ASSEMBLER	OPCODE	40 OPR ;
STARTP	:	ASSEMBLER	OPCODE	FD C, ;
STHB	:	ASSEMBLER	OPCODE	50 OPR ;
STHF	:	ASSEMBLER	OPCODE	18 OPR ;
STL	:	ASSEMBLER	OPCODE	D0 PRE ;  ( store local )
STLB	:	ASSEMBLER	OPCODE	17 OPR ;
STLF	:	ASSEMBLER	OPCODE	1C OPR ;
STNL	:	ASSEMBLER	OPCODE	E0 PRE ;  ( store non-local )
STOPERR	:	ASSEMBLER	OPCODE	55 OPR ;
STOPP	:	ASSEMBLER	OPCODE	15 OPR ;
STTIMER	:	ASSEMBLER	OPCODE	54 OPR ;
SUB	:	ASSEMBLER	OPCODE	FC C, ;
SUM	:	ASSEMBLER	OPCODE	52 OPR ;
TALT	:	ASSEMBLER	OPCODE	4E OPR ;
TALTWT	:	ASSEMBLER	OPCODE	51 OPR ;
TESTERR	:	ASSEMBLER	OPCODE	29 OPR ;
TESTHALTERR	:	ASSEMBLER	OPCODE	59 OPR ;
TESTPRANAL	:	ASSEMBLER	OPCODE	2A OPR ;
TIMERDISABLEH	:	ASSEMBLER	OPCODE	7A OPR ;
TIMERDISABLEL	:	ASSEMBLER	OPCODE	7B OPR ;
TIMERENABLEH	:	ASSEMBLER	OPCODE	7C OPR ;
TIMERENABLEL	:	ASSEMBLER	OPCODE	7D OPR ;
TIN	:	ASSEMBLER	OPCODE	2B OPR ;
UNPACKSN	:	ASSEMBLER	OPCODE	63 OPR ;
WCNT	:	ASSEMBLER	OPCODE	3F OPR ;
WSUB	:	ASSEMBLER	OPCODE	FA C, ;
XDBLE	:	ASSEMBLER	OPCODE	1D OPR ;
XOR	:	ASSEMBLER	OPCODE	33 OPR ;
XWORD	:	ASSEMBLER	OPCODE	3A OPR ;
FPADD	:	FPUASM	OPCODE	87 OPR ;
FPB32TOR64	:	FPUASM	OPCODE	9A OPR ;
FPCHKERROR	:	FPUASM	OPCODE	83 OPR ;
FPDIV	:	FPUASM	OPCODE	8C OPR ;
FPDUP	:	FPUASM	OPCODE	A3 OPR ;
FPENTRY	:	FPUASM	OPCODE	AB OPR ;
FPEQ	:	FPUASM	OPCODE	95 OPR ;
FPGT	:	FPUASM	OPCODE	94 OPR ;
FPI32TOR32	:	FPUASM	OPCODE	96 OPR ;
FPI32TOR64	:	FPUASM	OPCODE	98 OPR ;
FPINT	:	FPUASM	OPCODE	A1 OPR ;
FPLDNLADDDB	:	FPUASM	OPCODE	A6 OPR ;
FPLDNLADDSN	:	FPUASM	OPCODE	AA OPR ;
FPLDNLDB	:	FPUASM	OPCODE	8A OPR ;
FPLDNLMULDB	:	FPUASM	OPCODE	A8 OPR ;
FPLDNLMULSN	:	FPUASM	OPCODE	AC OPR ;
FPLDNLSN	:	FPUASM	OPCODE	8E OPR ;
FPLDNLSNI	:	FPUASM	OPCODE	86 OPR ;
FPLDZERODB	:	FPUASM	OPCODE	A0 OPR ;
FPLDZEROSN	:	FPUASM	OPCODE	9F OPR ;
FPMUL	:	FPUASM	OPCODE	8B OPR ;
FPNAN	:	FPUASM	OPCODE	91 OPR ;
FPNOTFINITE	:	FPUASM	OPCODE	93 OPR ;
FPORDERED	:	FPUASM	OPCODE	92 OPR ;
FPREMFIRST	:	FPUASM	OPCODE	8F OPR ;
FPREMSTEP	:	FPUASM	OPCODE	90 OPR ;
FPREV	:	FPUASM	OPCODE	A4 OPR ;
FPRTOI32	:	FPUASM	OPCODE	9D OPR ;
FPSTNLDB	:	FPUASM	OPCODE	84 OPR ;
FPSTNLI32	:	FPUASM	OPCODE	9E OPR ;
FPSTNLSN	:	FPUASM	OPCODE	88 OPR ;
FPSUB	:	FPUASM	OPCODE	89 OPR ;
FPTESTERR	:	FPUASM	OPCODE	9C OPR ;
FPUABS	:	FPUASM	OPCODE	B LDC FPENTRY ;
FPUCHKI32	:	FPUASM	OPCODE	E LDC FPENTRY ;
FPUCHKI64	:	FPUASM	OPCODE	F LDC FPENTRY ;
FPUCLEARERROR	:	FPUASM	OPCODE	9C LDC FPENTRY ;
FPUDIVBY2	:	FPUASM	OPCODE	11 LDC FPENTRY ;
FPUEXPDEC32	:	FPUASM	OPCODE	9 LDC FPENTRY ;
FPUEXPINC32	:	FPUASM	OPCODE	A LDC FPENTRY ;
FPUMULBY2	:	FPUASM	OPCODE	12 LDC FPENTRY ;
FPUNOROUND	:	FPUASM	OPCODE	D LDC FPENTRY ;
FPUR32TOR64	:	FPUASM	OPCODE	7 LDC FPENTRY ;
FPUR64TOR32	:	FPUASM	OPCODE	8 LDC FPENTRY ;
FPURM	:	FPUASM	OPCODE	5 LDC FPENTRY ;
FPURN	:	FPUASM	OPCODE	22 LDC FPENTRY ;
FPURP	:	FPUASM	OPCODE	4 LDC FPENTRY ;
FPURZ	:	FPUASM	OPCODE	6 LDC FPENTRY ;
FPUSETERROR	:	FPUASM	OPCODE	23 LDC FPENTRY ;
FPUSQRTFIRST	:	FPUASM	OPCODE	1 LDC FPENTRY ;
FPUSQRTLAST	:	FPUASM	OPCODE	3 LDC FPENTRY ;
FPUSQRTSTEP	:	FPUASM	OPCODE	2 LDC FPENTRY ;
EXECUTE	CODE	FORTH	PRIMITIVE	( addr -- )
[COS]	CODESUB	FPU	PRIMITIVE	
[MSGLITERAL]	CODE	OOPS	PRIMITIVE	
(.)	:	RUNTIME	PRIMITIVE	( N - ..# N) DUP >R ABS <# #S R> SIGN ;
RTNXT	VARIABLE	RUNTIME	PRIMITIVE	
["]	:	RUNTIME	PRIMITIVE	( PUT ADDRESS OF LITERAL STRING TO TOP )
[BASE]	CODESUB	RUNTIME	PRIMITIVE	( PUSH DATAPTR )
[CODEOB]	CODE	RUNTIME	PRIMITIVE	
[COLON]	CODE	RUNTIME	PRIMITIVE	( NEXTRETURN FWORDADDR -- )
[CON]	CODE	RUNTIME	PRIMITIVE	( nextret CALLINGADDR -- )
[Class]	COMPILEROBJECT	RUNTIME	PRIMITIVE	
[DDUP]	CODESUB	RUNTIME	PRIMITIVE	( DUP DATA ADDRESS STACK )
[DNEXT]	CODE	RUNTIME	PRIMITIVE	( DROP DAP STACK AND CALL NEXT )
[DOES>]	CODE	RUNTIME	PRIMITIVE	( a has calling addr b has nxtret )
[DYN]	CODESUB	RUNTIME	PRIMITIVE	( DUP DATA ADDRESS STACK )
[FORKHI]	:	RUNTIME	PRIMITIVE	R> DUP @ new hi forth Process BPW+ >R ;
[FORK]	:	RUNTIME	PRIMITIVE	R> DUP @ new forth Process BPW+ >R ;
[GOTO]	CODE	RUNTIME	PRIMITIVE	
[IF]	CODE	RUNTIME	PRIMITIVE	
[INDEX]	CODESUB	RUNTIME	PRIMITIVE	( ADD LITERAL TO DATAPTR AND PUSH )
[INLINE]	CODE	RUNTIME	PRIMITIVE	
[LITERAL]	CODE	RUNTIME	PRIMITIVE	
[NEXT]	CODE	RUNTIME	PRIMITIVE	
[OBJ]	CODE	RUNTIME	PRIMITIVE	
[OUTLINE]	CODE	RUNTIME	PRIMITIVE	
[SUPER]	CODESUB	RUNTIME	PRIMITIVE	( ADD OFFSET TO TOP AND CALL METHOD )
[VAR]	CODE	RUNTIME	PRIMITIVE	
[VOC]	CODE	RUNTIME	PRIMITIVE	( areg = vocab variable breg = return to next )
[W,CON]	CODE	RUNTIME	PRIMITIVE	( nextret , address of W + constant on tos )
abort"	CODE	RUNTIME	PRIMITIVE	
dot"	:	RUNTIME	PRIMITIVE	
.S	:	FORTH	STACK	
>R	CODE	FORTH	STACK	( MOVE TOS TO RS )
?DUP	CODE	FORTH	STACK	( DUP if non zero )
DAP!	CODE	FORTH	STACK	( reset data pntr stack pointer )
DEPTH	:	FORTH	STACK	STKLIM @ SP @ - BPW / 2- ;
DROP	CODE	FORTH	STACK	( W -- )
DUP	CODE	FORTH	STACK	( W - W W )
MP!	CODE	FORTH	STACK	( reset data pntr stack pointer )
OVER	CODE	FORTH	STACK	( A B -- A B A )
PICK	CODE	FORTH	STACK	( . . N - W )
R>	CODE	FORTH	STACK	( RET -- MOVE RS TO TOS )
ROT	CODE	FORTH	STACK	( A B C -- B C A )  SP ^^ LDL   2 LDNL
SP!	CODE	FORTH	STACK	( reset data stack pointer )
SWAP	CODE	FORTH	STACK	( A B -- B A )
VDROP	:	FORTH	STACK	( DROP TO OF VOCAB STACK )
>D	CODE	OOPS	STACK	( DUP DATA ADDRESS STACK )
>M	CODE	OOPS	STACK	( DUP DATA ADDRESS STACK )
D>	CODE	OOPS	STACK	( DUP DATA ADDRESS STACK )
DDROP	CODE	OOPS	STACK	( DUP DATA ADDRESS STACK )
DDUP	CODE	OOPS	STACK	( DUP DATA ADDRESS STACK )
M>	CODE	OOPS	STACK	( DUP DATA ADDRESS STACK )
MDROP	CODE	OOPS	STACK	( DUP DATA ADDRESS STACK )
RP	VARIABLE	RUNTIME	STACK	( return stack pointer )
SP	VARIABLE	RUNTIME	STACK	( data stack pointer )
STKLIM	VARIABLE	RUNTIME	STACK	( stack limit for underflow checking )
BOOT	:	FORTH	SYSTEM	FALSE WARMFLG ! DUMPBOOT DUMPMAIN KEY DROP ;
BOOTLENGTH	VARIABLE	FORTH	SYSTEM	
BOOTSTRAP	CODESUB	FORTH	SYSTEM	
BUFFSIZE	CONSTANT	FORTH	SYSTEM	1000
COLD	CODE	FORTH	SYSTEM	
COLD4	:	FORTH	SYSTEM	
END.	:	FORTH	SYSTEM	( release memory used for meth-table and H/C )
INTERPRET	:	FORTH	SYSTEM	
PROGRAM	:	FORTH	SYSTEM	( allocate memory used for meth-table and H/C )
STARTUPADDRESS	VARIABLE	FORTH	SYSTEM	
USER	VARIABLE	FORTH	SYSTEM	
VERSION	CONSTANT	FORTH	SYSTEM	VERSION 1+
WORD	CODE	FORTH	SYSTEM	
WS	VARIABLE	FORTH	SYSTEM	
WSLEN	CONSTANT	FORTH	SYSTEM	SPINIT WS -
*COLD3	VARIABLE	RUNTIME	SYSTEM	
ANCHOR	VARIABLE	RUNTIME	SYSTEM	( LINK ALLOCATED MEMORY HERE )
ASAVE	VARIABLE	RUNTIME	SYSTEM	
BSAVE	VARIABLE	RUNTIME	SYSTEM	
COLD3	:	RUNTIME	SYSTEM	
CP	VARIABLE	RUNTIME	SYSTEM	( colon pointer - points to [COLON] )
IP	VARIABLE	RUNTIME	SYSTEM	( interpretive pointer )
REMSMUDGE	:	RUNTIME	SYSTEM	SMUDGE LATEST @ ;
STARTUP	CODE	RUNTIME	SYSTEM	( address of startup info in B )
STRTVEC	VARIABLE	RUNTIME	SYSTEM	
WARM	CODE	RUNTIME	SYSTEM	( NB :- NEW WS IS ALREADY ACTIVE BUT STARTUP SETS IT AGAIN )
WARMFLG	VARIABLE	RUNTIME	SYSTEM	
DELAY	CODE	FORTH	TIMER	( N -- DELAY N 64 uS TICKS )
GETTIMER	CODE	FORTH	TIMER	( -- TIME )
TIMERIN	CODE	FORTH	TIMER	
TIMERWAIT	CODE	FORTH	TIMER	( N -- WAIT N 64 uS TICKS )
ASSEMBLER	VOCABULARY	FORTH	VOCABULARY	
COMPILER	VOCABULARY	FORTH	VOCABULARY	
CONTEXT	CODE	FORTH	VOCABULARY	
CURRENT	VARIABLE	FORTH	VOCABULARY	
DEBUGSTUFF	VOCABULARY	FORTH	VOCABULARY	
DEFINITIONS	:	FORTH	VOCABULARY	CONTEXT @ CURRENT ! ;
EMPTY	REMEMBER	FORTH	VOCABULARY	
FORTH	VOCABULARY	FORTH	VOCABULARY	
FORTHONLY	:	FORTH	VOCABULARY	( ONLY SEARCH FORTH VOCAB )
FPU	VOCABULARY	FORTH	VOCABULARY	
FPUASM	VOCABULARY	FORTH	VOCABULARY	
OOPS	VOCABULARY	FORTH	VOCABULARY	
PATH	:	FORTH	VOCABULARY	path List ;
REMEMBER	:	FORTH	VOCABULARY	
RUNTIME	VOCABULARY	FORTH	VOCABULARY	
UNLINKVOCAB	:	FORTH	VOCABULARY	
VLIST	:	FORTH	VOCABULARY	word List ;
MESSAGES	VOCABULARY	OOPS	VOCABULARY	
CONARRAY	VARIABLE	RUNTIME	VOCABULARY	VSTKSIZE BPW * NEWALLOT  ( ARRAY FOR SAVING SEARCH PATH )
CONINDEX	VARIABLE	RUNTIME	VOCABULARY	
VOCLINK	VARIABLE	RUNTIME	VOCABULARY